## Slide 1: Instructor Materials Chapter 6: VLANs
CCNA Routing and Switching
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 6: VLANs

## Slide 2: Instructor Materials – Chapter 6 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 14
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Routing and Switching Essentials 6.0 Planning Guide
Chapter 6: VLANs
Notes: Routing and Switching Essentials 6.0
Chapter 6: VLANs

## Slide 4: Chapter 6: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
6.0.1.2 | Class Activity | Vacation Station | Optional
6.1.1.5 | Packet Tracer | Who Hears the Broadcast? | Recommended
6.1.2.6 | Activity | Predict Switch Behavior | Recommended
6.1.2.7 | Packet Tracer | Investigating a VLAN Implementation | Recommended
6.2.1.2 | Syntax Checker | Creating a VLAN | -
6.2.1.3 | Syntax Checker | Assign Ports to VLANS | -
6.2.1.4 | Syntax Checker | Changing VLAN Port Membership | -
6.2.1.6 | Syntax Checker | Verifying VLAN Information | -
6.2.1.7 | Packet Tracer | Configuring VLANs | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 6: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
6.2.2.3 | Syntax Checker | Verifying Trunk Configuration | -
6.2.2.4 | Packet Tracer | Configuring Trunks | Recommended
6.2.2.5 | Lab | Configuring VLANs and Trunking | Recommended
6.2.3.7 | Packet Tracer | Troubleshooting a VLAN Implementation – Scenario 1 | Recommended
6.2.3.8 | Packet Tracer | Troubleshooting a VLAN Implementation – Scenario 2 | Recommended
6.2.3.9 | Lab | Troubleshooting VLAN Configurations | Optional
6.3.1.4 | Activity | Identify the Types of Inter-VLAN Routing | Recommended
6.3.2.4 | Lab | Configuring Per-Interface Inter-VLAN Routing | Recommended
6.3.3.4 | Syntax Checker | Configuring Router-on-a-Stick Inter-VLAN Routing | -
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 6: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
6.3.3.6 | Packet Tracer | Configuring Router-on-a-Stick Inter-VLAN Routing | Recommended
6.3.3.7 | Lab | Configuring 801.2Q Trunk-Based Inter-VLAN Routing | Optional
6.3.3.8 | Packet Tracer | Inter-VLAN Routing Challenge | Optional
6.4.1.1 | Activity | The Inside Track | Optional
6.4.1.2 | Packet Tracer | Skills Integration Challenge | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 6

## Slide 7: Chapter 6: Assessment
Students should complete Chapter 6, “Assessment” after completing Chapter 6.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 7

## Slide 8
Prior to teaching Chapter 6, the instructor should:
Complete Chapter 6, “Assessment.”
The objectives of this chapter are:
  Explain how VLANs segment broadcast domains in a small to medium-sized business network.
    Explain the purpose of VLANs in a switched network.
    Explain how a switch forwards frames based on VLAN configuration in a multi-switch environment.
  Implement VLANs to segment a small to medium-sized business network.
    Configure a switch port to be assigned to a VLAN based on requirements.
    Configure a trunk port on a LAN switch.
    Troubleshoot VLAN and trunk configurations in a switched network.
  Configure routing between VLANs in a small to medium-sized business network.
    Describe the two options for configuring Inter-VLAN routing.
    Configure Legacy Inter-VLAN Routing.
    Configure Router-on-a-Stick Inter-VLAN Routing.
Chapter 6: Best Practices
Notes: 8

## Slide 9
Chapter 6: Best Practices (Cont.)
Section 6.1
  Make this chapter as hands on as possible. Students should complete labs, Packet Tracer activities, and other activities.
  Emphasize that the devices are unaware of the existence of the VLAN to which they belong.
Notes: 9

## Slide 10
Chapter 6: Best Practices (Cont.)
Section 6.2
  When the students complete the troubleshooting labs, create additional challenges or have one team of students create problems on another team’s setup. Ensure that all changes and all solutions are documented.
Notes: 10

## Slide 11
Chapter 6: Best Practices (Cont.)
Section 6.3
  After students complete the legacy inter-VLAN routing lab and the router-on-a-stick inter-VLAN routing labs, ask them to present the advantages and disadvantages of each method.
Notes: 11

## Slide 12: Chapter 6: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna-blog
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Packet Tracer Know How 1: Packet Tracer 101 (self-enroll)
Notes: 12

## Slide 14: Chapter 6: VLANs
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 6: VLANs

## Slide 15: Chapter 6 - Sections & Objectives
6.1 VLAN Segmentation
  Explain the purpose of VLANs in a switched network.
  Explain how a switch forwards frames based on VLAN configuration in a multi-switch environment.
6.2 VLAN Implementations
  Configure a switch port to be assigned to a VLAN based on requirements.
  Configure a trunk port on a LAN switch.
  Troubleshoot VLAN and trunk configurations in a switched network.
6.3 Inter-VLAN Routing Using Routers
  Describe the two options for configuring Inter-VLAN routing.
  Configure Legacy Inter-VLAN Routing.
  Configure Router-on-a-Stick Inter-VLAN Routing
Notes: 15

## Slide 16: 6.1 VLAN Segmentation
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 6: VLANs

## Slide 17: Overview of VLANs VLAN Definitions
Notes: 6.1 – VLAN Segmentation
6.1.1 – Overview of VLANs
6.1.1.1 – VLAN Definitions

## Slide 18: Overview of VLANs VLAN Definitions (cont.)
VLANs allow an administrator to segment networks based on factors such as function, project team, or application, without regard for the physical location of the user or device.
VLANs enable the implementation of access and security policies according to specific groupings of users.
A VLAN is a logical partition of a Layer 2 network.
Multiple partitions can be created, allowing for multiple VLANs to co-exist.
Each VLAN is a broadcast domain, usually with its own IP network.
VLANs are mutually isolated, and packets can only pass between them via a router.
The partitioning of the Layer 2 network takes place inside a Layer 2 device, usually via a switch.
The hosts grouped within a VLAN are unaware of the VLAN’s existence.
Notes: 6.1 – VLAN Segmentation
6.1.1 – Overview of VLANs
6.1.1.1 – VLAN Definitions (cont.)

## Slide 19: Overview of VLANs Benefits of VLANs
Notes: 6.1 – VLAN Segmentation
6.1.1 – Overview of VLANs
6.1.1.2 – Benefits of VLANs

## Slide 20: Overview of VLANs Types of VLANs
Data VLAN – user generated traffic
Default VLAN – all switch ports become part of this VLAN until switch is configured, show vlan brief
Native VLAN – used for untagged traffic
Management VLAN – used to access management capabilities
Notes: 6.1 – VLAN Segmentation
6.1.1 – Overview of VLANs
6.1.1.3 – Types of VLANs

## Slide 21: Overview of VLANs Types of VLANs (cont.)
Notes: 6.1 – VLAN Segmentation
6.1.1 – Overview of VLANs
6.1.1.3 – Types of VLANs (cont.)

## Slide 22: Overview of VLANs Voice VLANs
Notes: 6.1 – VLAN Segmentation
6.1.1 – Overview of VLANs
6.1.1.4 – Voice VLANs

## Slide 23: Overview of VLANs Voice VLANs (cont.)
VoIP traffic is time-sensitive and requires:
  Assured bandwidth to ensure voice quality.
  Transmission priority over other types of network traffic.
  Ability to be routed around congested areas on the network.
  Delay of less than 150 ms across the network.
The voice VLAN feature enables access ports to carry IP voice traffic from an IP phone.
Notes: 6.1 – VLAN Segmentation
6.1.1 – Overview of VLANs
6.1.1.4 – Voice VLANs (cont.)

## Slide 24: VLANs in a Multi-Switched Environment VLAN Trunks
The links between switches S1 and S2, and S1 and S3 are configured to transmit traffic coming from VLANs 10, 20, 30, and 99 across the network. This network could not function without VLAN trunks.
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.1 – VLAN Trunks

## Slide 25: VLANs in a Multi-Switched Environment VLAN Trunks (cont.)
A VLAN trunk is a point-to-point link that carries more than one VLAN.
A VLAN trunk is usually established between switches so same-VLAN devices can communicate, even if physically connected to different switches.
A VLAN trunk is not associated to any VLANs; neither is the trunk ports used to establish the trunk link.
Cisco IOS supports IEEE802.1q, a popular VLAN trunk protocol.
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.1 – VLAN Trunks (cont.)

## Slide 26: VLANs in a Multi-Switched Environment Controlling Broadcast Domains with VLANs
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.2 - Controlling Broadcast Domains with VLANs

## Slide 27: VLANs in a Multi-Switched Environment Controlling Broadcast Domains with VLANs
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.2 - Controlling Broadcast Domains with VLANs (cont.)

## Slide 28: VLANs in a Multi-Switched Environment Controlling Broadcast Domains with VLANs
VLANs can be used to limit the reach of broadcast frames.
A VLAN is a broadcast domain of its own.
A broadcast frame sent by a device in a specific VLAN is forwarded within that VLAN only.
VLANs help control the reach of broadcast frames and their impact in the network.
Unicast and multicast frames are forwarded within the originating VLAN.
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.2 - Controlling Broadcast Domains with VLANs (cont.)

## Slide 29: VLANs in a Multi-Switched Environment Tagging Ethernet Frames for VLAN Identification
Frame tagging is the process of adding a VLAN identification header to the frame.
It is used to properly transmit multiple VLAN frames through a trunk link.
Switches tag frames to identify the VLAN to which they belong.
Different tagging protocols exist; IEEE 802.1Q is a vey popular example.
The protocol defines the structure of the tagging header added to the frame.
Switches add VLAN tags to the frames before placing them into trunk links and remove the tags before forwarding frames through non-trunk ports.
When properly tagged, the frames can transverse any number of switches via trunk links and still be forwarded within the correct VLAN at the destination.
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.3 - Tagging Ethernet Frames for VLAN Identification

## Slide 30: VLANs in a Multi-Switched Environment Tagging Ethernet Frames for VLAN Identification (cont.)
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.3 - Tagging Ethernet Frames for VLAN Identification (cont.)

## Slide 31: VLANs in a Multi-Switched Environment Native VLANs and 802.1Q Tagging
Control traffic sent on the native VLAN should not be tagged.
Frames received untagged, remain untagged and are placed in the native VLAN when forwarded.
If there are no ports associated to the native VLAN and no other trunk links, an untagged frame is dropped.
When configuring a switch port on a Cisco switch, configure devices so that they do not send tagged frames on the native VLAN.
In Cisco switches, the native VLAN is VLAN 1, by default.
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.4 - Native VLANs and 802.1Q Tagging

## Slide 32: VLANs in a Multi-Switched Environment Voice VLAN Tagging
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.5 - Voice VLAN Tagging

## Slide 33: VLANs in a Multi-Switched Environment Activity – Predict Switch Behavior
Scenario 1: PC 1 sends a broadcast.
Scenario 2: PC 2 sends a broadcast.
Scenario 3: PC 3 sends a broadcast.
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.6 - Activity – Predict Switch Behavior

## Slide 34: 6.2 VLAN Implementations
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 6: VLANs

## Slide 35: VLAN Assignment VLAN Ranges on Catalyst Switches
Cisco Catalyst 2960 and 3560 Series switches support over 4,000 VLANs.
VLANs are split into two categories:
  Normal range VLANs
    VLAN numbers from 1 to 1,005
    Configurations stored in the vlan.dat (in the flash memory)
    IDs 1002 through 1005 are reserved for Token Ring and Fiber Distributed Data Interface (FDDI) VLANs, automatically created and cannot be removed
  Extended Range VLANs
    VLAN numbers from 1,006 to 4,096
    Configurations stored in the running configuration (NVRAM)
    VLAN Trunking Protocol (VTP) does not learn extended VLANs
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.1 - VLAN Ranges on Catalyst Switches

## Slide 36: VLAN Assignment VLAN Ranges on Catalyst Switches (cont.)
Normal Range VLANs
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.1 - VLAN Ranges on Catalyst Switches

## Slide 37: VLAN Assignment Creating a VLAN
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.2 – Creating a VLAN

## Slide 38: VLAN Assignment Assigning Ports to VLANs
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.3 – Assigning Ports to VLANs

## Slide 39: VLAN Assignment Changing VLAN Port Membership
Remove VLAN Assignment
Interface F0/18 was previously assigned to VLAN 20 which is still active, F0/18 reset to VLAN1
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.4 - Changing VLAN Port Membership

## Slide 40: VLAN Assignment Changing VLAN Port Membership (cont.)
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.4 - Changing VLAN Port Membership (cont.)

## Slide 41: VLAN Assignment Changing VLAN Port Membership (cont.)
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.4 - Changing VLAN Port Membership (cont.)

## Slide 42: VLAN Assignment Deleting VLANs
The entire vlan.dat file can be deleted using the delete flash:vlan.dat privileged EXEC mode command
Abbreviated command version (delete vlan.dat) can be used if the vlan.dat file has not been moved from its default location
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.5 – Deleting VLANs

## Slide 43: VLAN Assignment Verifying VLAN Information
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.6 - Verifying VLAN Information

## Slide 44: VLAN Assignment Verifying VLAN Information (cont.)
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.6 - Verifying VLAN Information

## Slide 45: VLAN Trunks Configuring IEEE 802.1q Trunk Links
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunks
6.2.2.1 - Configuring IEEE 802.1q Trunk Links

## Slide 46: VLAN Assignment Configuring IEEE 802.1q Trunk Links (cont.)
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunks
6.2.2.1 - Configuring IEEE 802.1q Trunk Links (cont.)

## Slide 47: VLAN Trunks Resetting the Trunk to Default State
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunks
6.2.2.2 - Resetting the Trunk to Default State

## Slide 48: VLAN Trunks Resetting the Trunk to Default State (cont.)
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunks
6.2.2.2 - Resetting the Trunk to Default State (cont.)

## Slide 49: VLAN Trunks Verifying Trunk Configuration
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunk
6.2.2.3 - Verifying Trunk Configuration

## Slide 50: Troubleshoot VLANs and Trunks IP Addressing Issues with VLANs
It is a common practice to associate a VLAN with an IP network.
Because different IP networks only communicate through a router, all devices within a VLAN must be part of the same IP network to communicate.
The figure displays that PC1 cannot communicate to the server because it has a wrong IP address configured.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.1 - IP Addressing Issues with VLANs

## Slide 51: Troubleshoot VLANs and Trunks Missing VLANs
If all the IP address mismatches have been solved, but the device still cannot connect, check if the VLAN exists in the switch.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.2 - Missing VLANs

## Slide 52: Troubleshoot VLANs and Trunks Missing VLANs (cont.)
If the VLAN to which a port belongs is deleted, the port becomes inactive. All ports belonging to the VLAN that was deleted are unable to communicate with the rest of the network.
Not functional until the missing VLAN is created using the vlan vlan_id global configuration.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.2 - Missing VLANs (cont.)

## Slide 53: Troubleshoot VLANs and Trunks Introduction to Troubleshooting Trunks
  Note: To solve a native VLAN mismatch, configure the native VLAN to be the same VLAN on both sides of the link.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.3 - Introduction to Troubleshooting Trunks

## Slide 54: Troubleshoot VLANs and Trunks Common Problems with Trunks
Trunking issues are usually associated with incorrect configurations.
The most common type of trunk configuration errors are:
    Native VLAN mismatches
    Trunk mode mismatches
    Allowed VLANs on trunks
If a trunk problem is detected, the best practice guidelines recommend to troubleshoot in the order shown above.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.4 - Common Problems with Trunks

## Slide 55: Troubleshoot VLANs and Trunks Common Problems with Trunks (cont.)
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.4 - Common Problems with Trunks

## Slide 56: Troubleshoot VLANs and Trunks Incorrect Port Mode
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.5 - Incorrect Port Mode

## Slide 57: Troubleshoot VLANs and Trunks Incorrect VLAN List
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.6 - Incorrect VLAN List

## Slide 58: Troubleshoot VLANs and Trunks Incorrect VLAN List (cont.)
VLANs must be allowed in the trunk before their frames can be transmitted across the link.
Use the switchport trunk allowed vlan command to specify which VLANs are allowed in a trunk link.
Use the show interfaces trunk command to ensure the correct VLANs are permitted in a trunk.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.6 - Incorrect VLAN List (cont.)

## Slide 59: 6.3 Inter-VLAN Routing Using Routers
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 6: VLANs

## Slide 60: Inter-VLAN Routing Operation What is Inter-VLAN Routing?
Layer 2 switches cannot forward traffic between VLANs without the assistance of a router.
Inter-VLAN routing is a process for forwarding network traffic from one VLAN to another, using a router.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.1 – Inter-VLAN Routing Operation
6.3.1.1 - What is Inter-VLAN Routing?

## Slide 61: Inter-VLAN Routing Operation Legacy Inter-VLAN Routing
In the past:
Actual routers were used to route between VLANs.
Each VLAN was connected to a different physical router interface.
Packets would arrive on the router through one interface, be routed and leave through another.
Because the router interfaces were connected to VLANs and had IP addresses from that specific VLAN, routing between VLANs was achieved.
Large networks with large number of VLANs required many router interfaces.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.1 – Inter-VLAN Routing Operation
6.3.1.2 - Legacy Inter-VLAN Routing

## Slide 62: Inter-VLAN Routing Operation Legacy Inter-VLAN Routing (cont.)
In this example, the router was configured with two separate physical interfaces to interact with the different VLANs and perform the routing.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.1 – Inter-VLAN Routing Operation
6.3.1.2 - Legacy Inter-VLAN Routing (cont.)

## Slide 63: Inter-VLAN Routing Operation Router-on-a-Stick Inter-VLAN Routing
The router-on-a-stick approach uses only one of the router’s physical interface.
One of the router’s physical interfaces is configured as a 802.1Q trunk port so it can understand VLAN tags.
Logical subinterfaces are created; one subinterface per VLAN.
Each subinterface is configured with an IP address from the VLAN it represents.
VLAN members (hosts) are configured to use the subinterface address as a default gateway.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.1 – Inter-VLAN Routing Operation
6.3.1.3 - Router-on-a-Stick Inter-VLAN Routing

## Slide 64: Inter-VLAN Routing Operation Router-on-a-Stick Inter-VLAN Routing (cont.)
Router interface configured to operate as a trunk link and is connected to a trunked switch port. The router performs inter-VLAN routing by accepting VLAN-tagged traffic on the trunk interface coming from the adjacent switch, and then, internally routing between the VLANs using subinterfaces. The router then forwards the routed traffic, VLAN-tagged for the destination VLAN, out the same physical interface as it used to receive the traffic.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.1 – Inter-VLAN Routing Operation
6.3.1.3 - Router-on-a-Stick Inter-VLAN Routing (cont.)

## Slide 65: Inter-VLAN Routing Operation Identify the Types of Inter-VLAN Routing Activity
Legacy or Router-on-a-Stick?
Notes: 6.3 – Inter-VLAN Routing Using Router
6.3.1 – Inter-VLAN Routing Operation
6.3.1.4 - Identify the Types of Inter-VLAN Routing Activity

## Slide 66: Inter-VLAN Routing Operation Identify the Types of Inter-VLAN Routing Activity (cont.)
Legacy or Router-on-a-Stick?
Notes: 6.3 – Inter-VLAN Routing Using Router
6.3.1 – Inter-VLAN Routing Operation
6.3.1.4 - Identify the Types of Inter-VLAN Routing Activity (cont.)

## Slide 67: Configure Legacy Inter-VLAN Routing Configure Legacy Inter-VLAN Routing: Preparation
Legacy inter-VLAN routing requires routers to have multiple physical interfaces.
Each one of the router’s physical interfaces is connected to a unique VLAN.
Each interface is also configured with an IP address for the subnet associated with the particular VLAN.
Network devices use the router as a gateway to access the devices connected to the other VLANs.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.2 – Configure Legacy Inter-VLAN Routing
6.3.2.1 - Configure Legacy Inter-VLAN Routing: Preparation

## Slide 68: Configure Legacy Inter-VLAN Routing Configure Legacy Inter-VLAN Routing: Switch Configuration
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.2 – Configure Legacy Inter-VLAN Routing
6.3.2.2 - Configure Legacy Inter-VLAN Routing: Switch Configuration

## Slide 69: Configure Legacy Inter-VLAN Routing Configure Legacy Inter-VLAN Routing: Router Interface Configuration
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.2 – Configure Legacy Inter-VLAN Routing
6.3.2.3 - Configure Legacy Inter-VLAN Routing: Router Interface Configuration

## Slide 70: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Preparation
An alternative to legacy inter-VLAN routing is to use VLAN trunking and subinterfaces.
VLAN trunking allows a single physical router interface to route traffic for multiple VLANs.
The physical interface of the router must be connected to a trunk link on the adjacent switch.
On the router, subinterfaces are created for each unique VLAN.
Each subinterface is assigned an IP address specific to its subnet or VLAN and is also configured to tag frames for that VLAN.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.1 - Configure Router-on-a Stick: Preparation

## Slide 71: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Switch Configuration
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.2 - Configure Router-on-a Stick: Switch Configuration

## Slide 72: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Router Subinterface Configuration
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.3 - Configure Router-on-a Stick: Router Subinterface Configuration

## Slide 73: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Verifying Subinterfaces
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.4 - Configure Router-on-a Stick: Verifying Subinterfaces

## Slide 74: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Verifying Subinterfaces (cont.)
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.2 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.4 - Configure Router-on-a Stick: Verifying Subinterfaces (cont.)

## Slide 75: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Verifying Routing
Access to devices on remote VLANs can be tested using the ping command.
The ping command sends an ICMP echo request to the destination address.
When a host receives an ICMP echo request, it responds with an ICMP echo reply.
Tracert is a useful utility for confirming the routed path taken between two devices.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.5 - Configure Router-on-a Stick: Verifying Routing

## Slide 76: 6.4 Chapter Summary
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 6: VLANs

## Slide 77: Chapter Summary Summary
  Explain the purpose of VLANs in a switched network.
  Explain how a switch forwards frames based on VLAN configuration in a multi-switch environment.
  Configure a switch port to be assigned to a VLAN based on requirements.
  Configure a trunk port on a LAN switch.
  Troubleshoot VLAN and trunk configurations in a switched network.
  Describe the two options for configuring inter-VLAN routing.
  Configure Legacy Inter-VLAN Routing.
  Configure Router-on-a-Stick Inter-VLAN Routing
Notes: 6.4 - Summary

## Slide 78: Section 6.1 Terms and Commands
VLAN
Logical broadcast domain
Data VLAN
Default VLAN
Native VLAN
Management VLAN
show vlan brief
Voice VLAN
VLAN Trunk
VLAN Segmentation
IEEE 802.1Q
VLAN Tagging
Canonical Format Identifier (CFI)
User Priority
VLAN ID
Type
show interfaces int switchport
Notes: Terms and Commands

## Slide 79: Section 6.2 Terms and Commands
Normal Range VLANs
Extended Range VLANs
vlan vlan-id
name vlan-name
switchport mode access
switchport access vlan vlan-id
interface range
no switchport access vlan vlan-id
no vlan vlan-id
delete flash:vlan.dat
delete vlan.dat
show vlan
show interfaces
show vlan summary
show interfaces vlan vlan_id
switchport mode trunk
switchport trunk allowed vlan vlan_list
switchport trunk native vlan vlan_id
no switchport trunk allowed vlan
no switchport trunk native vlan
show interfaces switchport
no switchport access vlan vlan_id
show interfaces trunk
show interfaces int_id trunk
Notes: New Terms and Commands

## Slide 80: Section 6.3 Terms and Commands
Legacy Inter-VLAN Routing
Router-on-a-Stick Inter-VLAN Routing
interface interface_id.subinterface_id
encapsulation dot1q vlan_id
IEEE 802.1Q
Notes: Terms and Commands