## Slide 1: Instructor Materials Chapter 4: Introduction to Switched Networks
CCNA Routing and Switching
Routing & Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing & Switching Essentials v6.0
Chapter 4: Introduction to Switched Networks

## Slide 2: Instructor Materials – Chapter 4 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 13
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Routing and Switching Essentials 6.0
Planning Guide
Chapter 4: Introduction to Switched Networks
Notes: Routing and Switching Essentials Planning Guide
Chapter 4: Introduction to Switched Networks

## Slide 4: Chapter 4: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
4.0.1.2 | Class Activity | Sent or Received Instructions | Optional
4.1.1.6 | Activity | Identify Switched Network Terminology | -
4.1.2.3 | Activity | Identify Switch Hardware | -
4.2.1.2 | Video Demonstration | MAC Address Tables on Connected Switches | -
4.2.1.6 | Activity | Frame Forwarding Methods | -
4.2.1.7 | Activity | Switch It! | -
4.3.1.1 | Class Activity | It’s Network Access Time | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 4: Assessment
Students should complete Chapter 4 “Assessment” after completing Chapter 4.
Quizzes, labs, Packet Tracers, and other activities can be used to informally assess student progress.
Notes: 5

## Slide 6
Prior to teaching Chapter 4, the instructor should:
Complete Chapter 4 “Assessment.”
The objectives of this chapter are:
  Explain how switched networks support small to medium-sized businesses.
  Explain how data, voice, and video are converged in a switched network.
  Describe a switched network in a small to medium-sized business.
  Explain how Layer 2 switches forward data in a small to medium-sized LAN.
  Explain how frames are forwarded in a switched network.
  Compare a collision domain to a broadcast domain.
Chapter 4: Best Practices
Notes: 6

## Slide 7
Chapter 4: Best Practices (Cont.)
Section 4.2
  Accentuate the fact a switch must populate its CAM table on its own.
  Introduce the idea that, in a practical network, manual CAM setup is not doable.
  Emphasize that the CAM table borrows its name from the type of physical memory used and how fast it is.
  Highlight the need and basic operation of a CAM table.
Notes: 7

## Slide 8
Chapter 4: Best Practices (Cont.)
Section 4.2 (Cont.)
  If needed, use the following analogy to clarify the collision domain concept:
    A collision domain is a room full of people and people are the network devices. Two (or more) people cannot talk at the same time; they must compete for a chance to communicate.
    The greater the number of people in the room, the greater are the chances of any two people trying to speak at the same time.
    Switches act as room divisions, breaking up a big room into smaller rooms. By dividing people into rooms, the competition is smaller (the chances of any two people inside a room having something to say at the same time reduces).
    A process to choose who is to speak next is needed. [leaving a hook for CSMA/CD]
Notes: 8

## Slide 9
Chapter 4: Best Practices (Cont.)
Section 4.2 (cont.)
  The same analogy holds for broadcast domains, but stress that broadcasts (heard by the entire room) are loud while unicasts (conversations taking place within a division) are quiet:
    Announcements (broadcasts) can be heard through the divisions.
    All the people in the room must listen (process) to the announcement, disturbing any ongoing task.
    Even if the announcement is only relevant within a division, it must be loud to be heard by all people in that division. This makes it heard through the division boundaries, too.
    To solve this, the divisions must be physically separated, creating a number of remote smaller rooms.
    Now announcements cannot be sent to all people anymore, only to people inside the smaller room where the announcement was created.
Notes: 9

## Slide 10
Chapter 4: Best Practices (Cont.)
Section 4.2 (cont.)
    Room divisions (switches) create collision domains, but cannot limit the reach of an announcement (broadcast).
    Physically separating rooms limits the reach of announcements (broadcasts), but also forces the use of a messenger (router) if messages are to exchanged between remote rooms.
Notes: 10

## Slide 11: Chapter 4: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna-blog
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Packet Tracer Know How 1: Packet Tracer 101 (self-enroll)
Notes: 11

## Slide 13: Chapter 4: Switched Networks
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 4: Switched Networks

## Slide 14: Chapter 4 - Sections & Objectives
4.1 LAN Design
  Explain how switched networks support small to medium-sized businesses.
  Explain how data, voice, and video are converged in a switched network.
  Describe a switched network in a small to medium-sized business.
4.2 The Switched Environment
  Explain how Layer 2 switches forward data in a small to medium-sized LAN.
  Explain how frames are forwarded in a switched network.
  Compare a collision domain to a broadcast domain.
Notes: 14

## Slide 15: 4.1 LAN Design
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 4: LAN Design

## Slide 16: Converged Networks Growing Complexity of Networks
Our digital world is changing.
Information must be accessed from anywhere in the world.
Notes: 4.1 – LAN Design
4.1.1 – Converged Networks
4.1.1.1 – Growing Complexity of Networks

## Slide 17: Converged Networks Elements of a Converged Network
To support collaboration, networks employ converged solutions.
Data services include voice systems, IP phones, voice gateways, video support, and video conferencing.
Call control, voice messaging, mobility, and automated attendant are also common features.
  Multiple types of traffic; only one network to manage.
  Substantial savings over installation and management of separate voice, video, and data networks.
  Integrates IT management.
Notes: 4.1 – LAN Design
4.1.1 – Converged Networks
4.1.1.2 – Elements of a Converged Network

## Slide 18: Converged Networks Cisco Borderless Networks
A network architecture that allows organizations to connect anyone, anywhere, anytime, and on any device securely, reliably, and seamlessly.
Designed to address IT and business challenges, such as supporting the converged network and changing work patterns.
Notes: 4.1 – LAN Design
4.1.1 – Converged Networks
4.1.1.3 – Cisco Borderless Networks

## Slide 19: Converged Networks Hierarchy in the Borderless Switched Network
Borderless switched network design guidelines are built upon the following principles:
  Hierarchical
  Modularity
  Resiliency
  Flexibility
Notes: 4.1 – LAN Design
4.1.1 – Converged Networks
4.1.1.4 – Hierarchy in the Borderless Switched Network

## Slide 20: Converged Networks Access, Distribution, and Core Layers
Notes: 4.1 – LAN Design
4.1.1 – Converged Networks
4.1.1.5 – Access, Distribution, and Core Layers

## Slide 21: Switched Networks Role of Switched Networks
Switching technologies are crucial to network design.
Switching allows traffic to be sent only where it is needed in most cases, using fast methods.
A switched LAN:
  Allows more flexibility
  Allows more traffic management
  Supports quality of service, additional security, wireless, IP telephony, and mobility services
Notes: 4.1 – LAN Design
4.1.2 – Switched Networks
4.1.2.1 – Role of Switched Networks

## Slide 22: Switched Networks Form Factors
Fixed
Configuration
Switches
Notes: 4.1 – LAN Design
4.1.2 – Switched Networks
4.1.2.2 – Form Factors

## Slide 23: Switched Networks Form Factors
Modular
Platform
Notes: 4.1 – LAN Design
4.1.2 – Switched Networks
4.1.2.2 – Form Factors

## Slide 24: Switched Networks Form Factors
Stackable
Configuration
Switches
Notes: 4.1 – LAN Design
4.1.2 – Switched Networks
4.1.2.2 – Form Factors

## Slide 25: 4.2 The Switched Environment
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 4: Introduction to Switched Networks

## Slide 26: Frame Forwarding Switching as a General Concept in Networking and Telecommunications
A switch makes a decision based on ingress and a destination port.
A LAN switch keeps a table that it uses to determine how to forward traffic through the switch.
Cisco LAN switches forward Ethernet frames based on the destination MAC address of the frames.
Notes: 4.2 – The Switched Environment
4.2.1 – Frame Forwarding
4.2.1.1 - Switching as a General Concept in Networking and Telecommunications

## Slide 27: Frame Forwarding Dynamically Populating a Switch MAC Address Table
A switch must first learn which devices exist on each port before it can transmit a frame.
As a switch learns the relationship of ports to devices, it builds a table called a MAC address or content addressable memory (CAM) table.
CAM is a special type of memory used in high-speed searching applications.
The information in the MAC address table is used to send frames.
When a switch receives an incoming frame with a MAC address that is not found in the CAM table, it floods it to all ports, except the one that received the frame.
Notes: 4.2 – The Switched Environment
4.2.1 – Frame Forwarding
4.2.1.2 - Dynamically Populating a Switch MAC Address Table

## Slide 28: Frame Forwarding Switch Forwarding Methods
Notes: 4.2 – The Switched Environment
4.2.1 – Frame Forwarding
4.2.1.3 – Switch Forwarding Methods

## Slide 29: Frame Forwarding Store-and-Forward Switching
Allows the switch to:
  Check for errors (via FCS check)
  Perform automatic buffering
Slower forwarding process
Notes: 4.2 – The Switched Environment
4.2.1 – Frame Forwarding
4.2.1.4 - Store-and-Forward Switching

## Slide 30: Frame Forwarding Cut-Through Switching
Allows the switch to start forwarding in about 10 microseconds
No FCS check
No automatic buffering
Notes: 4.2 – The Switched Environment
4.2.1 – Frame Forwarding
4.2.1.5 – Cut-Through Switching

## Slide 31: Switching Domains Collision Domains
Ethernet switch port:
Operating in half duplex, each segment is in its own collision domain.
Operating in full duplex eliminates collisions.
By default, will auto-negotiate full duplex when the adjacent device can also operate in full duplex.
Collision domain - Segment where devices compete to communicate.
Notes: 4.2 – The Switched Environment
4.2.2 – Switching Domains
4.2.2.1 – Collision Domains

## Slide 32: Switching Domains Broadcast Domains
A broadcast domain is the extent of the network where a broadcast frame can be heard.
Switches forward broadcast frames to all ports; therefore, switches do not break broadcast domains.
All ports of a switch, with its default configuration, belong to the same broadcast domain.
If two or more switches are connected, broadcasts are forwarded to all ports of all switches, except for the port that originally received the broadcast.
Notes: 4.2 – The Switched Environment
4.2.2 – Switching Domains
4.2.2.2 – Broadcast Domains

## Slide 33: Switching Domains Alleviating Network Congestion
Switches help alleviate network congestion by:
Facilitating the segmentation of a LAN into separate collision domains.
Providing full-duplex communication between devices.
Taking advantage of their high-port density.
Buffering large frames.
Employing high-speed ports.
Taking advantage of their fast internal switching process.
Having a low, per-port cost.
Notes: 4.2 – The Switched Environment
4.2.2 – Switching Domains
4.2.2.3 – Alleviating Network Congestion

## Slide 34: 4.3 Chapter Summary
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 4: Introduction to Switched Networks

## Slide 35: Chapter Summary Summary
The trend in networks is towards convergence using a single set of wires and devices to handle voice, video, and data transmission.
There has been a dramatic shift in the way businesses operate.
There are no physical offices or geographic boundaries constraints. Resources must now be seamlessly available anytime and anywhere.
The Cisco Borderless Network architecture enables different elements, from access switches to wireless access points, to work together and allow users to access resources from any place, at any time.
The traditional, three-layer hierarchical design model divides the network into core, distribution, and access layers, and allows each portion of the network to be optimized for specific functionality.
It provides modularity, resiliency, and flexibility, which provides a foundation that allows network designers to overlay security, mobility, and unified communication features.
Switches use either store-and-forward or cut-through switching.
Every port on a switch forms a separate collision domain allowing for extremely high-speed, full-duplex communication.
Switch ports do not block broadcasts and connecting switches can extend the size of the broadcast domain, often resulting in degraded network performance.
Notes: 4.3.1 - Summary

## Slide 36: Section 4.1 Terms and Commands
Converged network
Cisco borderless networks
Core layer
Distribution layer
Fixed configuration switches
Modular configuration switches
Stackable configuration switches
Cost of a switch
Frame buffers
Notes: New Terms and Commands

## Slide 37: Section 4.2 Terms and Commands
Ingress port
Content addressable memory (CAM)
Cut-through switching
Store-and-forward switching
Frame-check-sequence (FCS)
Fragment free switching
Collision domain
Broadcast domain
Notes: New Terms and Commands