## Slide 1: Instructor Materials Chapter 5: Switch Configuration
CCNA Routing and Switching
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 5: Switch Configuration

## Slide 2: Instructor Materials – Chapter 5 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 11
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Routing and Switching Essentials 6.0
Planning Guide
Chapter 5: Switch Configuration
Notes: Routing and Switching Essentials Planning Guide
Chapter 5: Switch Configuration

## Slide 4: Chapter 5: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
5.0.1.2 | Class Activity | Stand By Me | Optional
5.1.1.6 | Lab | Basic Switch Configuration | Recommended
5.1.2.2 | Syntax Checker | Configure Switch Ports at the Physical Layer | Recommended
5.1.2.3 | Syntax Checker | Enable auto-MDIX | Recommended
5.2.1.4 | Packet Tracer | Configuring SSH | Recommended
5.2.2.8 | Packet Tracer | Configuring Switch Port Security | Recommended
5.2.2.9 | Packet Tracer | Troubleshooting Switch Port Security | Recommended
5.2.2.10 | Lab | Configuring Switch Security Features | Optional
5.3.1.1 | Class Activity | Switch Trio | Optional
5.3.1.2 | Packet Tracer | Skills Integration Challenge | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 5: Assessment
Students should complete Chapter 5, “Assessment” after completing Chapter 5.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 5

## Slide 6
Prior to teaching Chapter 5, the instructor should:
Complete Chapter 5 “Assessment.”
The objectives of this chapter are:
  Configure initial settings on a Cisco switch.
  Configure switch ports to meet network requirements.
  Configure the management virtual interface on a switch.
  Configure the port security feature to restrict network access.
Chapter 5: Best Practices
Notes: 6

## Slide 7
Chapter 5: Best Practices (Cont.)
Section 5.1
  Demonstrate switch boot sequence.
  Load IOS 12 and 15 on one switch and edit the BOOT environment variable to load from IOS 12 to IOS 15. Demonstrate the results of the command.
  Discuss the purpose of the files in dir flash:
  Provide access to 2960 switches so the students can experiment with the mode button and the LED indicators.
Demonstrate adding a console cable and configuring a switch in Packet Tracer.
Notes: 7

## Slide 8
Chapter 5: Best Practices (Cont.)
Section 5.2
Demonstrate Telnet versus SSH with Wireshark.
Create several Packet Tracer topologies for demonstration purposes.
Demonstrate port-security features and violation modes using Packet Tracer.
Recommendation – Students should keep notes of “show commands” and the results.
Notes: 8

## Slide 9: Chapter 5: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna-blog
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Packet Tracer Know How 1: Packet Tracer 101 (self-enroll)
Notes: 9

## Slide 11: Chapter 5: Switch Configuration
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 5: Switch Configuration

## Slide 12: Chapter 5 - Sections & Objectives
5.1 Basic Switch Configuration
  Configure initial settings on a Cisco switch.
  Configure switch ports to meet network requirements.
5.2 Switch Security: Management and Implementation
  Configure the management virtual interface on a switch.
  Configure the port security feature to restrict network access.
Notes: 12

## Slide 13: 5.1 Basic Switch Configuration
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 5: Switch Configuration

## Slide 14: Configure a Switch with Initial Settings Switch Boot Sequence
Power-on self test (POST).
Run boot loader software.
Boot loader performs low-level CPU initialization.
Boot loader initializes the flash file system.
Boot loader locates and loads a default IOS operating system software image into memory and passes control of the switch over to the IOS.
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.1 Switch Boot Sequence

## Slide 15: Configure a Switch with Initial Settings Switch Boot Sequence (cont.)
To find a suitable Cisco IOS image, the switch goes through the following steps:
Step 1. It attempts to automatically boot by using information in the BOOT environment variable.
Step 2. If this variable is not set, the switch performs a top-to-bottom search through the flash file system. It loads and executes the first executable file, if it can.
Step 3. The IOS software then initializes the interfaces using the Cisco IOS commands found in the configuration file and startup configuration, which is stored in NVRAM.
Note: The boot system command can be used to set the BOOT environment variable. Use the show boot command to see to what the current IOS boot file is set.
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.1 Switch Boot Sequence (cont.)

## Slide 16: Configure a Switch with Initial Settings Recovering From a System Crash
The boot loader can also be used to manage the switch if the IOS cannot be loaded.
The boot loader can be accessed through a console connection by:
  Connecting a PC by console cable to the switch console port. Unplug the switch power cord.
  Reconnecting the power cord to the switch and press and hold the Mode button.
  The System LED turns briefly amber and then solid green. Release the Mode button.
The boot loader switch: prompt appears in the terminal emulation software on the PC.
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.2 – Recovering From a System Crash

## Slide 17: Configure a Switch with Initial Settings Switch LED Indicators
Each port on Cisco Catalyst switches have status LED indicator lights.
By default, these LED lights reflect port activity, but they can also provide other information about the switch through the Mode button.
The following modes are available on Cisco Catalyst 2960 switches:
  System LED
  Redundant Power System (RPS) LED
  Port Status LED
  Port Duplex LED
  Port Speed LED
  Power over Ethernet (PoE) Mode LED
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.3 - Switch LED Indicators

## Slide 18: Configure a Switch with Initial Settings Preparing for Basic Switch Management
To remotely manage a Cisco switch, it must be configured to access the network.
A console cable is used to connect a PC to the console port of a switch for configuration.
The IP information (address, subnet mask, gateway) is to be assigned to a switch virtual interface (SVI).
If managing the switch from a remote network, a default gateway must also be configured.
Although these IP settings allow remote management and remote access to the switch, they do not allow the switch to route Layer 3 packets.
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.4 - Preparing for Basic Switch Management

## Slide 19: Configure a Switch with Initial Settings Configuring Switch Management Access
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.5 - Configuring Basic Switch Management Access with IPv4

## Slide 20: Configure a Switch with Initial Settings Configuring Switch Management Access (cont.)
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.5 - Configuring Basic Switch Management Access with IPv4 (cont.)

## Slide 21: Configure a Switch with Initial Settings Configuring Switch Management Access (cont.)
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.5 - Configuring Basic Switch Management Access with IPv4 (cont.)

## Slide 22: Configure Switch Ports Duplex Communication
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.1 – Duplex Communication

## Slide 23: Configure Switch Ports Configure Switch Ports at the Physical Layer
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.2 - Configure Switch Ports at the Physical Layer

## Slide 24: Configure Switch Ports Auto-MDIX
Certain cable types (straight-through or crossover) were historically required when connecting devices.
The automatic medium-dependent interface crossover (auto-MDIX) feature eliminates this problem.
When auto-MDIX is enabled, the interface automatically detects and appropriately configures the connection.
When using auto-MDIX on an interface, the interface speed and duplex must be set to auto.
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.3 - Auto-MDIX

## Slide 25: Configure Switch Ports Auto-MDIX (cont.)
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.3 - Auto-MDIX

## Slide 26: Configure Switch Ports Auto-MDIX (cont.)
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.3 - Auto-MDIX

## Slide 27: Configure Switch Ports Verifying Switch Port Configuration
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.4 - Verifying Switch Port Configuration

## Slide 28: Configure Switch Ports Network Access Layer Issue
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.5 – Network Access Layer Issue

## Slide 29: Configure Switch Ports Network Access Layer Issue (cont.)
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.5 – Network Access Layer Issue

## Slide 30: Configure Switch Ports Troubleshooting Network Access Layer Issues
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.6 - Troubleshooting Network Access Layer Issues

## Slide 31: 5.2 Switch Security: Management and Implementation
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 5: Switch Configuration

## Slide 32: Secure Remote Access SSH Operation
Secure Shell (SSH) is a protocol that provides a secure (encrypted), command-line based connection to a remote device.
Because of strong encryption features, SSH should replace Telnet for management connections.
SSH uses TCP port 22, by default.
Telnet uses TCP port 23.
A version of the IOS software, including cryptographic (encrypted) features and capabilities, is required to enable SSH on Catalyst 2960 switches.
Notes: 5.2 – Switch Security: Management and Implementation
5.2.1 – Secure Remote Access
5.2.1.1 - SSH Operation

## Slide 33: Secure Remote Access Configuring SSH
Verify SHH Support – show ip ssh
Configure the IP domain.
Generate RSA key pairs.
Configure user authentication.
Configure the vty lines.
Enable SSH version 2.
Notes: 5.2 – Switch Security: Management and Implementation
5.2.1 – Secure Remote Access
5.2.1.2 - Configuring SSH

## Slide 34: Secure Remote Access Verifying SSH
Notes: 5.2 – Switch Security: Management and Implementation
5.2.1 – Secure Remote Access
5.2.1.3 - Verifying SSH

## Slide 35: Secure Remote Access Verifying SSH (cont.)
Notes: 5.2 – Switch Security: Management and Implementation
5.2.1 – Secure Remote Access
5.2.1.3 - Verifying SSH

## Slide 36: Switch Port Security Secure Unused Ports
Notes: 5.2 – Switch Security: Management and Implementation
5.2.1 – Switch Port Security
5.2.2.1 - Secure Unused Ports

## Slide 37: Switch Port Security Port Security: Operation
The MAC addresses of legitimate devices are allowed access, while other MAC addresses are denied.
Any additional attempts to connect by unknown MAC addresses generate a security violation.
Secure MAC addresses can be configured in a number of ways:
    Static secure MAC addresses – manually configured and added to running configuration - switchport port-security mac-address mac-address
    Dynamic secure MAC addresses – removed when switch restarts
    Sticky secure MAC addresses – added to running configuration and learned dynamically - switchport port-security mac-address sticky interface configuration mode command
Notes: 5.2 – Switch Security: Management and Implementation
5.2.2 – Switch Port Security
5.2.2.2 - Port Security: Operation

## Slide 38: Switch Port Security Port Security: Violation Modes
IOS considers a security violation when:
    The maximum number of secure MAC addresses for that interface have been added to the CAM, and a station whose MAC address is not in the address table attempts to access the interface.
There are three possible actions to take when a violation is detected:
    Protect – no notification received
    Restrict – notification received of security violation
    Shutdown
    switchport port-security violation {protect | restrict |shutdown} interface configuration mode command
Notes: 5.2 – Switch Security: Management and Implementation
5.2.2 – Switch Port Security
5.2.2.3 - Port Security: Violation Modes

## Slide 39: Switch Port Security Port Security: Violation Modes (cont.)
Notes: 5.2 – Switch Security: Management and Implementation
5.2.2 – Switch Port Security
5.2.2.3 - Port Security: Violation Modes

## Slide 40: Switch Port Security Port Security: Configuring
Notes: 5.2 – Switch Security: Management and Implementation
5.2.2 – Switch Port Security
5.2.2.4 - Port Security: Configuring

## Slide 41: Switch Port Security Port Security: Verifying
Notes: 5.2 – Switch Security: Management and Implementation
5.2.2 – Switch Port Security
5.2.2.5 - Port Security: Verifying

## Slide 42: Switch Port Security Port Security: Verifying (cont.)
Notes: 5.2 – Switch Security: Management and Implementation
5.2.2 – Switch Port Security
5.2.2.5 - Port Security: Verifying

## Slide 43: Switch Port Security Ports in Error Disabled State
A port security violation can put a switch in error disabled state.
A port in error disabled is effectively shutdown.
The switch communicates these events through console messages.
Notes: 5.2 – Switch Security: Management and Implementation
5.2.2 – Switch Port Security
5.2.2.6 - Ports in Error Disabled State

## Slide 44: Switch Port Security Ports in Error Disabled State (cont.)
The show interface command also reveals a switch port on error disabled state.
A shutdown or no shutdown interface configuration mode command must be issued to re-enable the port.
Notes: 5.2 – Switch Security: Management and Implementation
5.2.2 – Switch Port Security
5.2.2.6 - Ports in Error Disabled State

## Slide 45: 5.3 Chapter Summary
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 5: Switch Configuration

## Slide 46: Chapter Summary Summary
Cisco LAN switch boot sequence.
Cisco LAN switch LED modes.
How to remotely access and manage a Cisco LAN switch through a secure connection.
Cisco LAN switch port duplex modes.
Cisco LAN switch port security, violation modes, and actions.
Best practices for switched networks.
Notes: 5.3 - Summary

## Slide 47: Chapter Summary Summary
When a Cisco LAN switch is first powered on it goes through the following boot sequence:
  1. First, the switch loads a power-on self-test (POST) program stored in ROM. POST checks the CPU subsystem. It tests the CPU, DRAM, and the portion of the flash device that makes up the flash file system.
  2. Next, the switch loads the boot loader software. The boot loader is a small program stored in ROM and is run immediately after POST successfully completes.
  3. The boot loader performs low-level CPU initialization. It initializes the CPU registers, which control where physical memory is mapped, the quantity of memory, and its speed.
  4. The boot loader initializes the flash file system on the system board.
  5. Finally, the boot loader locates and loads a default IOS operating system software image into memory and gives control of the switch over to the IOS.
If the Cisco IOS files are missing or damaged, the boot loader program can be used to reload or recover from the problem.
The operational status of the switch is displayed by a series of LEDs on the front panel. These LEDs display such things as port status, duplex, and speed.
Notes: 5.3 - Summary

## Slide 48: Chapter Summary Summary
An IP address is configured on the SVI of the management VLAN to allow for remote configuration of the device. A default gateway belonging to the management VLAN must be configured on the switch using the ip default-gateway command. If the default gateway is not properly configured, remote management is not possible.
It is recommended that Secure Shell (SSH) be used to provide a secure (encrypted) management connection to a remote device to prevent the sniffing of unencrypted user names and passwords, which is possible when using protocols such as Telnet.
One of the advantages of a switch is that it allows full-duplex communication between devices, effectively doubling the communication rate. Although it is possible to specify the speed and duplex settings of a switch interface, it is recommended that the switch be allowed to set these parameters automatically to avoid errors.
Port security is only one defense against network compromise.
Notes: 5.3 - Summary

## Slide 49: Section 5.1 Terms and Commands
Power on Self-test (POST)
Boot loader
BOOT environment variable
boot system
show boot
Mode button
System LED
boot loader switch:
dir flash:
System LED
Redundant Power System (RPS) LED
Port Status LED
Port Duplex LED
Port Speed LED
Power Over Ethernet (POE) LED
Switch virtual interface (SVI)
VLAN
Full-duplex
Half-duplex
Auto-mdix
interface vlan 99
ip default-gateway
show ip interface brief
duplex auto
speed auto
mdix auto
show interfaces
Input errors
Runts
Giants
CRC Error
Output errors
Collisions
Late Collisions
Notes: Terms and Commands

## Slide 50: Section 5.2 Terms and Commands
Secure Shell (SSH)
show ip ssh version 2
crypto key generate rsa
crypto key zeroize rsa
Username username secret password
transport input ssh
login local
show ip ssh
Static Secure MAC Address
Dynamic Secure MAC Address
Sticky Secure MAC Address
show port-security
show port-security mac-address
show port-security mac-address sticky
show port-security interface
Protect
Restrict
Shutdown
switchport port-security violation{protect | restrict | shutdown}
Switchport port-security maximum #
show port-security interface interface-id
show port-security address
Secure-shutdown
Notes: Terms and Commands