## Slide 1: Instructor Materials Chapter 3: Dynamic Routing
CCNA Routing and Switching
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 3: Dynamic Routing

## Slide 2: Instructor Materials – Chapter 3 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 15
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Routing and Switching Essentials v6.0
Planning Guide
Chapter 3: Dynamic Routing
Notes: Routing and Switching Essentials v6.0 Planning Guide
Chapter 3: Dynamic Routing

## Slide 4: Chapter 3: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
3.0.1.2 | Class Activity | How Much Does This Cost | Optional
3.1.2.5 | Activity | Compare Static and Dynamic Routing | -
3.2.1.2 | Syntax Checker | Advertising the R2 and R3 Networks | -
3.2.1.3 | Syntax Checker | Verifying RIP Settings and Routes on R2 and R3 Networks | -
3.2.1.4 | Syntax Checker | Enable and Verify RIPv2 on R2 and R3 | -
3.2.1.5 | Syntax Checker | Disable Automatic Summarization on R2 and R3 | -
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 3: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
3.2.1.6 | Syntax Checker | Configuring and Verifying a Passive Interface on R2 and R3 | -
3.2.1.7 | Syntax Checker | Verifying the Gateway of Last Resort on R2 and R3 | -
3.2.1.8 | Packet Tracer | Configuring RIPv2 | Recommended
3.2.1.9 | Lab | Configuring RIPv2 | Optional
3.3.1.4 | Activity | Identify Parts of an IPv4 Routing Table Entry | -
3.3.2.6 | Activity | Identify Parent and Child IPv4 Routes | -
3.3.3.3 | Activity | Determine the Longest Match Route | -
3.3.4.4 | Activity | Identify Parts of an IPv6 Routing Table Entry | -
3.4.1.1 | Class Activity | IPv6, Details, Details… | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 3: Assessment
Students should complete Chapter 3, “Assessment” after completing Chapter 3.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 6

## Slide 7
Prior to teaching Chapter 3, the instructor should:
Complete Chapter 3, “Assessment.”
The objectives of this chapter are:
  Explain the purpose of dynamic routing protocols.
  Explain the use of dynamic routing and static routing.
  Configure the RIPv2 routing protocol.
  Explain the components of an IPv4 routing table entry for a given route.
  Explain the parent/child relationship in a dynamically built routing table.
  Determine which route will be used to forward a IPv4 packet.
  Determine which route will be used to forward a IPv6 packet.
Chapter 3: Best Practices
Notes: 7

## Slide 8
Chapter 3: Best Practices (Cont.)
Section 3.1
Create topologies in Packet Tracer similar to the topologies in the chapter and demonstrate static versus dynamic routing. Stress the advantages and disadvantages of static and dynamic routing.
During this chapter, consider setting up a large network as a Packet Tracer demonstration to allow students to see size and complexity.
Discuss with students the advantages and disadvantages of using routing protocols rather than static routing. Introduce terms such as metrics, convergence, distance vector, link state, classless, classful, IGP, and EGP.
Notes: 8

## Slide 9
Chapter 3: Best Practices (Cont.)
Section 3.2
Demonstrate each RIP command using Packet Tracer. Follow-up with the recommended lab, 3.2.1.8 Configuring RIPv2.
Syntax checkers in this section can be used to assist student in memorizing commands and interpreting error commands.
Notes: 9

## Slide 10
Chapter 3: Best Practices (Cont.)
Section 3.3
Reading routing tables is crucial in troubleshooting. Provide many examples of pre-configured topologies for practice.
Notes: 10

## Slide 11
Chapter 3: Best Practices (Cont.)
Discussion Questions
1. When do we need to use static routing?
2. When do we need to use dynamic routing?
3. What are the advantages and disadvantages of static and dynamic routing?
4. Compare and contrast the distance vector and link-state routing protocols.
5. What is the advantage of classless routing protocols over classful routing protocols?
6. Why do we want to have convergence in the shortest possible time after a change in a network?
7. Why do we need to have multiple metrics?
8. What affects the speed of convergence?
Notes: 11

## Slide 12
Chapter 3: Best Practices (Cont.)
Story for Chapter 3
When two companies join forces, their networks too must unite. Our customer had purchased one of its competitors and we were asked to integrate these two very different and very large networks. Each company’s remote offices needed access to all of the existing company networks as well as those of the new company. The static routing statements on each company’s core routers had grown as they each added remote offices. With the merger of these two companies’ networks, the number of static routes had doubled. For this merger to work, a simple answer to a complex problem had to be found. Because these networks were all managed by Cisco routers, a very simple EIGRP network schema was installed on all interconnected routers. This new dynamically routed network eliminated the need to maintain static routes on any of the core or remote office routers. In addition, it allowed for easy future expansion of any additional networks. With only a few hours of consulting time and a basic knowledge of dynamic routing, the network merger went through without a problem.
Notes: 12

## Slide 13: Chapter 3: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna-blog
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Packet Tracer Know How 1: Packet Tracer 101 (self-enroll)
Notes: 13

## Slide 15: Chapter 3: Dynamic Routing
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 3: Dynamic Routing

## Slide 16: Chapter 3 - Sections & Objectives
3.1 Dynamic Routing Protocols
  Explain the purpose of dynamic routing protocols.
  Explain the use of dynamic routing and static routing
3.2 RIPv2
  Configure the RIPv2 routing protocol.
3.3 The Routing Table
  Explain the components of an IPv4 routing table entry for a given route.
  Explain the parent/child relationship in a dynamically built routing table.
  Determine which route will be used to forward a IPv4 packet.
  Determine which route will be used to forward a IPv6 packet.
3.4 Summary
Notes: 16

## Slide 17: 3.1 Dynamic Routing Protocols
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 3: Dynamic Routing

## Slide 18: Dynamic Routing Protocol Overview Dynamic Routing Protocol Evolution
Dynamic routing protocols have been used in networks since the late 1980s.
Newer versions support the communication based on IPv6.
Routing Protocols Classification
Notes: 3.1 – Dynamic Routing Protocols
3.1.1 – Dynamic Routing Protocol Overview
3.1.1.1 – Dynamic Routing Protocol Evolution

## Slide 19: Dynamic Routing Protocol Overview Dynamic Routing Protocols Components
Routing Protocols are used to facilitate the exchange of routing information between routers.
The purpose of dynamic routing protocols includes:
Discovery of remote networks
Maintaining up-to-date routing information
Choosing the best path to destination networks
Ability to find a new best path if the current path is no longer available
Notes: 3.1 – Dynamic Routing Protocols
3.1.1 – Dynamic Routing Protocol Overview
3.1.1.2 - Dynamic Routing Protocols Components

## Slide 20: Dynamic Routing Protocol Overview Dynamic Routing Protocols Components (cont.)
Main components of dynamic routing protocols include:
Data structures - Routing protocols typically use tables or databases for its operations. This information is kept in RAM.
Routing protocol messages - Routing protocols use various types of messages to discover neighboring routers, exchange routing information, and other tasks to learn and maintain accurate information about the network.
Algorithm - Routing protocols use algorithms for facilitating routing information for best path determination.
Notes: 3.1 – Dynamic Routing Protocols
3.1.1 – Dynamic Routing Protocol Overview
3.1.1.2 - Dynamic Routing Protocols Components (cont.)

## Slide 21: Dynamic versus Static Routing Static Routing Uses
Networks typically use a combination of both static and dynamic routing.
Static routing has several primary uses:
Providing ease of routing table maintenance in smaller networks that are not expected to grow significantly.
Routing to and from a stub network. A network with only one default route out and no knowledge of any remote networks.
Accessing a single default router. This is used to represent a path to any network that does not have a match in the routing table.
Notes: 3.1 – Dynamic Routing Protocols
3.1.2 – Dynamic Versus Static Routing
3.1.2.1 - Static Routing Uses

## Slide 22: Dynamic verses Static Routing Static Routing Uses (cont.)
Notes: 3.1 – Dynamic Routing Protocols
3.1.2 – Dynamic verses Static Routing
3.1.2.1 - Static Routing Uses (cont.)

## Slide 23: Dynamic verses Static Routing Static Routing Advantages and Disadvantages
Notes: 3.1 – Dynamic Routing Protocols
3.1.2 – Dynamic verses Static Routing
3.1.2.2 - Static Routing Advantages and Disadvantages

## Slide 24: Dynamic verses Static Routing Dynamic Routing Advantages & Disadvantages
Notes: 3.1 – Dynamic Routing Protocols
3.1.2 – Dynamic verses Static Routing
3.1.2.4 – Dynamic Routing Advantages and Disadvantages

## Slide 25: 3.2 RIPv2
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 3: Dynamic Routing

## Slide 26: Configuring the RIP Protocol Router RIP Configuration Mode
Notes: 3.2 – RIPv2
3.2.1 – Configuring the RIP Protocol
3.2.1.1 – Router RIP Configuration Modes

## Slide 27: Configuring the RIP Protocol Verify RIP Routing
Notes: 3.2 – RIPv2
3.2.1 – Configuring the RIP Protocol
3.2.1.3 – Verify RIP Routing

## Slide 28: Configuring the RIP Protocol Enable and Verify RIPv2
Notes: 3.2 – RIPv2
3.2.1 – Configuring the RIP Protocol
3.2.1.4 – Enable and Verify RIPv2

## Slide 29: Configuring the RIP Protocol Disable Auto Summarization
Similarly to RIPv1, RIPv2 automatically summarizes networks at major network boundaries by default.
To modify the default RIPv2 behavior of automatic summarization, use the no auto-summary router configuration mode command.
This command has no effect when using RIPv1.
When automatic summarization has been disabled, RIPv2 no longer summarizes networks to their classful address at boundary routers. RIPv2 now includes all subnets and their appropriate masks in its routing updates.
The show ip protocols now states that automatic network summarization is not in effect.
Notes: 3.2 – RIPv2
3.2.1 – Configuring the RIP Protocol
3.2.1.5– Disable Automatic Summarization

## Slide 30: Configuring the RIP Protocol Configuring Passive Interfaces
Sending out unneeded updates on a LAN impacts the network in three ways:
Wasted Bandwidth
Wasted Resources
Security Risk
Notes: 3.2 – RIPv2
3.2.1 – Configuring the RIP Protocol
3.2.1.6 – Configuring Passive Interfaces

## Slide 31: Configuring the RIP Protocol Propagate a Default Route
Notes: 3.2 – RIPv2
3.2.1 – Configuring the RIP Protocol
3.2.1.7– Propagate a Default Route

## Slide 32: 3.3 The Routing Table
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 3: Dynamic Routing

## Slide 33: Parts of an IPv4 Route Entry Routing Table Entries
Notes: 3.3 – The Routing Table
3.3.1 – Parts of an IPv4 Route Entry
3.3.1.1 –Routing Table Entries

## Slide 34: Parts of an IPv4 Route Entry Routing Table Entries
Notes: 3.3 – The Routing Table
3.3.1 – Parts of an IPv4 Route Entry
3.3.1.1 –Routing Table Entries

## Slide 35: Parts of an IPv4 Route Entry Directly Connected Entries
Notes: 3.3 – The Routing Table
3.3.1 – Parts of an IPv4 Route Entry
3.3.1.2 –Directly Connected Entries

## Slide 36: Parts of an IPv4 Route Entry Remote Network Entries
Notes: 3.3 – The Routing Table
3.3.1 – Parts of an IPv4 Route Entry
3.3.1.3 – Remote Network Entries

## Slide 37: Dynamically Learned IPv4 Routes Routing Table Terms
Routes are discussed
in terms of:
Ultimate route
Level 1 route
Level 1 parent route
Level 2 child routes
Notes: 3.3 – The Routing Table
3.3.2 – Dynamically Learned IPv4 Routes
3.3.2.1 – Routing Table Terms

## Slide 38: Dynamically Learned IPv4 Routes Ultimate Route
An ultimate route is a routing table entry that contains either a next-hop IP address or an exit interface.
Directly connected, dynamically learned, and link local routes are ultimate routes.
Notes: 3.3 – The Routing Table
3.3.2 – Dynamically Learned IPv4 Routes
3.3.2.2 – Ultimate Route

## Slide 39: Dynamically Learned IPv4 Routes Level 1 Route
Notes: 3.3 – The Routing Table
3.3.2 – Dynamically Learned IPv4 Routes
3.3.2.3 – Level 1 Route

## Slide 40: Dynamically Learned IPv4 Routes Level 1 Parent Route
Notes: 3.3 – The Routing Table
3.3.2 – Dynamically Learned IPv4 Routes
3.3.2.4 – Level 1 Parent Route

## Slide 41: Dynamically Learned IPv4 Routes Level 2 Child Route
Notes: 3.3 – The Routing Table
3.3.2 – Dynamically Learned IPv4 Routes
3.3.2.5– Level 2 Child Route

## Slide 42: The IPv4 Route Lookup Process Route Lookup Process
If the best match is a level 1 ultimate route, then this route is used to forward the packet.
If the best match is a level 1 parent route, proceed to the next step.
The router examines child routes (the subnet routes) of the parent route for a best match.
If there is a match with a level 2 child route, that subnet is used to forward the packet.
If there is not a match with any of the level 2 child routes, proceed to the next step.
Notes: 3.3 – The Routing Table
3.3.3 – The IPv4 Route Lookup Process
3.3.3.1 – Route Lookup Process

## Slide 43: The Ipv4 Route Lookup Process Route Lookup Process (cont.)
The router continues searching level 1 supernet routes in the routing table for a match, including the default route, if there is one.
If there is now a lesser match with a level 1 supernet or default routes, the router uses that route to forward the packet.
If there is not a match with any route in the routing table, the router drops the packet.
Notes: 3.3 – The Routing Table
3.3.3 – The IPv4 Route Lookup Process
3.3.3.1 – Route Lookup Process (cont.)

## Slide 44: The IPv4 Route Lookup Process Best Route = Longest Match
Notes: 3.3 – The Routing Table
3.3.3 – The IPv4 Route Lookup Process
3.3.3.2 – Best Route = Longest Match

## Slide 45: The IPv4 Route Lookup Process IPv6 Routing Table Entries
Components of the IPv6 routing table are very similar to the IPv4 routing table (directly connected interfaces, static routes, and dynamically learned routes).
IPv6 is classless by design, all routes are effectively level 1 ultimate routes. There is no level 1 parent of level 2 child routes.
Notes: 3.3 – The Routing Table
3.3.4 – Analyze an IPv6 Routing Table
3.3.4.1 – IPv6 Routing Table Entries

## Slide 46: Analyze an IPVv6 Routing Table Directly Connected Entries
Notes: 3.3 – The Routing Table
3.3.4 – Analyze an IPv6 Routing Table
3.3.4.2 – Directly Connected Entries

## Slide 47: Analyze an IPVv6 Routing Table Remote IPv6 Network Entries
Notes: 3.3 – The Routing Table
3.3.4 – Analyze an IPv6 Routing Table
3.3.4.3 - Remote IPv6 Network Entries

## Slide 48: 3.4 Summary
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 6: Network Layer

## Slide 49: Chapter 3: Summary
Dynamic routing protocols:
Used by routers to automatically learn about remote networks from other routers.
Purpose includes: discovery of remote networks, maintaining up-to-date routing information, choosing the best path to destination networks, and ability to find a new best path if the current path is no longer available.
Best choice for large networks but static routing is better for stub networks.
Function to inform other routers about changes.
Notes: Chapter 3: Summary

## Slide 50: Chapter 3: Summary (cont.)
Dynamic routing protocols:
Responsible for discovering remote networks, as well as maintaining accurate network information.
Upon a change in the topology routing protocols propagate that information throughout the routing domain.
Convergence: The process of bringing all routing tables to a state of consistency, where all of the routers in the same routing domain, or area, have complete and accurate information about the network. Some routing protocols converge faster than others.
Notes: Chapter 3: Summary

## Slide 51: Chapter 3: Summary (cont.)
Dynamic routing protocols:
Cisco routers use the administrative distance value to determine which routing source to use.
Each dynamic routing protocol has a unique administrative value, along with static routes and directly connected networks.
Directly connected networks are preferred source, followed by static routes and then various dynamic routing protocols.
Notes: Chapter 3: Summary

## Slide 52: Chapter 3: Summary (cont.)
Dynamic routing protocols:
Each dynamic routing protocol has a unique administrative value, along with static routes and directly connected networks. The lower the administrative value, the more preferred the route source.
A directly connected network is always the preferred source, followed by static routes and then various dynamic routing protocols.
Routing table entries contain a route source, a destination network, and an outgoing interface.
Route sources can be either connected, local, static, or from a dynamic routing protocol.
IPv4 routing tables can contain four types of routes: ultimate routes, level 1 routes, level 1 parent routes, and level 2 child routes.
Because IPv6 is classless by design, all routes are effectively level 1 ultimate routes. There is no level 1 parent of level 2 child routes.
Notes: Chapter 3 Summary

## Slide 53: Section 3.1 Terms and Commands
Static routing
Dynamic routing
RIPv1
RIPv2
OSPF
IS-IS
IGRP
EIGRP
BGP
Routing table
Stub network
Update messages
Notes: New Terms and Commands

## Slide 54: Section 3.2 Terms and Commands
router rip
no router rip
network network-address
show ip protocols
show ip route
version 2
no version
no auto-summary
passive-interface
passive-interface default
no passive-interface
ip route 0.0.0.0 0.0.0.0
default-information originate
Notes: New Terms and Commands

## Slide 55: Section 3.3 Terms and Commands
Classful routing
Classless addressing
Route source (C and L)
Destination network
Outgoing interface
Administrative distance (AD)
Metric
Route timestamp
Ultimate route
Level 1 route
Level 1 parent route
Level 2 child route
Network route
Supernet route
Default route
Notes: New Terms and Commands