## Slide 1: Instructor Materials Chapter 8: DHCP
CCNA Routing and Switching
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 8: DHCP

## Slide 2: Instructor Materials – Chapter 8 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 12
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Routing and Switching Essentials 6.0 Planning Guide
Chapter 8: DHCP
Notes: Routing and Switching Essentials 6.0
Chapter 8: DHCP

## Slide 4: Chapter 8: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
8.1.1.5 | Activity | Identify the Steps in DHCPv4 Operation | -
8.1.2.1 | Syntax Checker | Configuring a DCHPv4 Server | -
8.1.2.3 | Syntax Checker | Configure DCHPv4 Relay | -
8.1.2.4 | Lab | Configuring Basic DHCPv4 on a Router | Recommended
8.1.2.5 | Lab | Configuring Basic DHCPv4 on a Switch | Optional
8.1.3.1 | Syntax Checker | Configuring a Router as DHCP Client | -
8.1.3.3 | Packet Tracer | Configuring DHCPv4 Using Cisco IOS | Recommended
8.1.4.4 | Lab | Troubleshooting DCHPv4 | Optional
8.2.1.8 | Activity | Identify the Steps in DHCPv6 Operation | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 8: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
8.2.2.3 | Syntax Checker | Configuring and Verifying Stateless DHCPv6 | -
8.2.3.3 | Syntax Checker | Configuring and Verifying Stateful DHCPv6 | -
8.2.3.4 | Syntax Checker | Configuring a Router as a DHCPv6 Relay Agent | -
8.2.3.5 | Lab | Configuring Stateless and Stateful DHCPv6 | Recommended
8.2.4.4 | Lab | Troubleshooting DHCPv6 | Recommended
8.3.1.1 | Class Activity | IoE and DHCP | Optional
8.3.1.2 | Packet Tracer | Skills Integration Challenge | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 8: Assessment
Students should complete Chapter 8 “Assessment” after completing Chapter 8.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 6

## Slide 7
Prior to teaching Chapter 8, the instructor should:
Complete Chapter 8 “Assessment.”
The objectives of this chapter are:
  Explain how DHCPv4 operates in a small- to medium-sized business network.
  Configure a router as a DHCPv4 server.
  Configure a router as a DHCPv4 client.
  Troubleshoot a DHCP configuration for IPv4 in a switched network.
  Explain the operation of DHCPv6.
  Configure stateless DHCPv6 for a small to medium-sized business.
  Configure stateful DHCPv6 for a small to medium-sized business.
  Troubleshoot a DHCP configuration for IPv6 in a switched network.
Chapter 8: Best Practices
Notes: 7

## Slide 8
Chapter 8: Best Practices (Cont.)
Section 8.1
  The instructor should ensure this chapter becomes as hands-on as possible.
  Discuss the advantages of using DHCP in a network.
  Provide extra opportunities for students to troubleshoot DHCPv4 issues.
Notes: 8

## Slide 9
Chapter 8: Best Practices (Cont.)
Section 8.2
  Provide opportunities for students to do both (DHCPv4 and DHCPv6) labs in Packet Tracer and hands-on mode.
  Provide extra opportunities for the students to troubleshoot DHCPv6 issues.
  When discussing this chapter you will need preconfigured DHCPv4 and DHCPv6 topologies. Students will learn best by seeing the commands and the results.
Notes: 9

## Slide 10: Chapter 8: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna-blog
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Packet Tracer Know How 1: Packet Tracer 101 (self-enroll)
Notes: 10

## Slide 12: Chapter 8: DHCP
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 8: DHCP

## Slide 13: Chapter 8 - Sections & Objectives
8.1 DHCPv4
  Explain how DHCPv4 operates in a small- to medium-sized business network.
  Configure a router as a DHCPv4 server.
  Configure a router as a DHCPv4 client.
  Troubleshoot a DHCP configuration for IPv4 in a switched network.
8.2 DHCPv6
  Explain the operation of DHCPv6.
  Configure stateless DHCPv6 for a small to medium-sized business.
  Configure stateful DHCPv6 for a small to medium-sized business.
  Troubleshoot a DHCP configuration for IPv6 in a switched network.
Notes: 13

## Slide 14: 8.1 DHCPv4
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 8: DHCPv4

## Slide 15: DHCPv4 Operation Introducing DHCPv4
DHCPv4:
  assigns IPv4 addresses and other network configuration information dynamically
  useful and timesaving tool for network administrators
  dynamically assigns, or leases, an IPv4 address from a pool of addresses
A Cisco router can be configured to provide DHCPv4 services.
Administrators configure DHCPv4 servers so that leases expire. Then the client must ask for another address, although the client is typically reassigned the same address.
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.1 – DHCPv4 Operation
8.1.1.1 – Introduction DHCPv4

## Slide 16: DHCPv4 Operation DHCPv4 Operation
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.1 – DHCPv4 Operation
8.1.1.2 – DHCPv4 Operation

## Slide 17: DHCPv4 Operation DHCPv4 Operation (cont.)
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.1 – DHCPv4 Operation
8.1.1.2 – DHCPv4 Operation

## Slide 18: DHCPv4 Operation DHCPv4 Message Format
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.1 – DHCPv4 Operation
8.1.1.3 - DHCPv4 Message Format

## Slide 19: DHCPv4 Operation DHCPv4 Discover and Offer Messages
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.1 – DHCPv4 Operation
8.1.1.4 - DHCPv4 Discover and Offer Messages

## Slide 20: DHCPv4 Operation DHCPv4 Discover and Offer Messages (cont.)
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.1 – DHCPv4 Operation
8.1.1.4 - DHCPv4 Discover and Offer Messages (cont.)

## Slide 21: Configure DHCPv4 Server Configure a Basic DHCPv4 Server
A Cisco router running the Cisco IOS software can be configured to act as a DHCPv4 server. To set up DHCP:
  Exclude addresses from the pool.
  Set up the DHCP pool name.
  Define the range of addresses and subnet mask. Use the default-router command for the default gateway. Optional parameters that can be included in the pool – dns server, domain-name.
To disable DHCP, use the no service dhcp command.
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.2 – Configure DHCPv4 Server
8.1.2.1 - Configure a Basic DHCPv4 Server

## Slide 22: Configure DHCPv4 Server Verifying DHCPv4
Commands to verify DHCP:
  show running-config | section dhcp
  show ip dhcp binding
  show ip dhcp server statistics
On the PC, issue the ipconfig /all command.
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.2 – Configure DHCPv4 Server
8.1.2.2 - Verifying DHCPv4

## Slide 23: Configure DHCPv4 Server DHCPv4 Relay
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.2 – Configure DHCPv4 Server
8.1.2.3 - DHCPv4 Relay

## Slide 24: Configure DHCPv4 Server DHCPv4 Relay (cont.)
  Using an IP helper address enables a router to forward DHCPv4 broadcasts to the DHCPv4 server. Acting as a relay.
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.2 – Configure DHCPv4 Server
8.1.2.3 - DHCPv4 Relay (cont.)

## Slide 25: Configure DHCPv4 Client Configuring a Router as a DHCPv4 client
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.3 – Configure DHCPv4 Client
8.1.3.1 - Configuring a Router as a DHCPv4 client

## Slide 26: Configure DHCPv4 Client Configuring a Wireless Router as a DHCPv4 Client
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.3 – Configure DHCPv4 Client
8.1.3.2 - Configuring a Wireless Router as a DHCPv4 Client

## Slide 27: Troubleshooting DHCPv4 Troubleshooting Tasks
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.4– Troubleshooting DHCPv4
8.1.4.1 - Troubleshooting Tasks

## Slide 28: Troubleshooting DHCPv4 Verify Router DHCPv4 Configuration
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.4– Troubleshooting DHCPv4
8.1.4.2 - Verify Router DHCPv4 Configuration

## Slide 29: Troubleshooting DHCPv4 Debugging DHCPv4
  The figure shows an extended ACL permitting only packets with UDP destination ports of 67 or 68. These are the typical ports used by DHCPv4 clients and servers when sending DHCPv4 messages. The extended ACL is used with the debug ip packet command to display only DHCPv4 messages.
Notes: 8.1 – Dynamic Host Configuration Protocol v4
8.1.4 – Troubleshooting DHCPv4
8.1.4.3 - Debugging DHCPv4

## Slide 30: 8.2 DHCPv6
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 8: Dynamic Host Configuration Protocol v6

## Slide 31: SLAAC and DHCPv6 Stateless Address Autoconfiguration (SLAAC)
  SLAAC uses ICMPv6 Router Solicitation and Router Advertisement messages to provide addressing and other configuration information that would normally be provided by a DHCP server:
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.1 – SLAAC and DHCPv6
8.2.1.1 - Stateless Address Autoconfiguration (SLAAC)

## Slide 32: SLAAC and DHCPv6 SLAAC Operation
  A router must have IPv6 routing enabled before it can send RA messages: Router(config)# ipv6 unicast-routing
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.1 – SLAAC and DHCPv6
8.2.1.2 - SLAAC Operation

## Slide 33: SLAAC and DHCPv6 SLAAC and DHCPv6
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.1 – SLAAC and DHCPv6
8.2.1.3 - SLAAC and DHCPv6

## Slide 34: SLAAC and DHCPv6 SLAAC Option
  SLAAC is the default option on Cisco routers. Both the M flag and the O flag are set to 0 in the RA, as shown in the figure.
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.1 – SLAAC and DHCPv6
8.2.1.4 - SLAAC Option

## Slide 35: SLAAC and DHCPv6 Stateless DHCPv6 Option
  To modify the RA message sent on the interface of a router to indicate stateless DHCPv6, use the following command: Router(config-if)# ipv6 nd other-config-flag
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.1 – SLAAC and DHCPv6
8.2.1.5 - Stateless DHCPv6 Option

## Slide 36: SLAAC and DHCPv6 Stateful DHCPv6 Option
This option is the most similar to DHCPv4. In this case, the RA message informs the client not to use the information in the RA message. All addressing information and configuration information must be obtained from a stateful DHCPv6 server. Router(config-if)# ipv6 nd managed-config-flag
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.1 – SLAAC and DHCPv6
8.2.1.6 - Stateless DHCPv6 Option (cont.)

## Slide 37: SLAAC and DHCPv6 DHCPv6 Operations
If stateless or stateful DHCPv6 is indicated in the RA message, then the device begins DHCPv6 client/server communications.
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.1 – SLAAC and DHCPv6
8.2.1.7 - DHCPv6 Operations

## Slide 38: Stateless DHCPv6 Configuring a Router as a Stateless DHCPv6 Server
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.2 – Stateless DHCPv6
8.2.2.1 - Configuring a Router as a Stateless DHCPv6 Server

## Slide 39: Stateless DHCPv6 Configuring a Router as a Stateless DHCPv6 Client
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.2 – Stateless DHCPv6
8.2.2.2 - Configuring a Router as a Stateless DHCPv6 Client

## Slide 40: Stateless DHCPv6 Verifying Stateless DHCPv6
Verify the stateless DHCP client using the following commands:
show ipv6 interface
debug ipv6 dhcp detail
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.2 – Stateless DHCPv6
8.2.2.3 - Verifying Stateless DHCPv6

## Slide 41: Stateful DHCPv6 Server Configuring a Router as a Stateful DHCPv6 Server
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.3– Stateful DHCPv6 Server
8.2.3.1 - Configuring a Router as a Stateful DHCPv6 Server

## Slide 42: Stateful DHCPv6 Server Configuring a Router as a Stateful DHCPv6 Server (cont.)
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.3– Stateful DHCPv6 Server
8.2.3.1 - Configuring a Router as a Stateful DHCPv6 Server (cont.)

## Slide 43: Stateful DHCPv6 Server Configuring a Router as a Stateful DHCPv6 Client
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.3– Stateful DHCPv6 Server
8.2.3.2 - Configuring a Router as a Stateful DHCPv6 Client

## Slide 44: Stateful DHCPv6 Server Verifying Stateful DHCPv6
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.3 – Stateful DHCPv6 Server
8.2.3.3 - Verifying Stateful DHCPv6

## Slide 45: Stateful DHCPv6 Server Verifying Stateful DHCPv6 (cont.)
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.3– Stateful DHCPv6 Server
8.2.3.3 - Verifying Stateful DHCPv6 (cont.)

## Slide 46: Stateful DHCPv6 Configuring a Router as a DHCPv6 Relay Agent
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.3– Stateful DHCPv6 Server
8.2.3.4 - Configuring a Router as a DHCPv6 Relay Agent

## Slide 47: Troubleshooting DHCPv6 Troubleshooting Tasks
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.4 – Troubleshooting DHCPv6
8.2.4.1 - Troubleshooting Tasks

## Slide 48: Troubleshooting DHCPv6 Verify Router DHCPv6 Configuration
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.4 – Troubleshooting DHCPv6
8.2.4.2 - Verify Router DHCPv6 Configuration

## Slide 49: Troubleshooting DHCPv6 Debugging DHCPv6
Notes: 8.2 – Dynamic Host Configuration Protocol v6
8.2.4 – Troubleshooting DHCPv6
8.2.4.3 - Debugging DHCPv6

## Slide 50: 8.3 Summary
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 8: DHCP

## Slide 51: Chapter Summary Summary
Explain how DHCPv4 operates in a small- to medium-sized business network.
Configure a router as a DHCPv4 server.
Configure a router as a DHCPv4 client.
Troubleshoot a DHCP configuration for IPv4 in a switched network.
Explain the operation of DHCPv6.
Configure stateless DHCPv6 for a small to medium-sized business.
Configure stateful DHCPv6 for a small to medium-sized business.
Troubleshoot a DHCP configuration for IPv6 in a switched network.
Notes: 8.4 - Summary

## Slide 52: Section 8.1 Terms and Commands
Dynamic Host Configuration Protocol (DHCP)
DHCP Discover (DHCPDISCOVER)
DHCP Offer (DHCPOFFER)
DHCP Request (DHCPREQUEST)
DHCP Acknowledgment (DHCPACK)
Operation (OP) Code
Hardware Address Length
Hops
Transaction Identifier
ip dhcp excluded-address
ip dhcp pool pool-name
default-router
dns-server
domain-name domain
lease
netbios-name-server
no service dhcp
show running-config | section dhcp
show ip dhcp binding
show ip dhcp server statistics
ip helper-address
ip address dhcp
show ip dhcp conflict
debug ip packet
debug ip dhcp server events
Notes: Terms and Commands

## Slide 53: Section 8.2 Terms and Commands
Stateless Address Autoconfiguration (SLAAC)
Dynamic Host Configuration Protocol for IPv6 (Stateful DHCPv6)
Router Advertisement (RA) message
Stateless DHCPv6 Option (Router Advertisement and DHCPv6)
Stateful DHCPv6 (DHCPv6 only)
Stateless DHCPv6 client
Stateful DHCPv6 client
DHCPv6 SOLICIT
DHCPv6 ADVERTISE
DHCPv6 REQUEST
no ipv6 nd managed-config-flag
no ipv6 nd other-config-flag
ipv6 nd other-config-flag
ipv6 nd managed-config-flag
ipv6 dhcp server pool-name
ipv6 enable
ipv6 address autoconfig
show ipv6 dhcp pool
show ipv6 interface type number
debug ipv6 dhcp detail
address prefix
ipv6 dhcp server pool-name
ipv6 dhcp pool pool-name
ipv6 enable
ipv6 address dhcp
show ipv6 dhcp binding
ipv6 dhcp relay destination ipv6_address
show ipv6 dhcp interface type number
Notes: New Terms and Commands