## Slide 1: Instructor Materials Chapter 9: NAT for IPv4
CCNA Routing and Switching
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 9: NAT for IPv4

## Slide 2: Instructor Materials – Chapter 9 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 13
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Routing and Switching v6.0 Planning Guide
Chapter 9: NAT for IPv4
Notes: Routing and Switching Planning Guide
Chapter 9: NAT for IPv4

## Slide 4: Chapter 9: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
9.0.1.2 | Class Activity | Conceptual NAT | Optional
9.1.1.6 | Interactive Activity | Identify NAT Terminology | 
9.1.2.6 | Packet Tracer | Investigating NAT Operation | Recommended
9.2.1.1 | Syntax Checker | Configuring Static NAT | 
9.2.1.4 | Packet Tracer | Configuring Static NAT | 
9.2.2.2 | Syntax Checker | Configure Dynamic NATs | 
9.2.2.5 | Packet Tracer | Configuring Dynamic NAT | Recommended
9.2.2.6 | Lab | Configuring Dynamic and Static NAT | Optional
9.2.3.1 | Syntax Checker | Configuring PAT using an Address Pool | 
9.2.3.2 | Syntax Checker | Configuring PAT using a Single Address | 
9.2.3.5 | Interactive Activity | Identify the Address Information at Each Hop | 
9.2.3.6 | Packet Tracer | Implementing Static and Dynamic NAT | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 9: Activities (Cont.)
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
9.2.3.7 | Lab | Configuring Port Address Translation (PAT) | Recommended
9.2.4.4 | Packet Tracer | Configuring Port Forwarding on a Wireless Router | Optional
9.3.1.4 | Packet Tracer | Verifying and Troubleshooting NAT Configurations | Recommended
9.3.1.5 | Lab | Troubleshooting NAT Configurations | Optional
9.4.1.1 | Class Activity | NAT Check | Optional
9.4.1.2 | Packet Tracer | Skills Integration Challenge | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 9: Assessment
Students should complete Chapter 9, “Assessment” after completing Chapter 9.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 6

## Slide 7
Prior to teaching Chapter 9, the instructor should:
Complete Chapter 9, “Assessment.”
  Ensure all the activities are completed. This is a very important concept and hands-on time is vital.
  Basic NAT Troubleshooting information:
  http://www.cisco.com/en/US/customer/tech/tk648/tk361/technologies_tech_note09186a0080094c32.shtml
The objectives of this chapter are:
  Describe NAT characteristics.
  Describe the benefits and drawbacks of NAT.
  Configure static NAT using the CLI.
  Configure dynamic NAT using the CLI.
  Configure PAT using the CLI.
  Configure port forwarding using the CLI.
  Configure NAT64.
  Use show commands to verify NAT operation.
Chapter 9: Best Practices
Notes: 7

## Slide 8
Chapter 9: Best Practices (Cont.)
Overview
All public IPv4 addresses that transverse the Internet must be registered with a Regional Internet Registry (RIR). However, with a theoretical maximum of 4.3 billion addresses, IPv4 address space is severely limited.
With the proliferation of personal computing and the advent of the World Wide Web, it soon became obvious that 4.3 billion IPv4 addresses would not be enough.
The long term solution was IPv6, but more immediate solutions to address exhaustion were required.
For the short term, several solutions were implemented by the IETF, including Network Address Translation (NAT) and RFC 1918, Address Allocation for Private Internets.
Notes: 8

## Slide 9: Chapter 9: Best Practices (Cont.)
Section 9.1
  How NAT, combined with the use of private address space, is used to both conserve and more efficiently use IPv4 addresses to provide networks of all sizes access to the Internet.
  NAT characteristics, terminology, and general operations.
  Three different types of NAT are static NAT, dynamic NAT, and NAT with overloading.
  The benefits and disadvantages of NAT.
Section 9.2
  The configuration, verification, and analysis of static NAT, dynamic NAT, and NAT with overloading.
  How port forwarding can be used to access an internal devices from the Internet.
Notes: 9

## Slide 10: Chapter 9: Best Practices (Cont.)
Section 9.3
  Troubleshooting NAT using show and debug commands.
  How NAT for IPv6 is used to translate between IPv6 addresses and IPv4 addresses.
Notes: 10

## Slide 11: Chapter 9: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna-blog
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Packet Tracer Know How 1: Packet Tracer 101 (self-enroll)
Notes: 11

## Slide 13: Chapter 9: NAT for IPv4
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 9: NAT for IPv4

## Slide 14: Chapter 9 - Sections & Objectives
9.1 Network Layer Protocols
  Explain how NAT provides IPv4 address scalability in a small to medium-sized business network.
9.2 Configuring NAT
  Configure NAT services on the edge router to provide IPv4 address scalability in a small to medium-sized business network.
9.3 Troubleshoot NAT Configurations
  Troubleshoot NAT issues in a small to medium-sized business network.
Notes: 14

## Slide 15: 9.1 NAT Operation
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 9: NAT for IPv4

## Slide 16: NAT Operation NAT Characteristics
IPv4 Private Address Space
  10.0.0.0 /8, 172.16.0.0 /12, and 192.168.0.0 /16
What is NAT?
  Process to translate network IPv4 address
  Conserve public IPv4 addresses
  Configured at the border router for translation
NAT Terminology
  Inside address
  Inside local address
  Inside global address
  Outside address
  Outside local address
  Outside global address
Notes: 9.1 – NAT Operation
9.1.1 – NAT Characteristics

## Slide 17: NAT Operation Types of NAT
Static NAT
  One-to-one mapping of local and global addresses
  Configured by the network administrator and remain constant.
Dynamic NAT
  Uses a pool of public addresses and assigns them on a first-come, first-served basis
  Requires that enough public addresses for the total number of simultaneous user sessions
Port Address Translation (PAT)
  Maps multiple private IPv4 addresses to a single public IPv4 address or a few addresses
  Also known as NAT overload
  Validates that the incoming packets were requested
  Uses port numbers to forward the response packets to the correct internal device
Notes: 9.1 – NAT Operation
9.1.2 – Types of NAT

## Slide 18: NAT Operation NAT Advantages
Advantages of NAT
  Conserves the legally registered addressing scheme
  Increases the flexibility of connections to the public network
  Provides consistency for internal network addressing schemes
  Provides network security
Disadvantages of NAT
  Performance is degraded
  End-to-end functionality is degraded
  End-to-end IP traceability is lost
  Tunneling is more complicated
  Initiating TCP connections can be disrupted
Notes: 9.1 – NAT Operation
9.1.3 – NAT Advantages

## Slide 19: 9.2 Configuring NAT
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 9: NAT for IPv4

## Slide 20: Configuring NAT Configuring Static NAT
Configuring Static NAT
  Create the mapping between the inside local and outside local addresses
    ip nat inside source static local-ip global-ip
  Define which interfaces belong to the inside network and which belong to the outside network
    ip nat inside
    ip nat outside
Analyzing Static NAT
Verifying Static NAT
  show ip nat translations
  show ip nat statistics
  clear ip nat statistics
Notes: 9.2 – Configuring NAT
9.2.1 – Configuring Static NAT

## Slide 21: Configuring NAT Configuring Dynamic NAT
Dynamic NAT Operation
  The pool of public IPv4 addresses (inside global address pool) is available to any device on the inside network on a first-come, first-served basis.
  With dynamic NAT, a single inside address is translated to a single outside address.
  The pool must be large enough to accommodate all inside devices.
  A device is unable to communicate to any external networks if no addresses are available in the pool.
Notes: 9.2 – Configuring NAT
9.2.2 – Configuring Dynamic NAT

## Slide 22: Configuring NAT Configuring Dynamic NAT (Cont.)
Configuring Dynamic NAT
  Create the mapping between the inside local and outside local addresses
    ip nat pool name start-ip end-ip {netmask netmask | prefix-length prefix-length}
  Create a standard ACL to permit those addresses to be translated
    access-list access-list-number permit source [source-wildcard]
  Bind the ACL to the pool
    ip nat inside source list access-list-number pool name
  Identify the inside and outside interfaces
    ip nat inside
    ip nat outside
Notes: 9.2 – Configuring NAT
9.2.2 – Configuring Dynamic NAT

## Slide 23: Configuring NAT Configuring Dynamic NAT (Cont.)
Analyzing Dynamic NAT
Verifying Dynamic NAT
  show ip nat translations
  show ip nat translations verbose
  clear ip nat statistics
  clear ip nat translations *
Notes: 9.2 – Configuring NAT
9.2.2 – Configuring Dynamic NAT

## Slide 24: Configuring NAT Configuring Port Address Translations (PAT)
Configuring PAT: Address Pool
  Create the mapping between the inside local and outside local addresses
    ip nat pool name start-ip end-ip {netmask netmask | prefix-length prefix-length}
  Create a standard ACL to permit those addresses to be translated
    access-list access-list-number permit source [source-wildcard]
  Bind the ACL to the pool
    ip nat inside source list access-list-number pool name
  Identify the inside and outside interfaces
    ip nat inside
    ip nat outside
Notes: 9.2 – Configuring NAT
9.2.3 – Configuring Port Address Translations (PAT)

## Slide 25: Configuring NAT Configuring Port Address Translations (PAT) (Cont.)
Configuring PAT: Single Address
  Define a standard ACL to permit those addresses to be translated
    access-list access-list-number permit source [source-wildcard]
  Establish dynamic source translation, specify the ACL, exit interface, and overload option
    ip nat inside source list access-list-number interface type name overload
  Identify the inside and outside interfaces
    ip nat inside
    ip nat outside
Notes: 9.2 – Configuring NAT
9.2.3 – Configuring Port Address Translations (PAT)

## Slide 26: Configuring NAT Configuring Port Address Translations (PAT) (Cont.)
Analyzing PAT
Verifying PAT
  show ip nat translations
  show ip nat statistics
  slear ip nat statistics
Notes: 9.2 – Configuring NAT
9.2.3 – Configuring Port Address Translations (PAT)

## Slide 27: Configuring NAT Port Forwarding
Port Forwarding
  Port forwarding is the act of forwarding a network port from one network node to another.
  A packet sent to the public IP address and port of a router can be forwarded to a private IP address and port in inside network.
  Port forwarding is helpful in situations where servers have private addresses, not reachable from the outside networks.
Wireless Router Example
Configuring Port Forwarding with IOS
  ip nat inside source [static {tcp | udp local-ip local-port global-ip global-port} [extendable]
Notes: 9.2 – Configuring NAT
9.2.4 – Port Forwarding

## Slide 28: Configuring NAT Configuring NAT and IPv6
NAT for IPv6?
  IPv6 with a 128-bit address provides 340 undecillion addresses.
  Address space is not an issue for IPv6.
  IPv6 makes IPv4 public-private NAT unnecessary by design; however, IPv6 does implement a form of private addresses, and it is implemented differently than they are for IPv4.
IPv6 Unique Local Address
  IPv6 unique local addresses (ULAs) are designed to allow IPv6 communications within a local site.
  ULAs are not meant to provide additional IPv6 address space.
  ULAs have the prefix FC00::/7, which results in a first hextet range of FC00 to FDFF.
  ULAs are also known as local IPv6 addresses (not to be confused with IPv6 link-local addresses).
Notes: 9.2 – Configuring NAT
9.2.5 – Configuring NAT and IPv6

## Slide 29: Configuring NAT Configuring NAT and IPv6 (Cont.)
NAT for IPv6
  IPv6 also uses NAT, but in a much different context.
  In IPv6, NAT is used to provide transparent communication between IPv6 and IPv4.
  NAT64 is not intended to be a permanent solution; it is meant to be a transition mechanism.
  Network Address Translation-Protocol Translation (NAT-PT) was another NAT-based transition mechanism for IPv6, but is now deprecated by IETF.
  NAT64 is now recommended.
Notes: 9.2 – Configuring NAT
9.2.5 – Configuring NAT and IPv6

## Slide 30: 9.3 Troubleshooting NAT
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 9: NAT for IPv4

## Slide 31: Troubleshooting NAT Troubleshooting NAT Configurations
Troubleshooting NAT: show commands
  clear ip nat statistics
  clear ip nat translations *
  show ip nat statistics
  Show ip nat translations
Troubleshooting NAT: debug commands
  debug ip nat
Notes: 9.3 – Troubleshooting NAT
9.3.1 – Troubleshooting NAT Configurations

## Slide 32: 9.4 Chapter Summary
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 9: NAT for IPv4

## Slide 33: Chapter Summary Summary
How NAT is used to help alleviate the depletion of the IPv4 address space.
NAT conserves public address space and saves considerable administrative overhead in managing adds, moves, and changes.
NAT for IPv4, including:
  NAT characteristics, terminology, and general operations
  Different types of NAT, including static NAT, dynamic NAT, and NAT with overloading
  Benefits and disadvantages of NAT
The configuration, verification, and analysis of static NAT, dynamic NAT, and NAT with overloading.
How port forwarding can be used to access an internal devices from the Internet.
Troubleshooting NAT using show and debug commands.
How NAT for IPv6 is used to translate between IPv6 addresses and IPv4 addresses.
Notes: 9.4.1 - Summary

## Slide 34: Section 9.1 New Terms and Commands
Dynamic Network Address Translation (Dynamic NAT)
Global Address
Inside Address
Inside Global Address
Inside Local Address
Local Address
Network Address Translation (NAT)
Outside Address
Outside Global Address
Outside Local Address
Port Address Translation (PAT)
Private Address
Public Address
RFC 1918
Static Network Address Translation (Static NAT)
Notes: New Terms and Commands

## Slide 35: Section 9.2 New Terms and Commands
show ip nat statistics command
clear ip nat statistics command
clear ip nat translation * command
ip nat inside source command
ip nat inside source list access-list-number pool name command
ip nat pool command
ip nat translation timeout command
NAT64
Overload
Port Forwarding
show ip nat statistics command
show ip nat translations command
Unique Local Address (ULA)
Notes: New Terms and Commands

## Slide 36: Section 9.3 New Terms and Commands
debug ip nat command
debug ip nat detailed command
Notes: New Terms and Commands