## Slide 1: Instructor Materials Chapter 2: Static Routing
CCNA Routing and Switching
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials
Chapter 2: Static Routing

## Slide 2: Instructor Materials – Chapter 2 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 15
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Routing and Switching Essentials 6.0 Planning Guide
Chapter 2: Static Routing
Notes: Routing and Switching Essentials
Chapter 2: Static Routing

## Slide 4: Chapter 2: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
2.0.1.2 | Class Activity | Which Way Should We Go? | Optional
2.1.1.4 | Class Activity | Identify the Advantages and Disadvantages of Static Routing | -
2.1.2.6 | Class Activity | Identify the Type of Static Route | -
2.2.1.3 | Syntax Checker | Configuring Next-hop Static Routes on R2 (Fig.3) | Recommended
2.2.1.3 | Syntax Checker | Configuring Next-Hop Static Routes on R3 (Fig.4) | -
2.2.1.4 | Syntax Checker | Configure Directly Connected Static Routes on R2 (Fig. 3) | Recommended
2.2.1.4 | Syntax Checker | Configure Directly Connected Static Routes on R3 (Fig.4) | -
2.2.1.5 | Syntax Checker | Configure Fully Specified Static Routes on R2 (Fig. 3) | -
2.2.1.5 | Syntax Checker | Configure Fully Specified Static Routes on R3 (Fig.4) | -
Notes: 4

## Slide 5: Chapter 2: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
2.2.1.6 | Syntax Checker | Verify the Static Routing Settings on R2 (Fig. 4) | -
2.2.1.6 | Syntax Checker | Verify the Static Routing Settings on R3 (Fig. 5) | -
2.2.2.4 | Packet Tracer | Configuring IPv4 Static and Default Routes | Recommended
2.2.2.5 | Lab | Lab Configuring IPv4 Static and Default Routes | Optional
2.2.3.1 | Syntax Checker | Enabling IPv6 Unicast Routing on R2 (Fig.3) | -
2.2.3.1 | Syntax Checker | Enabling IPv6 Unicast Routing on R3 (Fig.4) | -
2.2.3.3 | Syntax Checker | Configure Next-Hop Static IPv6 Routes on R2 (Fig.3) | -
2.2.3.3 | Syntax Checker | Configure Next-Hop Static IPv6 Routes on R3 (Fig.4) | -
2.2.3.4 | Syntax Checker | Configure Directly Connected Static IPv6 Routes on R2 (Fig.3) | -
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 2: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
2.2.3.4 | Syntax Checker | Configure Directly Connected Static IPv6 Routes on R3 (Fig.4) | -
2.2.3.5 | Syntax Checker | Configure a Fully Specified Static IPv6 Route on R2 (Fig.3) | -
2.2.4.4 | Packet Tracer | Configuring IPv6 Static and Default Routes | Recommended
2.2.4.5 | Lab | Configuring IPv6 Static and Default Routes | Optional
2.2.5.2 | Syntax Checker | Configure a Floating Static Route on R3 | -
2.2.5.4 | Packet Tracer | Configuring Floating Static Routes | Recommended
2.2.6.2 | Syntax Checker | Configure Host Static Routes (Fig.3) | -
2.3.2.3 | Packet Tracer | Troubleshooting Static Routes | Recommended
2.3.2.4 | Lab | Troubleshooting IPv4 and IPv6 Static Routes | Optional
2.4.1.1 | Class Activity | Make It Static | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 6

## Slide 7: Chapter 2: Assessment
Students should complete Chapter 2, “Assessment” after completing Chapter 2.
Quizzes, labs, Packet Tracers, and other activities can be used to informally assess student progress.
Notes: 7

## Slide 8
Prior to teaching Chapter 2, the instructor should:
Complete Chapter 2, “Assessment.”
The objectives of this chapter are:
  Explain the advantages and disadvantages of static routing.
  Explain the purpose of different types of static routes.
  Configure IPv4 and IPv6 static routes by specifying a next-hop address.
  Configure IPv4 and IPv6 default routes.
  Configure a floating static route to provide a backup connection.
  Configure IPv4 and IPv6 static host routes that direct traffic to a specific host.
  Explain how a router processes packets when a static route is configured.
  Troubleshoot common static and default route configuration issues.
Chapter 2: Best Practices
Notes: 8

## Slide 9
Chapter 2: Best Practices (Cont.)
Section 2.1
Routers learn about remote networks dynamically using routing protocols, or manually using static routes. In many cases, routers use a combination of both dynamic routing protocols and static routes. This chapter focuses on static routing.
Static routes do not require the same amount of processing and overhead as dynamic routing protocols.
Discuss the advantages and disadvantages of static routing.
Point out where are and how static routes are used
  Easy to maintain routing table in small networks that are not expected to grow.
  Routing to and from stub networks.
  Using a single default route to represent a path to any network that does not have a more specific match with another route in the routing table. Default routes are used to send traffic to any destination beyond the next upstream router.
  Stress the advantages of static routing. It is easy for students to discount static routing in favor of dynamic.
Notes: 9

## Slide 10
Chapter 2: Best Practices (Cont.)
Section 2.1(cont.)
Highlight the types of IPv4 and IPv6 static routes that will be examined in the chapter:
  Standard static route
  Default static route
  Floating static route
Section 2.2
Set up in Packet Tracer the sample topology that is used in the curriculum. Share with the students so that they can do the static route configurations “hands-on” as you demonstrate.
Clarify the meaning of the terms next-hop and exit interface.
Discuss the use of default routes and ask students to explain how default routes would be incorporated in their institution’s network?
Notes: 10

## Slide 11
Chapter 2: Best Practices (Cont.)
Section 2.2
Encourage students to use the Syntax Checker activities to practice the new commands.
Explain the necessity for using a fully specified static route which includes both the exit interface and the next-hop address. (Necessary with older IOS not using CEF)
Demonstrate how to verify static routes using:
  show ip route
  show ip route static
  show ip route network
  show ipv6 route
  show ipv6 route static
  show ipv6 route network
Notes: 11

## Slide 12
Chapter 2: Best Practices (Cont.)
Section 2.2 (cont.)
Discuss the use of Floating Static Routes as backup routes.
Explain that the Cisco IOS automatically installs a local host route when an interface address is configured on the router. Indicated with an “L”. Show this as it happens using Packet Tracer.
Have students examine routing table output and identify the Static, Default and Local Host routes.
Section 2.3
Demonstrate methodical troubleshooting of static routes using ping, traceroute, show ip route, show ip interface brief and show cdp neighbors detail.
Provide students with as many opportunities as possible to hone their troubleshooting skills.
Notes: 12

## Slide 13: Chapter 2: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna-blog
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Packet Tracer Know How 1: Packet Tracer 101 (self-enroll)
Notes: 13

## Slide 15: Chapter 2: Static Routing
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 2: Static Routing

## Slide 16: Chapter 2 - Sections & Objectives
2.1 Static Routing Implementation
  Explain the advantages and disadvantages of static routing.
  Explain the purpose of different types of static routes.
2.2 Configure Static and Default Routes
  Configure IPv4 and IPv6 static routes by specifying a next-hop address.
  Configure IPv4 and IPv6 default routes.
  Configure a floating static route to provide a backup connection.
  Configure IPv4 and IPv6 static host routes that direct traffic to a specific host
2.3 Troubleshoot Static and Default Route Issues
  Explain how a router processes packets when a static route is configured.
  Troubleshoot common static and default route configuration issues.
Notes: 16

## Slide 17: 2.1 Static Routing Implementation
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 2: Static Routing

## Slide 18: Static Routing Reach Remote Networks
A router can learn about remote networks in one of two ways:
Manually - Remote networks are manually entered into the route table using static routes.
Dynamically - Remote routes are automatically learned using a dynamic routing protocol.
Notes: 2.1 – Static Routing
2.1.1.1 – Reach Remote Networks

## Slide 19: Static Routing Why Use Static Routing?
Static routing provides some advantages over dynamic routing, including:
Static routes are not advertised over the network, resulting in better security.
Static routes use less bandwidth than dynamic routing protocols, no CPU cycles are used to calculate and communicate routes.
The path a static route uses to send data is known.
Notes: 2.1.1.2 – Why Use Static Routing?

## Slide 20: Static Routing When to Use Static Routes
Static routing has three primary uses:
Providing ease of routing table maintenance in smaller networks.
Routing to and from stub networks. A stub network is a network accessed by a single route, and the router has no other neighbors.
Using a single default route to represent a path to any network that does not have a more specific match with another route in the routing table.
Notes: 2.1.1.3 – When to Use Static Routes

## Slide 21: Types of Static Routes Static Route Applications
Static Routes are often used to:
Connect to a specific network.
Provide a Gateway of Last Resort for a stub network.
Reduce the number of routes advertised by summarizing several contiguous networks as one static route.
Create a backup route in case a primary route link fails.
Notes: 2.1.2 - Types of Static Routes
2.1.2.1 – Static Route Applications

## Slide 22: Types of Static Routes Standard Static Route
Notes: 2.1.2.2 Standard Static Route

## Slide 23: Types of Static Routes Default Static Route
A default static route is a route that matches all packets.
A default route identifies the gateway IP address to which the router sends all IP packets that it does not have a learned or static route.
A default static route is simply a static route with 0.0.0.0/0 as the destination IPv4 address.
Notes: 2.1.2.3 Default Static Route

## Slide 24: Types of Static Routes Summary Static Route
Notes: 2.1.2.4 Summary Static Route

## Slide 25: Types of Static Routes Floating Static Route
Notes: 2.1.2.5 Floating Static Route

## Slide 26: 6.2 Configure Static and Default Routes
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 2: Static Routing

## Slide 27: Configure IPv4 Static Routes ip route Command
Notes: 2.2 Configure Static and Default Routes
2.2.1.1 ip route Command

## Slide 28: Configure IPv4 Static Routes Next-Hop Options
The next hop can be identified by an IP address, exit interface, or both. How the destination is specified creates one of the three following route types:
Next-hop route - Only the next-hop IP address is specified.
Directly connected static route - Only the router exit interface is specified.
Fully specified static route - The next-hop IP address and exit interface are specified.
Notes: 2.2.1.2 Next-Hop Options

## Slide 29: Configure IPv4 Static Routes Configure a Next-Hop Static Route
Notes: 2.2.1.3 Configure a Next-Hop Static Route

## Slide 30: Configure IPv4 Static Routes Configure Directly Connected Static Route
Notes: 2.2.1.4 Configure a Directly Connected Static Route

## Slide 31: Configure IPv4 Static Routes Configure a Fully Specified Static Route
Notes: 2.2.1.5 Configure a Fully Specified Static Route

## Slide 32: Configure IPv4 Static Routes Verify a Static Route
Notes: 2.2.1.6 Verify a Static Route

## Slide 33: Configure IPv4 Static Routes Default Static Route
Notes: 2.2.2.1 Default Static Route

## Slide 34: Configure IPv4 Static Routes Configure a Default Static Route
Notes: 2.2.2.2 Configure a Default Static Route

## Slide 35: Configure IPv4 Static Routes Verify a Default Static Route
Verify a Default Static Route
Verify a Default Static Route
Notes: 2.2.2.3 Verify a Default Static Route

## Slide 36: Configure IPv6 Static Routes The ipv6 route Command
Verify a Default Static Route
Verify a Default Static Route
Notes: 2.2.3.1 The ipv6 route Command

## Slide 37: Configure IPv6 Static Routes Next-Hop Options
Verify a Default Static Route
Verify a Default Static Route
Next-hop static IPv6 route - Only the next-hop IPv6 address is specified
Directly connected static IPv6 route - Only the router exit interface is specified
Fully specified static IPv6 route - The next-hop IPv6 address and exit interface are specified
Notes: 2.2.3.2 Next-Hop Options

## Slide 38: Configure IPv6 Static Routes Configure a Next-Hop Static IPv6 Route
Verify a Default Static Route
Verify a Default Static Route
Notes: 2.2.3.3 Configure a Next-Hop Static IPv6 Route

## Slide 39: Configure IPv6 Static Routes Directly Connected Static IPv6 Route
Verify a Default Static Route
Verify a Default Static Route
Notes: 2.2.3.4 Configure a Directly Connected Static IPv6 Route

## Slide 40: Configure IPv6 Static Routes Fully Specified Static IPv6 Route
Verify a Default Static Route
Verify a Default Static Route
Notes: 2.2.3.5 Configure a Fully Specified Static IPv6 Route

## Slide 41: Configure IPv6 Static Routes Verify IPv6 Static Routes
Verify a Default Static Route
Verify a Default Static Route
In addition to ping and traceroute, commands to verify static routes include:
show ipv6 route
show ipv6 route static
show ipv6 route network
Notes: 2.2.3.6 Verify IPv6 Static Routes

## Slide 42: Configure IPv6 Default Routes Default Static IPv6 Route
Verify a Default Static Route
Verify a Default Static Route
Notes: 2.2.4.1 Default Static IPv6 Route

## Slide 43: Configure IPv6 Default Routes Configure a Default Static IPv6 Route
Verify a Default Static Route
Verify a Default Static Route
Notes: 2.2.4.2 Configure a Default Static IPv6 Route

## Slide 44: Configure IPv6 Default Routes Verify a Default IPv6 Static Route
Verify a Default Static Route
Verify a Default Static Route
Notes: 2.2.4.3 Verify a Default Static Route

## Slide 45: Configure IPv6 Default Routes Floating Static Routes
Verify a Default Static Route
Verify a Default Static Route
Floating static routes have an administrative distance greater than the administrative distance of another static route or dynamic routes.
The static route “floats” and is not used when the route with the better administrative distance is active.
If the preferred route is lost the floating static route can take over.
Notes: 2.2.5.1 Floating Static Routes

## Slide 46: Configure IPv6 Default Routes Configure an IPv4 Floating Static Route
Verify a Default Static Route
Verify a Default Static Route
Notes: 2.2.5.2 Configure an IPv4 Floating Static Route

## Slide 47: Configure IPv6 Default Routes Test the IPv4 Floating Static Route
Verify a Default Static Route
Verify a Default Static Route
To test a floating static route:
Use the show ip route command to verify that the routing table is using the default static route.
Use the traceroute command to follow the traffic flow out the primary route.
Disconnect the link or shutdown the primary interface(s). In the curriculum example the serial interfaces on R2 are shutdown.
Use a show ip route command to verify that the routing table is using the floating static route.
Use a traceroute command to follow the traffic flow out the backup route.
Notes: 2.2.5.3 Test the IPv4 Floating Static Route

## Slide 48: Configure Static Host Routes Automatically Installed Host Routes
Verify a Default Static Route
Verify a Default Static Route
A host route is an IPv4 address with a 32-bit mask or an IPv6 address with a 128-bit mask.
Automatically installed when an IP address is configured on the router.
The local routes are marked with “L” in the output of the routing table.
Notes: 2.2.6.1 Automatically Installed Host Routes

## Slide 49: Configure Static Host Routes Configure IPv4 and IPv6 Static Host Routes
Verify a Default Static Route
Verify a Default Static Route
Notes: 2.2.6.3 Configure IPv4 and IPv6 Static Host Routes

## Slide 50: Configure Static Host Routes Configure IPv4 and IPv6 Static Host Routes
Verify a Default Static Route
Verify a Default Static Route
Notes: 2.2.6.3 Configure IPv4 and IPv6 Static Host Routes

## Slide 51: 6.2 Troubleshoot Static and Default Route Issues
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 2: Static Routing

## Slide 52: Packet Processing with Static Routes Static Routes and Packet Forwarding
Verify a Default Static Route
Notes: 2.3.1.1 Static Routes and Packet Forwarding

## Slide 53: Troubleshoot IPv4 Static and Default Route Configuration Troubleshoot a Missing Route
Verify a Default Static Route
IOS troubleshooting commands include:
ping
Extended ping enables you to specify the source IP address for the ping packets.
traceroute
show ip route
show ip interface brief
show cdp neighbors detail
Notes: 2.3.2.1 Troubleshoot a Missing Route

## Slide 54: Packet Processing with Static Routes Solve a Connectivity Problem
Verify a Default Static Route
Finding a missing (or misconfigured) route requires using the right tools in a methodical manner.
Use the ping command to confirm the destination can’t be reached.
A traceroute would also reveal the closest router (or hop) that fails to respond as expected. In this case, the router would then send an Internet Control Message Protocol (ICMP) destination unreachable message back to the source.
The next step is to investigate the routing table using the show ip route command. Look for missing or misconfigured routes.
Incorrect static routes are a common cause of routing problems.
Notes: 2.3.2.2 Solve a Connectivity Problem

## Slide 55: 2.4 Chapter Summary
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 2: Static Routing

## Slide 56: Chapter Summary Summary
  Explain the advantages and disadvantages of static routing.
  Explain the purpose of different types of static routes.
  Configure IPv4 and IPv6 static routes by specifying a next-hop address.
  Configure IPv4 and IPv6 default routes.
  Configure a floating static route to provide a backup connection.
  Configure IPv4 and IPv6 static host routes that direct traffic to a specific host.
  Explain how a router processes packets when a static route is configured.
  Troubleshoot common static and default route configuration issues.
Notes: Summary

## Slide 57: Section 2.1 Terms and Commands
static route
administrative distance (AD)
stub network
default route
0.0.0.0/0
default static route
Gateway of Last Resort
more specific match
summary static route
floating static route
Notes: Terms and Commands

## Slide 58: Section 2.2 Terms and Commands
exit-intf
next hop
recursive static route
recursive lookup
directly connected static route
CEF (Cisco Express Forwarding)
FIB (Forwarding Information Base)
fully specified static route
edge router
stub router
quad-zero route
::/0
destination network
Ipv6 route command
Fully specified static IPv6 route
show ipv6 route
show ipv6 route static
show ipv6 route network
IPv4 Static Host Routes
IPv6 Static Host Routes
Notes: Terms and Commands

## Slide 59: Section 2.3 Terms and Commands
Extended ping
Notes: New Terms and Commands