## Slide 1: Modeling Wi-Fi Protected Setup Brute-Force Mitigations Using Markov Chains
Lloyd Jones

## Slide 2: Outline
Introduction
Problem Statement
Background Information
Problem Solving Approach
Results

## Slide 3: Introduction
Wi-Fi Protected Setup (WPS) – technology used for easy connection to wireless devices
  Simpler than remembering long WEP/WPA passphrase
  Push-button and PIN method
Known weaknesses in WPS
Importance

## Slide 4: Problem Statement
Compare brute-force times based on different mitigation mechanisms
Variables to consider:
  PIN verification time
  Overall time limit
  Lockouts/Delays
0 < d < 5 | Access point-imposed delay between PIN attempts (seconds)
L(s/p) 0 < s < 120 3 <= p <= 25 | Lockout (s) in seconds per amount of consecutive incorrect PINs (p)
t > 0 | Time limit for successful attempt (minutes)
A1,2,3…n 1 < n < 11,000 | PIN attempts in numerical order
0 < v < 5 | Access point PIN validation time in seconds
0 < P0 < 1 | Probability of client being in unauthenticated state
0 < P1 < 1 | Probability of brute-forcing first half of PIN
0 < P2 < 1 | Probability of brute-forcing second half of PIN
0 < P < 1 | Overall probability of successful brute-force given d, L(s/p), t, v

## Slide 5: Background Information
WPS Vulnerability discovered by Stefan Viehboch in 2011
Caused by splitting PIN into two halves
  Should be 107 (10,000,000)possible PINs
  Actually 104 + 103 = 11,000
1 | 2 | 3 | 4 | 5 | 6 | 7 | Checksum
First half of PIN |  |  |  | Second half of PIN |  |  | 

## Slide 6: Background Information
Message | Direction | Purpose
M4 | Enrollee -> Registrar | Send first half of PIN
M5 | Registrar-> Enrollee | ACK/NACK for first half of PIN
M6 | Enrollee -> Registrar | Send second half of PIN
M7 | Registrar-> Enrollee | ACK/NACK for second half of PIN
WPS Exchange Structure

## Slide 7: Background Information
Open source tools available to take advantage of this vulnerability
Reaver, Bully, and others
Other tools available to detect if WPS is enabled

## Slide 8: Problem Solving Approach
Model and compare scenarios
  Baseline
  Per PIN delay
  Lockout of s seconds per p PINs
  Combination
Equations Used
P =

## Slide 9: Problem Solving Approach
P =
Markov Chain Representation
States Used:
P0 – unassociated/unauthenticated
P1 – First half of PIN correct
P2 – Second half of PIN correct

## Slide 10: Results
Baseline
  No delays/lockouts
  Verification time: 3 seconds
  Time limit: 5 hours
P =
Overall: 79% chance of success

## Slide 11: Results
5 Second per PIN Delay
  Verification time: 3 seconds
  Time limit: 5 hours
P =
Overall: 22% chance of success

## Slide 12: Results
10 Second per PIN Delay
  Verification time: 3 seconds
  Time limit: 5 hours
P =
Overall: 13% chance of success

## Slide 13: Results
30 Second per 10 PINs Lockout
  Verification time: 3 seconds
  Time limit: 5 hours
P =
Overall: 37.5% chance of success

## Slide 14: Results
60 Second per 5 PINs Lockout
  Verification time: 3 seconds
  Time limit: 5 hours
P =
Overall: 10% chance of success

## Slide 15: Results
60 Second per 5 PINs Lockout with 5 Second per PIN Delay
  Verification time: 3 seconds
  Time limit: 5 hours
P =
Overall: 7% chance of success

## Slide 16: Results

## Slide 17: Results

## Slide 18: Results
Lockout mechanisms are not necessarily better than delay mechanisms, and vice-versa
Neither can protect against an attacker with lots of time on his/her hands
Both are more of a bandage on a gaping wound

## Slide 19: Questions?