## Slide 1: Wireless Networks 5G Technologies
Notes: [List of Acronyms in alphabetic order]
CSI Channel State Information
DL Downlink
DRX Discontinuous Reception
eMBB enhanced Mobile Broadband
FDD Frequency Division Duplex
FR Frequency Range
GEO Geosynchronous Orbit
HAP High-Altitude Platform
HARQ Hybrid Automatic Repeat Request
LEO Low Earth Orbit
LTE-M Long Term Evolution - Machine Type Communication
MIMO Multiple-Input and Multiple-Output
NB-IoT Narrow Band-Internet of Things
NC-JT Noncoherent Joint Transmission
NTN Non-Terrestrial Network
PAPR Peak to Average Power Ratio
QoE Quality of Experience
RAN Radio Access Network
SI Study Item
SR Scheduling Request
TCI Transmission Configuration Indicator
TDD Time Division Duplex
TRP Transmission Reception Point
UE User Equipment
UL Uplink
URLCC Ultra-Reliable Low-Latency Communication
V2X Vehicle-to-Everything
WI Work Item
XR eXtended Reality
3GPP 3rd generation partnership project

## Slide 2: Table of Contents
Why 5G Communications?
Possible Applications using 5G
Network Fundamentals
Before 5G Communications
5G Communications
Security Issues
Assignment 1: Research
Assignment 2: Hands-on
Summary

## Slide 3: Table of Contents
Why 5G Communications?
Possible Applications using 5G
Network Fundamentals
Before 5G Communications
5G Communications
Security Issues
Summary

## Slide 4: Why 5G Communications?

## Slide 5: Why 5G Communications?
eMBB (Enhanced Mobile Broadband)
  Faster Throughput and Bandwidth
URLLC (Ultra-reliable and Low Latency Communication)
  4G is not enough for real-time response.
  Uninterrupted Services
mMTC (massive Machine Type Communication)
  Exponentially Increasing # of Users/Devices
More Flexible Architecture
Intelligent Network
Energy Efficiency
More Secure than 4G
Notes: ITU
https://www.itu.int/en/membership/documents/missions/gva-mission-briefing-5g-28sept2016.pdf
Why 5G communication?
1. ultra-reliable and low latency communications and
2. massive machine-type communications

## Slide 6: 5G Capability Perspectives from the ITU-R IMT-2020 Vision Recommendation
Emerging Trends in 5G/IMT2020, ITU, https://www.itu.int/en/membership/documents/missions/gva-mission-briefing-5g-28sept2016.pdf

## Slide 7: Possible Applications using 5G

## Slide 8: 5G Usage Scenarios (1)
Emerging Trends in 5G/IMT2020, ITU, https://www.itu.int/en/membership/documents/missions/gva-mission-briefing-5g-28sept2016.pdf
Notes: eMBB
mMTC
uRLLC

## Slide 9: 5G Usage Scenarios (2)
European Telecommunications Standards Institute (ESTI), https://www.etsi.org/technologies/5G

## Slide 10: Network Fundamentals

## Slide 11: What is Computer Networks?
A collection of autonomous computers interconnected by a single or multiple technologies
  Interconnected via:
    Copper wire
    Fiber optics
    Microwaves
    Infrared
    Communication satellites, etc.

## Slide 12: What is a protocol?
Communications between computers requires very specific unambiguous rules
A protocol is a set of rules that governs how two or more communicating parties are to interact
  Internet Protocol (IP)
  Transmission Control Protocol (TCP)
  HyperText Transfer Protocol (HTTP)
  Simple Mail Transfer Protocol (SMTP)

## Slide 13: What is a communication network?
The equipment (hardware & software) and facilities that provide the basic communication service
Virtually invisible to the user; Usually represented by a cloud
Equipment
  Routers, servers, switches, multiplexers, hubs, modems, …
Facilities
  Copper wires, coaxial cables, optical fiber
  Ducts, conduits, telephone poles …
How are communication networks designed and operated?

## Slide 14: Communication Network Architecture
Network architecture: the plan that specifies how the network is built and operated
Architecture is driven by the network services
Overall communication process is complex
Network architecture partitions overall communication process into separate functional areas called layers

## Slide 15: OSI Reference Model
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application

## Slide 16: OSI Reference Model & TCP/IP Protocol Stack
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application
Application
Layer
TCP
IP Layer
Network
Interface
Layer
Application
UDP
OSI 7 Layers
TCP/IP Protocol

## Slide 17: Headers & Trailers
Application
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application
Application
APP DATA
AH
APP DATA
TH
AH
APP DATA
NH
TH
AH
APP DATA
DH
NH
TH
AH
APP DATA
CRC
bits

## Slide 18: Layers, Services & Protocols
n+1
entity
n-SAP
n+1
entity
n-SAP
n entity
n entity
n-SDU
n-SDU
n-SDU
H
H
n-SDU
n-PDU

## Slide 19: Connectionless & Connection-Oriented Services
Connection-Oriented
  Three-phases:
    Connection setup between two SAPs to initialize state information
    SDU transfer
    Connection release
  e.g. TCP, ATM
Connectionless
  Immediate SDU transfer
  No connection setup
  e.g. UDP, IP

## Slide 20: Segmentation & Reassembly
n-PDU
n-SDU
n-PDU
n-PDU
Reassembly
n-SDU
n-PDU
n-PDU
n-PDU
Segmentation

## Slide 21: Multiplexing
n+1
entity
n+1
entity
n+1
entity
n+1
entity
n entity
n entity
n-SDU
n-SDU
n-SDU
H
H
n-SDU
n-PDU

## Slide 22: Multiplexing
FDM (Frequency Division Multiplexing)
TDM (Time Division Multiplexing)

## Slide 23: Before 5G Communications

## Slide 24: Before 5G Communications
1G
1979~
4G
2009~
5G
2019~
2G
1991~
3G
2001~
Image Source: https://www.cengn.ca/information-centre/innovation/timeline-from-1g-to-5g-a-brief-history-on-cell-phones/
Notes: https://commsbrief.com/what-do-the-terms-1g-2g-3g-4g-and-5g-really-mean/#:~:text=1G%2C%202G%2C%203G%2C%204G%20and%205G%20are%20the%20five,Stands%20for
Timeline & History of 1g, 2g, 3g, 4g, and 5g
https://www.cengn.ca/information-centre/innovation/timeline-from-1g-to-5g-a-brief-history-on-cell-phones/

## Slide 25: Before 5G Communications
Adnan Ghayas, “What do the terms 1G, 2G, 3G, 4G and 5G really mean?,” COMMSBRIEF, March 3, 2020
https://commsbrief.com/what-do-the-terms-1g-2g-3g-4g-and-5g-really-mean/#:~:text=1G%2C%202G%2C%203G%2C%204G%20and%205G%20are%20the%20five,Stands%20for
Notes: https://commsbrief.com/what-do-the-terms-1g-2g-3g-4g-and-5g-really-mean/#:~:text=1G%2C%202G%2C%203G%2C%204G%20and%205G%20are%20the%20five,Stands%20for

## Slide 26: 5G Communications

## Slide 27: 5G Standard and Specification
International Telecommunication Union (ITU)
Overall Concepts
The 3rd Generation Partnership (3GPP)
Specifications
https://www.5gtechnologyworld.com/5g-radios-increase-emphasis-on-compliance-testing/
2G | Phases 1, 2, 2+, Releases 97, 98
3G | Releases 99, Release 4, 5, 6, 7
4G | Releases 8, 9, 10, 11, 12, 13, 14
5G | Releases 15, 16, 17, 18, 19

## Slide 28: 5G Capability Perspectives from the ITU-R IMT-2020 Vision Recommendation
Emerging Trends in 5G/IMT2020, ITU, https://www.itu.int/en/membership/documents/missions/gva-mission-briefing-5g-28sept2016.pdf

## Slide 29: Reference

## Slide 30: 5G Network Architecture
Notes: UMTS: Universal Mobile Telecommunications Service
eNodeB: evolved Node Base-station
DU: Distributed Unit
CU: Central Unit

## Slide 31: 5G NR (New Radio) Architecture
Notes: RAN: Radio Access Network
RF
PHY
MAC
RLC: Radio Link Control
SDAP
RRC

## Slide 32
Analog to Digital / Digital to Analog
Modulation, Coding and Rate Matching
Scheduling, HARQ (Hybrid Automatic Repeat Request), Multiplexing/Demultiplexing
ARQ, Segmentation
Radio
Unit
Distributed
Unit
Central
Unit
Robust Header Compression (RoHC), Security
QoS Flow Handling
Public Land Mobile Network (PLMN) ID selection, SIB, Mobility, 5GC Connect
Notes: SIB: System Information Block
https://www.techplayon.com/5g-nr-system-information-type1-sib-1/

## Slide 33
“5G NR Layer 2 – Packet Data Convergence Protocol (PDCP) Overview,” January 5, 2022,
https://www.techplayon.com/5g-nr-layer-2-packet-data-convergence-protocol-pdcp-overview/
Notes: https://en.wikipedia.org/wiki/Non-access_stratum
Non-access stratum (NAS) is a functional layer in the NR, LTE, UMTS and GSM wireless telecom protocol stacks between the core network and user equipment. This layer is used to manage the establishment of communication sessions and for maintaining continuous communications with the user equipment as it moves. The NAS is defined in contrast to the Access Stratum which is responsible for carrying information over the wireless portion of the network.

## Slide 34: Reference: 5G Core Note 7
Notes: Note 7
다시 공부해서 꼭 필요한 부분만 설명해주기
Network Slide가 뭔지 설명해주기

## Slide 35: 5G Core Architecture

## Slide 36: Frequency Bands & SUL Coverage
Hua Shou, “New Features in the Next Release of 5G New Radio,”
https://ofinno.com/wp-content/uploads/2020/08/OFNO_White_Sheet_082120.pdf
SUL (supplementary Uplink) Coverage
Frequency Bands
Notes: Numerology: Numerology in 5G/NR refers to Sub Carrier Spacing (SCS).
What is the advantage of numerology in 5G?
It allows the 5G base station (known as the gNB) to allocate radio resources in a more flexible way. As a first step, the sub-carrier spacing can be increased from 15 to 30 kHz. To put it very simply, that means that we double the resources in the frequency domain.
What is numerology 0 in 5G?
In 5G NR, subcarrier spacing of 15, 30, 60, 120 and 240 KHz are supported. As you see here, each numerology is labled as a parameter (u, mu in Greek). The numerology (u = 0) represents subcarrier spacing of 15 kHz which is same as LTE.

## Slide 37
https://www.exfo.com/es/recursos/blog/rf-5g-new-radio-top-5-questions/

## Slide 38: Numerology: Subcarrier Spacing (SPS)
Supported Transmission Numerology
5G NR frame structure with multiple numerology parameters
Notes: https://info-nrlte.com/2020/04/25/introduction-to-numerology/
Numerology corresponds to one subcarrier spacing in the frequency domain. NR supports a flexible numerology with a range of subcarrier spacings, based on scaling a baseline subcarrier spacing of 15 kHz. By scaling a reference subcarrier spacing by an integer N, different numerologies can be defined.
Numerology: Numerology in 5G/NR refers to Sub Carrier Spacing (SCS).
What is the advantage of numerology in 5G?
It allows the 5G base station (known as the gNB) to allocate radio resources in a more flexible way. As a first step, the sub-carrier spacing can be increased from 15 to 30 kHz. To put it very simply, that means that we double the resources in the frequency domain.
What is numerology 0 in 5G?
In 5G NR, subcarrier spacing of 15, 30, 60, 120 and 240 KHz are supported. As you see here, each numerology is labled as a parameter (u, mu in Greek). The numerology (u = 0) represents subcarrier spacing of 15 kHz which is same as LTE.

## Slide 39
Jose Luis Carcel, Belkacem Mouhouche, Manuel Fuentes, and Edurado Garro, “IMT-2020 Key Performance Indicators: Evaluation and Extension Towards 5G New Radio Point-to-Multipoint,”
IEEE International Symposium on Broadband Multimedia Systems and Broadcasting, 2019, DOI:10.1109/BMSB47279.2019.8971948

## Slide 40: OFDMA (Orthogonal Frequency Division Multiple Access)
Combined time/frequency domain view of OFDM signal. (Image: Keysight Technologies)
https://www.5gtechnologyworld.com/the-basics-of-5gs-modulation-ofdm/

## Slide 41: Modulation
Houman Sadeghi Kaji, “Understanding 5G, A Practical Guide to Deploying and Operating 5G Networks, 5G New Radio,”Sept 1, 2021
https://www.linkedin.com/pulse/understanding-5g-practical-guide-deploying-operating-new-houman

## Slide 42: Duplex Schemes
TDD
  Uplink and downlink transmission use the same carrier frequency and are separated in different time slices
FDD
  Uplink and downlink transmission use the different frequencies simultaneously

## Slide 43: Network Slicing
https://www.3gpp.org/news-events/3gpp-news/sys-architecture

## Slide 44: Deployment Options: Standalone vs. Non-Standalone
https://www.3gpp.org/news-events/3gpp-news/sys-architecture
- - - Control Plane
___ User Plane

## Slide 45: Antenna: MIMO (Multiple Input Multiple Output)
Spatial Diversity: Improve Coverage
Spatial Multiplexing: Higher Data Rate (Spectral Efficiency)
=> mMIMO (massive MIMO)
  Standard MIMO usually uses 2 or 4 antennas.
  mMIMO uses as many as 96 to 128 antennas.
Tx arrays | Rx arrays | MIMO
2 | 2 | 2*2
4 | 2 | 4*2
2 | 4 | 2*4
4 | 4 | 4*4
8 | 8 | 8*8

## Slide 46: Beaming
Spatial Multiplexing - MIMO

## Slide 47: Beamforming and Coverage

## Slide 48: 5G Security Issues
[References] https://en.wikipedia.org/wiki/5G

## Slide 49
The attack surface is getting bigger
  IoT devices, enabled by 5G technology, from 7 billion in 2018 to 21.5 billion by 2025:
    (ex) the capacity for DDoS attacks, cryptojacking, and other cyberattacks
  "immature and insufficiently tested," and "enables the movement and access of vastly higher quantities of data, and thus broadens attack surfaces“
Fears of potential espionage of users of foreign equipment vendors
Electromagnetic Interference
Reference: "A Formal Analysis of 5G Authentication,“ ETH Zurich, the University of Lorraine and the University of Dundee, October 18, 2018
Notes: https://en.wikipedia.org/wiki/5G
Health:
According to the New York Times, one origin of the 5G health controversy was an erroneous unpublished study that physicist Bill P. Curry did for the Broward County School Board in 2000 which indicated that the absorption of external microwaves by brain tissue increased with frequency.[136]
According to experts this was wrong, the millimeter waves used in 5G are safer than lower frequency microwaves because they cannot penetrate the skin and reach internal organs.

## Slide 50
"The Clean Network"
  Launched in August, 2020
    the U.S. State Department launched "The Clean Network" as a U.S. government-led, bi-partisan effort to address:
      "the long-term threat to data privacy, security, human rights and principled collaboration posed to the free world from authoritarian malign actors".
  More than 60 nations had publicly committed by December 2020
    The United States announced that:
      more than 60 nations, representing more than two thirds of the world's gross domestic product,
      and 200 telecom companies
    This alliance of democracies included:
      27 of the 30 NATO members; 26 of the 27 EU members, 31 of the 37 OECD nations, 11 of the 12 Three Seas nations as well as South Korea, Japan, Israel, Australia, Singapore, Taiwan, Canada, Vietnam, and India.
Notes: "The Clean Network"
  In August, 2020, the U.S. State Department launched "The Clean Network" as a U.S. government-led, bi-partisan effort to address what it described as "the long-term threat to data privacy, security, human rights and principled collaboration posed to the free world from authoritarian malign actors".
  In December 2020, the United States announced that more than 60 nations, representing more than two thirds of the world's gross domestic product, and 200 telecom companies, had publicly committed to the principles of The Clean Network. This alliance of democracies included 27 of the 30 NATO members; 26 of the 27 EU members, 31 of the 37 OECD nations, 11 of the 12 Three Seas nations as well as Japan, Israel, Australia, Singapore, Taiwan, Canada, Vietnam, and India.

## Slide 51: Assignments

## Slide 52: Assignment 1: Research
Write a one-page summary on possible applications using 5G technologies, the topics might include, but not limited, to the following:
Emerging Trends in 5G/IMT2020, ITU, https://www.itu.int/en/membership/documents/missions/gva-mission-briefing-5g-28sept2016.pdf

## Slide 53: Assignment 2: Hands-on Activity
Guide to get started
Build a network router
  You will receive a Raspberry PI 4 Kit in May.
  A hands-on activity will be posted in D2L.
  Extra zoom session in June or July: Only For those who need to work on the activity.

## Slide 54: Summary & Wrap-up

## Slide 55: Summary
Why 5G Communications?
Possible Applications using 5G
Network Fundamentals
Before 5G Communications
5G Communications
Security Issues
Assignment 1: Research
Assignment 2: Hands-on
Summary

## Slide 56: Summary
Why 5G Communications?
Possible Applications using 5G
Network Fundamentals
Before 5G Communications
5G Communications
Security Issues
Summary