## Slide 1: Lecture 1 Overview of Communication Networks and Services

## Slide 2: What is Computer Networks?
A collection of autonomous computers interconnected by a single or multiple technologies
  Interconnected via:
    Copper wire
    Fiber optics
    Microwaves
    Infrared
    Communication satellites, etc.

## Slide 3: Services & Applications
Service: Basic information transfer capability
  Internet transfer of individual block of information
  Internet reliable transfer of a stream of bytes
  Real-time transfer of a voice signal
Applications build on communication services
  E-mail & web build on reliable stream service
  Fax and modems build on basic telephone service
New applications build on multiple networks
  SMS builds on Internet reliable stream service and cellular telephone text messaging

## Slide 4: What is a protocol?
Communications between computers requires very specific unambiguous rules
A protocol is a set of rules that governs how two or more communicating parties are to interact
  Internet Protocol (IP)
  Transmission Control Protocol (TCP)
  HyperText Transfer Protocol (HTTP)
  Simple Mail Transfer Protocol (SMTP)

## Slide 5: What is a communication network?
The equipment (hardware & software) and facilities that provide the basic communication service
Virtually invisible to the user; Usually represented by a cloud
Equipment
  Routers, servers, switches, multiplexers, hubs, modems, …
Facilities
  Copper wires, coaxial cables, optical fiber
  Ducts, conduits, telephone poles …
How are communication networks designed and operated?

## Slide 6: OSI Reference Model
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application

## Slide 7: OSI Reference Model & TCP/IP Protocol Stack
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application
Application
Layer
TCP
IP Layer
Network
Interface
Layer
Application
UDP
OSI 7 Layers
TCP/IP Protocol

## Slide 8: Communication Network Architecture
Network architecture: the plan that specifies how the network is built and operated
Architecture is driven by the network services
Overall communication process is complex
Network architecture partitions overall communication process into separate functional areas called layers
Next we will trace evolution of three network architectures: telegraph, telephone, and computer networks

## Slide 9: Network Architecture Evolution
Telegraph Networks
  Message switching & digital transmission
Telephone Networks
  Circuit Switching
  Analog transmission → digital transmission
  Mobile communications
Internet
  Packet switching & computer applications
Next-Generation Internet
  Multiservice packet switching network

## Slide 10: Network Architecture Evolution
Telegraph
networks
Telephone
networks
Internet, Optical
& Wireless
networks
Information transfer
per second (bits/second)
Next
Generation
Internet
?
[Source] https://www.statista.com/statistics/616210/average-internet-connection-speed-in-the-us/
    https://ourworldindata.org/internet

## Slide 11: Brief History of the Internet
[Source] https://www.dugcampbell.com/history-of-the-internet/

## Slide 12: Brief History of the Internet

## Slide 13: Brief History of the Internet

## Slide 14: Brief History of the Internet

## Slide 15: Wireless Communication Landscape
[Source] https://gblogs.cisco.com/uki/wireless-wireless-everywhere/
[Source] https://www.controlglobal.com/articles/2013/verhappen-wireless/

## Slide 16: 5G Network
[Source] https://www.qualcomm.com/invention/5g/what-is-5g#:~:text=A%3A%205G%20is%20the%205th,machines%2C%20objects%2C%20and%20devices.
[Source] https://engtechmag.files.wordpress.co/2018/09/gn38319c_en.jpg

## Slide 17: 5G Network
[Source] https://link.springer.com/chapter/10.1007/978-1-4842-2896-8_5 (August 14, 2019)

## Slide 18: Classification of interconnected processors by scale.

## Slide 19: Metric Units
The principal metric prefixes.

## Slide 20: Ethernet Local Area Network
In 1980s, affordable workstations available
Need for low-cost, high-speed networks
  To interconnect local workstations
  To access local shared resources (printers, storage, servers)
Low cost, high-speed communications with low error rate possible using coaxial cable
Ethernet is the standard for high-speed wired access to computer networks

## Slide 21: Ethernet Medium Access Control
Network interface card (NIC) connects workstation to LAN
Each NIC has globally unique address
Frames are broadcast into coaxial cable
NICs listen to medium for frames with their address
Transmitting NICs listen for collisions with other stations, and abort and reschedule retransmissions
Transceivers

## Slide 22: The Internet
Different network types emerged for data transfer between computers
Each network has its protocols and is possibly built on different technologies
Internetworking protocols required to enable communications between computers attached to different networks
Internet: a network of networks

## Slide 23: Internet Protocol (IP)
Routers (gateways) interconnect different networks
Host computers prepare IP packets and transmit them over their attached network
Routers forward IP packets across networks
Best-effort IP transfer service, no retransmission
Net 1
Net 2
Router

## Slide 24: Names and IP Addresses
Routing is done based on 32-bit IP addresses
Dotted-decimal notation
  128.100.11.1
Hosts are also identified by name
  Easier to remember
  Hierarchical name structure
  tesla.comm.utoronto.edu
Domain Name System (DNS) provided conversion between names and addresses

## Slide 25: Internet Applications
All Internet applications run on TCP or UDP
TCP: HTTP (web); SMTP (e-mail); FTP (file transfer; telnet (remote terminal)
UDP: DNS, RTP (voice & multimedia)
TCP & UDP incorporated into computer operating systems
Any application designed to operate over TCP or UDP will run over the Internet!!!

## Slide 26: Standards
New technologies very costly and risky
Standards allow players to share risk and benefits of a new market
  Reduced cost of entry
  Interoperability and network effect
  Compete on innovation
  Completing the value chain
    Chips, systems, equipment vendors, service providers
Example
  802.11 wireless LAN products

## Slide 27: Standards Bodies
Internet Engineering Task Force
  Internet standards development
  Request for Comments (RFCs): www.ietf.org
International Telecommunications Union
  International telecom standards
IEEE 802 Committee
  Local area and metropolitan area network standards
  https://en.wikipedia.org/wiki/IEEE_802 (As of February 2019)
Industry Organizations
  MPLS Forum, WiFi Alliance, World Wide Web Consortium