## Slide 1: Lecture 2 Applications and Layered Architecture
Protocols, Services & Layering
OSI Reference Model
TCP/IP Architecture
How the Layers Work Together
Berkeley Sockets

## Slide 2: Lecture 2 Applications and Layered Architecture
Protocols, Services & Layering
OSI Reference Model
TCP/IP Architecture
How the Layers Work Together

## Slide 3: Lecture 2 Applications and Layered Architecture
Protocols, Services & Layering

## Slide 4: Layers, Services & Protocols
The overall communications process between two or more machines connected across one or more networks is very complex
Layering partitions related communications functions into groups that are manageable
Each layer provides a service to the layer above
Each layer operates according to a protocol

## Slide 5: Web Browsing Application
World Wide Web allows users to access resources (i.e. documents) located in computers connected to the Internet
Documents are prepared using HyperText Markup Language (HTML)
A browser application program is used to access the web
The browser displays HTML documents that include links to other documents
Each link references a Uniform Resource Locator (URL) that gives the name of the machine and the location of the given document
Let’s see what happens when a user clicks on a link

## Slide 6: 1. DNS
User clicks on http://www.nytimes.com/
URL contains Internet name of machine (www.nytimes.com), but not Internet address
Internet needs Internet address to send information to a machine
Browser software uses Domain Name System (DNS) protocol to send query for Internet address
DNS system responds with Internet address
Q. www.nytimes.com?
A. 64.15.247.200

## Slide 7: 2. TCP
Browser software uses HyperText Transfer Protocol (HTTP) to send request for document
HTTP server waits for requests by listening to a well-known port number (80 for HTTP)
HTTP client sends request messages through an “ephemeral port number,” e.g. 1127
HTTP needs a Transmission Control Protocol (TCP) connection between the HTTP client and the HTTP server to transfer messages reliably
TCP Connection Request
From: 128.100.11.13 Port 1127
To: 64.15.247.200 Port 80
ACK, TCP Connection Request
From: 64.15.247.200 Port 80 To:128.100.11.13 Port 1127
ACK

## Slide 8: 3. HTTP
HTTP client sends its request message: “GET …”
HTTP server sends a status response: “200 OK”
HTTP server sends requested file
Browser displays document
Clicking a link sets off a chain of events across the Internet!
Let’s see how protocols & layers come into play…
GET / HTTP/1.1
200 OK
Content

## Slide 9: Example: TCP
TCP is a transport layer protocol
Provides reliable byte stream service between two processes in two computers across the Internet
Sequence numbers keep track of the bytes that have been transmitted and received
Error detection and retransmission used to recover from transmission errors and losses
TCP is connection-oriented: the sender and receiver must first establish an association and set initial sequence numbers before data is transferred
Connection ID is specified uniquely by
(send port #, send IP address, receive port #, receiver IP address)

## Slide 10: Example: HTTP
HTTP is an application layer protocol
Retrieves documents on behalf of a browser application program
HTTP specifies fields in request messages and response messages
  Request types; Response codes
  Content type, options, cookies, …
HTTP specifies actions to be taken upon receipt of certain messages

## Slide 11: HTTP uses service of TCP
HTTP
server
HTTP
client
TCP
Port 80
Port 1127
TCP
Response
GET
TCP
80, 1127
GET
1127, 80
bytes
Response
GET
Response

## Slide 12: Example: UDP
UDP is a transport layer protocol
Provides best-effort datagram service between two processes in two computers across the Internet
Port numbers distinguish various processes in the same machine
UDP is connectionless
Datagram is sent immediately
Quick, simple, but not reliable

## Slide 13: Example: DNS Protocol
DNS protocol is an application layer protocol
DNS is a distributed database that resides in multiple machines in the Internet
DNS protocol allows queries of different types
  Name-to-address or Address-to-name
DNS usually involves short messages and so uses service provided by UDP
Well-known port 53

## Slide 14
Local Name Server: resolve frequently-used names
  University department, ISP
  Contacts Root Name server if it cannot resolve query
Root Name Servers: 13 globally
  Resolves query or refers query to Authoritative Name Server
Authoritative Name Server: last resort
  Every machine must register its address with at least two authoritative name servers
1
2
3
4
5
6
Local
Name
Server
Root
Name
Server
Authoritative
Name
Server

## Slide 15: DNS (More…)
Click here to open the class note on DNS.

## Slide 16: Summary
Layers: related communications functions
  Application Layer: HTTP, DNS
  Transport Layer: TCP, UDP
  Network Layer: IP
Services: a protocol provides a communications service to the layer above
  TCP provides connection-oriented reliable byte transfer service
  UDP provides best-effort datagram service
Each layer builds on services of lower layers
  HTTP builds on top of TCP
  DNS builds on top of UDP
  TCP and UDP build on top of IP

## Slide 17: Lecture 2 Applications and Layered Architecture
Protocols, Services & Layering
OSI Reference Model
TCP/IP Architecture
How the Layers Work Together

## Slide 18: Lecture 2 Applications and Layered Architecture
OSI Reference Model

## Slide 19: Why Layering?
Layering simplifies design, implementation, and testing by partitioning overall communications process into parts
Protocol in each layer can be designed separately from those in other layers
Protocol makes “calls” for services from layer below
Layering provides flexibility for modifying and evolving protocols and services without having to change layers below
Monolithic non-layered architectures are costly, inflexible, and soon obsolete

## Slide 20: Open Systems Interconnection
Network architecture:
  Definition of all the layers
  Design of protocols for every layer
By the 1970s every computer vendor had developed its own proprietary layered network architecture
Problem: computers from different vendors could not be networked together
Open Systems Interconnection (OSI) was an international effort by the International Organization for Standardization (ISO) to enable multivendor computer interconnection

## Slide 21: OSI Reference Model
Describes a seven-layer abstract reference model for a network architecture
Purpose of the reference model was to provide a framework for the development of protocols
OSI also provided a unified view of layers, protocols, and services which is still in use in the development of new protocols
Detailed standards were developed for each layer, but most of these are not in use
TCP/IP protocols preempted deployment of OSI protocols

## Slide 22: 7-Layer OSI Reference Model
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Network
Layer
Application
Application
Data Link
Layer
Physical
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Communicating End Systems
One or More Network Nodes
End-to-End Protocols

## Slide 23: Physical Layer
Transfers bits across link
Definition & specification of the physical aspects of a communications link
  Mechanical: cable, plugs, pins...
  Electrical/optical: modulation, signal strength, voltage levels, bit times, …
  functional/procedural: how to activate, maintain, and deactivate physical links…
Ethernet, DSL, cable modem, telephone modems…
Twisted-pair cable, coaxial cable, optical fiber, radio, infrared, …

## Slide 24: Data Link Layer
Transfers frames across direct connections
Groups bits into frames
Detection of bit errors; Retransmission of frames
Activation, maintenance, & deactivation of data link connections
Medium access control for local area networks
Flow control
Data Link
Layer
Physical
Layer
Data Link
Layer
Physical
Layer
frames
bits

## Slide 25: Network Layer
Transfers packets across multiple links and/or multiple networks
Addressing must scale to large networks
Nodes jointly execute routing algorithm to determine paths across the network
Forwarding transfers packet across a node
Congestion control to deal with traffic surges
Connection setup, maintenance, and teardown when connection-based

## Slide 26: Internetworking
Internetworking between networks using the same protocols is part of network layer and provides transfer of packets across multiple networks
Gateway (including up to presentation layer) can connect networks using difference protocols.
G = gateway H = host
Net 1
Net 5
Net 3
Net 2
H
Net 3
G
H
H
H
G
G
G
G
G
Net 1
Net 2
Net 4
Net 5
     
Ethernet LAN
ATM
Switch
ATM
Switch
ATM
Switch
ATM
Switch
ATM
Network

## Slide 27: Transport Layer
Transfers data end-to-end from process in a machine to process in another machine
Reliable stream transfer or quick-and-simple single-block transfer
Multiplexing
Message segmentation and reassembly
Connection setup, maintenance, and release
Transport
Layer
Network
Layer
Transport
Layer
Network
Layer
Network
Layer
Network
Layer
Communication Network

## Slide 28: Application & Upper Layers
Application Layer: Provides services that are frequently required by applications: DNS, web access, file transfer, email…
Presentation Layer: machine-independent representation of data…
Session Layer: dialog management, recovery from errors, …
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Application
Application
Layer
Transport
Layer
Application
Incorporated into Application Layer

## Slide 29: Application & Upper Layers
Application Layer: Provides services that are frequently required by applications: DNS, web access, file transfer, email…
Presentation Layer: machine-independent representation of data…
Session Layer: dialog management, recovery from errors, …
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Application
Application
Layer
Transport
Layer
Application

## Slide 30: Headers & Trailers
Each protocol uses a header that carries addresses, sequence numbers, flag bits, length indicators, etc…
CRC check bits may be appended for error detection
Application
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application
Application
APP DATA
AH
APP DATA
TH
AH
APP DATA
NH
TH
AH
APP DATA
DH
NH
TH
AH
APP DATA
CRC
bits

## Slide 31: OSI Unified View: Protocols
Layer n in one machine interacts with layer n in another machine to provide a service to layer n +1
The entities comprising the corresponding layers on different machines are called peer processes.
The machines use a set of rules and conventions called the layer-n protocol.
Layer-n peer processes communicate by exchanging Protocol Data Units (PDUs)
n
Entity
n
Entity
Layer n peer protocol
n-PDUs

## Slide 32: OSI Unified View: Services
Communication between peer processes is virtual and actually indirect
Layer n+1 transfers information by invoking the services provided by layer n
Services are available at Service Access Points (SAP’s)
Each layer passes data & control information to the layer below it until the physical layer is reached and transfer occurs
The data passed to the layer below is called a Service Data Unit (SDU)
SDU’s are encapsulated in PDU’s

## Slide 33: Layers, Services & Protocols
n+1
entity
n-SAP
n+1
entity
n-SAP
n entity
n entity
n-SDU
n-SDU
n-SDU
H
H
n-SDU
n-PDU

## Slide 34: Interlayer Interaction
layer
N+1 user
N provider
System A
System B
N provider
N+1 user
Request
Indication
Response
Confirm

## Slide 35: Connectionless & Connection-Oriented Services
Connection-Oriented
  Three-phases:
    Connection setup between two SAPs to initialize state information
    SDU transfer
    Connection release
  E.g. TCP, ATM
Connectionless
  Immediate SDU transfer
  No connection setup
  E.g. UDP, IP
Layered services need not be of same type
  TCP operates over IP
  IP operates over ATM

## Slide 36: Segmentation & Reassembly
n-PDU
A layer may impose a limit on the size of a data block that it can transfer for implementation or other reasons
Thus a layer-n SDU may be too large to be handled as a single unit by layer-(n-1)
Sender side: SDU is segmented into multiple PDUs
Receiver side: SDU is reassembled from sequence of PDUs
n-SDU
n-PDU
n-PDU
n-PDU
Segmentation
(a)
n-SDU
n-PDU
n-PDU
Reassembly
(b)

## Slide 37: Multiplexing
n+1
entity
n+1
entity
n+1
entity
n+1
entity
Sharing of layer n service by multiple layer n+1 users
Multiplexing tag or ID required in each PDU to determine which users an SDU belongs to
n entity
n entity
n-SDU
n-SDU
n-SDU
H
H
n-SDU
n-PDU

## Slide 38: Multiplexing
FDM (Frequency Division Multiplexing)
TDM (Time Division Multiplexing)
WDM (Wavelength Division Multiplexing)

## Slide 39: Summary: 7-Layer OSI Reference Model
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Application
Layer
Presentation
Layer
Session
Layer
Transport
Layer
Network
Layer
Data Link
Layer
Physical
Layer
Network
Layer
Application
Application
Data Link
Layer
Physical
Layer
Network
Layer
Data Link
Layer
Physical
Layer
One or More Network Nodes
End-to-End Protocols

## Slide 40: Lecture 2 Applications and Layered Architecture
Protocols, Services & Layering
OSI Reference Model
TCP/IP Architecture
How the Layers Work Together

## Slide 41: Lecture 2 Applications and Layered Architecture
TCP/IP Architecture
How the Layers Work Together

## Slide 42: Why Internetworking?
To build a “network of networks” or internet
  operating over multiple, coexisting, different network technologies
  providing ubiquitous connectivity through IP packet transfer
  achieving huge economies of scale
G
G
G
G
G
G
H
Net 5
Net 5
H
Net 5
Net 2
H
Net 5
Net 3
H
Net 5
Net 1
Net 5
Net 4

## Slide 43: Why Internetworking?
To provide universal communication services
  independent of underlying network technologies
  providing common interface to user applications
G
G
G
G
G
G
H
Net 5
Net 5
H
Net 5
Net 2
H
Net 5
Net 3
H
Net 5
Net 1
Net 5
Net 4
Reliable Stream Service
User Datagram Service

## Slide 44: Why Internetworking?
To provide distributed applications
  Any application designed to operate based on Internet communication services immediately operates across the entire Internet
  Rapid deployment of new applications
    Email, WWW, Peer-to-peer
  Applications independent of network technology
    New networks can be introduced below
    Old network technologies can be retired

## Slide 45: Internet Protocol Approach
IP packets transfer information across Internet
Host A IP → router→ router…→ router→ Host B IP
IP layer in each router determines next hop (router)
Network interfaces transfer IP packets across networks
Router
Internet
Layer
Network
Interface
Transport
Layer
Internet
Layer
Network
Interface
Transport
Layer
Internet
Layer
Network
Interface
Host A
Host B
Net 5
Net 1
Net 5
Net 2
Net 5
Net 3
Router
Internet
Layer
Network
Interface
Router
Internet
Layer
Network
Interface
Net 5
Net 4

## Slide 46
TCP/IP Protocol Suite
(ICMP, ARP)
Diverse network technologies
Reliable stream service
User
datagram service
Distributed applications
HTTP
SMTP
RTP
TCP
UDP
IP
Network
interface 1
Network
interface 3
Network
interface 2
DNS
Best-effort
connectionless packet transfer

## Slide 47: Internet Names & Addresses
Internet Names
Domain Name
  Unique name
  Independent of physical location
  Facilitate memorization by humans
  Organization under single administrative unit
Host Name
  Name given to host computer
User Name
  Name assigned to user
leongarcia@comm.utoronto.ca
Internet Addresses
Each host has globally unique logical 32 bit IP address
Separate address for each physical connection to a network
Routing decision is done based on destination IP address
IP address has two parts:
  netid and hostid
  netid unique
  netid facilitates routing
Dotted Decimal Notation:
  int1.int2.int3.int4
  (intj = jth octet)
  128.100.10.13
DNS resolves IP name to IP address

## Slide 48: Physical Addresses
LANs (and other networks) assign physical addresses to the physical attachment to the network
The network uses its own address to transfer packets or frames to the appropriate destination
IP address needs to be resolved to physical address at each IP network interface
Example: Ethernet uses 48-bit addresses
  Each Ethernet network interface card (NIC) has globally unique Medium Access Control (MAC) or physical address
  First 24 bits identify NIC manufacturer; second 24 bits are serial number
  00:90:27:96:68:07 12 hex numbers
Intel

## Slide 49: More Information on IP Address and Subnetting
Click here or go to Lecture 2-1 Note for more information on IP addressing and Subnetting

## Slide 50: Example internet
(1,1)
s
(1,2)
w
(2,1)
(1,3) r
(2,2)
PPP
Netid=2
Ethernet
(netid=1)
PC
Server
Router
Workstation
 | netid | hostid | Physical address
server | 1 | 1 | s
workstation | 1 | 2 | w
router | 1 | 3 | r
router | 2 | 1 | -
PC | 2 | 2 | -
*PPP does not use addresses

## Slide 51: Encapsulation
Ethernet header contains:
  source and destination physical addresses
  network protocol type (e.g. IP)
IP header
IP Payload
Ethernet header
FCS
IP header
IP Payload

## Slide 52: IP packet from workstation to server
IP packet has (1,2) IP address for source and (1,1) IP address for destination
IP table at workstation indicates (1,1) connected to same network, so IP packet is encapsulated in Ethernet frame with addresses w and s
Ethernet frame is broadcast by workstation NIC and captured by server NIC
NIC examines protocol type field and then delivers packet to its IP layer
(1,1)
s
(1,2)
w
(2,1)
(1,3) r
(2,2)
PPP
Ethernet
PC
Server
Router
Workstation
(1,2), (1,1)
w, s

## Slide 53: IP packet from server to PC
(1,1)
s
(1,2)
w
(2,1)
(1,3) r
(2,2)
PC
Server
Router
Workstation
IP packet has (1,1) and (2,2) as IP source and destination addresses
IP table at server indicates packet should be sent to router, so IP packet is encapsulated in Ethernet frame with addresses s and r
Ethernet frame is broadcast by server NIC and captured by router NIC
NIC examines protocol type field and then delivers packet to its IP layer
IP layer examines IP packet destination address and determines IP packet should be routed to (2,2)
Router’s table indicates (2,2) is directly connected via PPP link
IP packet is encapsulated in PPP frame and delivered to PC
PPP at PC examines protocol type field and delivers packet to PC IP layer
(1,1), (2,2)
s, r
(1,1), (2,2)

## Slide 54: How the layers work together
Network interface
IP
TCP
HTTP
Network interface
IP
Network interface
IP
TCP
HTTP
Ethernet
PPP
Router
(1,1)
s
(2,1)
(1,3) r
(2,2)
PPP
Ethernet
(a)
(b)
Server
PC
PC
Server
Router
TCP uses node-to-node
Unreliable packet transfer of IP
Server IP address & PC IP address
Internet
HTTP uses process-to-process
Reliable byte stream transfer of
TCP connection:
Server socket: (IP Address, 80)
PC socket (IP Address, Eph. #)

## Slide 55: Encapsulation
TCP Header contains source & destination port numbers
IP Header contains source and destination IP addresses; transport protocol type
Ethernet Header contains source & destination MAC addresses; network protocol type
HTTP Request
TCP header
HTTP Request
IP header
TCP header
HTTP Request
Ethernet header
IP header
TCP header
HTTP Request
FCS

## Slide 56: How the layers work together: Network Analyzer
Wireshark network analyzer captures all frames observed by its Ethernet NIC
Sequence of frames and contents of frame can be examined in detail down to individual bytes
Internet

## Slide 57: Wireshark.org

## Slide 58: Wireshark.org

## Slide 59: Wireshark.org

## Slide 60: Wireshark.org

## Slide 61: Wireshark windows
Top Pane shows frame/packet sequence
Middle Pane shows encapsulation for a given frame
Bottom Pane shows hex & text

## Slide 62: Top pane: frame sequence
DNS Query
TCP Connection Setup
HTTP Request & Response

## Slide 63: Middle pane: Encapsulation
Ethernet Frame
Ethernet Destination and Source Addresses
Protocol Type

## Slide 64: Middle pane: Encapsulation
IP Packet
IP Source and Destination Addresses
Protocol Type
And a lot of other stuff!

## Slide 65: Middle pane: Encapsulation
TCP Segment
Source and Destination Port Numbers
HTTP Request
GET

## Slide 66
Recap: TCP/IP Protocol Suite
(ICMP, ARP)
Diverse network technologies
Transport Layer
HTTP
SMTP
RTP
TCP
UDP
IP
Network
interface 1
Network
interface 3
Network
interface 2
DNS
Internet Layer
Application Layer
Network Interface Layer

## Slide 67: Summary
Encapsulation is key to layering
IP provides for transfer of packets across diverse networks
TCP and UDP provide universal communications services across the Internet
Distributed applications that use TCP and UDP can operate over the entire Internet
Internet names, IP addresses, port numbers, sockets, connections, physical addresses

## Slide 68: Lecture 2 Applications and Layered Architectures
Sockets

## Slide 69: Socket API
A socket is defined by an IP address and a port number
API (Application Programming Interface)
  Provides a standard set of functions that can be called by applications
Berkeley UNIX Sockets API
  Abstraction for applications to send & receive data
  Applications create sockets that “plug into” network
  Applications write/read to/from sockets
  Implemented in the kernel
  Facilitates development of network applications
  Hides details of underlying protocols & mechanisms
Also in Windows, Linux, and other OS’s

## Slide 70: Communications through Socket Interface
Client
Server
descriptor
port number
descriptor
port number
Application references a
socket through a descriptor
Socket bound to a port number
Application 1
Socket
Socket interface
User
Kernel
Application 2
User
Kernel
Underlying communication protocols
Underlying communication protocols
Communications network
Socket
Socket interface

## Slide 71: Stream mode of service
Connection-oriented
First, setup connection between two peer application processes
Then, reliable bidirectional in-sequence transfer of byte stream (boundaries not preserved in transfer)
Multiple write/read between peer processes
Finally, connection release
Uses TCP
Connectionless
Immediate transfer of one block of information (boundaries preserved)
No setup overhead & delay
Destination address with each block
Send/receive to/from multiple peer processes
Best-effort service only
  Possible out-of-order
  Possible loss
Uses UDP

## Slide 72: Client & Server Differences
Server
  Specifies well-known port # when creating socket
  May have multiple IP addresses (net interfaces)
  Waits passively for client requests
Client
  Assigned ephemeral port #
  Initiates communications with server
  Needs to know server’s IP address & port #
    DNS for URL & server well-known port #
  Server learns client’s address & port #