## Slide 1: Lecture 3 Digital Transmission Fundamentals
Line Coding
Error Detection and Correction

## Slide 2: Lecture 3 Digital Transmission Fundamentals
Line Coding

## Slide 3: What is Line Coding?
Mapping of binary information sequence into the digital signal that enters the channel
  Ex. “1” maps to +A square pulse; “0” to –A pulse

## Slide 4: Line coding examples
NRZ-inverted
(differential
encoding)
1
0
1
0
1
1
0
0
1
Unipolar
NRZ
Bipolar
encoding
Manchester
encoding
Differential
Manchester
encoding
Polar NRZ

## Slide 5: Unipolar & Polar Non-Return-to-Zero (NRZ)
Unipolar NRZ
“1” maps to +A pulse
“0” maps to no pulse
High Average Power
Long strings of A or 0
  Poor timing
  Low-frequency content
Simple
Polar NRZ
“1” maps to +A/2 pulse
“0” maps to –A/2 pulse
Better Average Power
Long strings of +A/2 or –A/2
  Poor timing
  Low-frequency content
Simple
1
0
1
0
1
1
0
0
1
Unipolar NRZ
Polar NRZ

## Slide 6: Bipolar Code
Three signal levels: {-A, 0, +A}
“1” maps to +A or –A in alternation
“0” maps to no pulse
String of 1s produces a square wave
  Spectrum centered at T/2
Long string of 0s causes receiver to lose synch
Zero-substitution codes
1
0
1
0
1
1
0
0
1
Bipolar Encoding

## Slide 7: Manchester code
“1” maps into A/2 first T/2, -A/2 last T/2
“0” maps into -A/2 first T/2, A/2 last T/2
Every interval has transition in middle
  Timing recovery easy
  Uses double the minimum bandwidth
Simple to implement
Used in 10-Mbps Ethernet & other LAN standards
1
0
1
0
1
1
0
0
1
Manchester Encoding

## Slide 8: Differential Coding
“1” mapped into transition in signal level
“0” mapped into no transition in signal level
Also used with Manchester coding
NRZ-inverted
(differential
encoding)
1
0
1
0
1
1
0
0
1
Differential
Manchester
encoding

## Slide 9: Lecture 3 Digital Transmission Fundamentals
Line Coding
Error Detection and Correction

## Slide 10: Lecture 3 Digital Transmission Fundamentals
Error Detection and Correction

## Slide 11: Error Control
Digital transmission systems introduce errors
Applications require certain reliability level
  Data applications require error-free transfer
  Voice & video applications tolerate some errors
Error control used when transmission system does not meet application requirement
Error control ensures a data stream is transmitted to a certain level of accuracy despite errors
Two basic approaches:
  Error detection & retransmission (ARQ: Automatic Retransmission Request)
  Forward error correction (FEC)

## Slide 12: Key Idea
All transmitted data blocks (“codewords”) satisfy a pattern
If received block doesn’t satisfy pattern, it is in error
Redundancy: Only a subset of all possible blocks can be codewords
Blindspot: when channel transforms a codeword into another codeword
Channel
Encoder
User
information
Pattern
checking
All inputs to channel
satisfy pattern or condition
Channel
output
Deliver user
information or
set error alarm

## Slide 13: Single Parity Check
Append an overall parity check to k information bits
Info Bits: b1, b2, b3, …, bk
Check Bit: bk+1= b1+ b2+ b3+ …+ bk modulo 2
Codeword: (b1, b2, b3, …, bk,, bk+1)
All codewords have even # of 1s
Receiver checks to see if # of 1s is even
  All error patterns that change an odd # of bits are detectable
  All even-numbered patterns are undetectable
Parity bit used in ASCII code

## Slide 14: Example of Single Parity Code
Information (7 bits): (0, 1, 0, 1, 1, 0, 0)
Parity Bit: b8 = 0 + 1 +0 + 1 +1 + 0 = 1
Codeword (8 bits): (0, 1, 0, 1, 1, 0, 0, 1)
If single error in bit 3 : (0, 1, 1, 1, 1, 0, 0, 1)
  # of 1’s =5, odd
  Error detected
If errors in bits 3 and 5: (0, 1, 1, 1, 0, 0, 0, 1)
  # of 1’s =4, even
  Error not detected

## Slide 15: Two-Dimensional Parity Check
1 0 0 1 0 0
0 1 0 0 0 1
1 0 0 1 0 0
1 1 0 1 1 0
1 0 0 1 1 1
Bottom row consists of check bit for each column
Last column consists of check bits for each row
More parity bits to improve coverage
Arrange information as columns
Add single parity bit to each column
Add a final “parity” column
Used in early error control systems

## Slide 16: Error-detecting capability
1 0 0 1 0 0
0 0 0 1 0 1
1 0 0 1 0 0
1 0 0 0 1 0
1 0 0 1 1 1
1 0 0 1 0 0
0 0 0 0 0 1
1 0 0 1 0 0
1 0 0 1 1 0
1 0 0 1 1 1
1 0 0 1 0 0
0 0 0 1 0 1
1 0 0 1 0 0
1 0 0 1 1 0
1 0 0 1 1 1
1 0 0 1 0 0
0 0 0 0 0 1
1 0 0 1 0 0
1 1 0 1 1 0
1 0 0 1 1 1
Arrows indicate failed check bits
Two errors
One error
Three errors
Four errors (undetectable)
1, 2, or 3 errors can always be detected; Not all patterns >4 errors can be detected

## Slide 17: Other Error Detection Codes
Many applications require very low error rate
Need codes that detect the vast majority of errors
Single parity check codes do not detect enough errors
Two-dimensional codes require too many check bits
The following error detecting codes used in practice:
  CRC Polynomial Codes

## Slide 18: Polynomial Codes
Polynomials instead of vectors for codewords
Polynomial arithmetic instead of check sums
Implemented using shift-register circuits
Also called cyclic redundancy check (CRC) codes
Most data communications standards use polynomial codes for error detection
Polynomial codes also basis for powerful error-correction methods

## Slide 19
Addition:
Multiplication:
Binary vectors map to polynomials
(ik-1 , ik-2 ,…, i2 , i1 , i0)  ik-1xk-1 + ik-2xk-2 + … + i2x2 + i1x + i0
(x7 + x6 + 1) + (x6 + x5) = x7 + x6 + x6 + x5 + 1
= x7 +(1+1)x6 + x5 + 1
= x7 +x5 + 1 since 1+1=0 mod2
(x + 1) (x2 + x + 1) = x(x2 + x + 1) + 1(x2 + x + 1)
= x3 + x2 + x + (x2 + x + 1)
= x3 + 1
Binary Polynomial Division

## Slide 20: Binary Polynomial Division
Division with Decimal Numbers
32
35 ) 1222
3
105
17
2
4
140
divisor
quotient
remainder
dividend
1222 = 34 x 35 + 32
dividend = quotient x divisor +remainder
Polynomial Division
x3 + x + 1 ) x6 + x5
x6 + x4 + x3
x5 + x4 + x3
x5 + x3 + x2
x4 + x2
x4 + x2 + x
x
= q(x) quotient
= r(x) remainder
divisor
dividend
+ x
+ x2
x3
Note: Degree of r(x) is less than degree of divisor

## Slide 21: Polynomial Coding
Code has binary generator polynomial of degree n–k
k information bits define polynomial of degree k – 1
Find remainder polynomial of at most degree n – k – 1
g(x) ) xn-k i(x)
q(x)
r(x)
xn-ki(x) = q(x)g(x) + r(x)
Define the codeword polynomial of degree n – 1
b(x) = xn-ki(x) + r(x)
n bits
k bits
n-k bits
g(x) = xn-k + gn-k-1xn-k-1 + … + g2x2 + g1x + 1
i(x) = ik-1xk-1 + ik-2xk-2 + … + i2x2 + i1x + i0

## Slide 22: Polynomial example: k = 4, n–k = 3
Transmitted codeword:
      b(x) = x6 + x5 + x
      b = (1,1,0,0,0,1,0)
1011 ) 1100000
1110
1011
1110
1011
1010
1011
010
x3 + x + 1 ) x6 + x5
x3 + x2 + x
x6 + x4 + x3
x5 + x4 + x3
x5 + x3 + x2
x4 + x2
x4 + x2 + x
x
Generator polynomial: g(x)= x3 + x + 1
Information: (1,1,0,0) i(x) = x3 + x2
Encoding: x3i(x) = x6 + x5

## Slide 23: The Pattern in Polynomial Coding
All codewords satisfy the following pattern:
All codewords are a multiple of g(x)!
Receiver should divide received n-tuple by g(x) and check if remainder is zero
If remainder is nonzero, then received n-tuple is not a codeword
b(x) = xn-ki(x) + r(x) = q(x)g(x) + r(x) + r(x) = q(x)g(x)

## Slide 24: Standard Generator Polynomials
CRC-8:
CRC-16:
CCITT-16:
CCITT-32:
CRC = cyclic redundancy check
HDLC, XMODEM, V.41
IEEE 802, DoD, V.42
Bisync
ATM
= x8 + x2 + x + 1
= x16 + x15 + x2 + 1
= (x + 1)(x15 + x + 1)
= x16 + x12 + x5 + 1
= x32 + x26 + x23 + x22 + x16 + x12 + x11 + x10 + x8 + x7 + x5 + x4 + x2 + x + 1