## Slide 1: Lecture 2-1 IP Addressing & Subnetting
IP Addressing
Subnetting

## Slide 2: Lecture 2-1 IP Addressing & Subnetting
IP Addressing

## Slide 3: Addressing
Domain names: “radford.edu”
IP Addresses: iii.jjj.kkk.lll, dotted decimal
  Example: Radford University has a computer (somewhere) with IP address 137.45.192.36
MAC (Hardware) Address
  Hexadecimal digits separated by colons or dash.
  Example: 00-06-6B-FF-0A-B4
Specific .vs. Broadcast (FF-FF-FF-FF-FF-FF) Addresses

## Slide 4: IP Addresses
An IP Packet can be sent to
  A single workstation (unicast)
    Efficient for data between pairs of addresses
  A specific list of workstations (multicast)
    Efficient for specific groups, but must specify all individual workstations IP addresses
  All stations on a network (broadcast)
    Efficient for large (unknown) group – use special broadcast IP address.
IP addresses have a special broadcast address
Class .vs. Classless Addressing.
Internet Assigned Numbers Authority (IANA)
Notes: The Internet Assigned Numbers Authority (IANA) manages the IP address space allocations globally and delegates five regional Internet registries (RIRs) to allocate IP address blocks to local Internet registries (Internet service providers) and other entities.

## Slide 5: Special IP Addresses
THIS computer - all 0’s--both prefix and suffix
  0.0.0.0
THIS network broadcast - all 1’s prefix and suffix
  255.255.255.255
remote net broadcast - net prefix all 1’s suffix
  Ex: 137.45.192.255
Network address - net prefix all 0’s suffix
  137.45.192.0
loopback - 127.x.x.x but usually 127.0.0.1
Everything else is a Host IP Address like 137.45.192.96

## Slide 6: IP Address Ranges, Or “Classes”
From: | To: | Description
1.x.x.x | 126.x.x.x | Class A license
127.x.x.x | 127.x.x.x | Loop back
128.x.x.x | 191.x.x.x | Class B license (172.16 thru 31. 0. 0 reserved for private addresses)
192.x.x.x | 223.x.x.x | Class C license (192. 168. x. 0 reserved for private addresses)
224.0.0.0 | 224.0.0.255 | Multicast: Reserved Link Local Addresses
224.0.1.0 | 238.255.255.255 | Multicast: Globally Scoped Addresses
239.0.0.0 | 239.255.255.255 | Multicast: Limited Scope Addresses
240.x.x.x | 255.255.255.254 | Experimental
255.255.255.255 |  | Broadcast

## Slide 7: IP Format
137.45.104.172

## Slide 8: Dotted Decimal vs Binary
137.45.104.172
10001001001011010110100010101100

## Slide 9: Conversion Between Decimal & Binary
128
64
32
16
8
4
2
1
1
0
0
0
1
0
0
1
128
0
0
0
8
0
0
1
137
X
X
X
X
X
X
X
X
=
=
=
=
=
=
=
=

## Slide 10: Conversion Between Decimal & Binary
128
64
32
16
8
4
2
1
1
0
0
0
1
0
0
1
128
0
0
0
8
0
0
1
137
0
0
1
0
1
1
0
1
0
0
32
0
8
4
0
1
45
0
1
1
0
1
0
0
0
0
64
32
0
8
0
0
0
104
1
0
1
0
1
1
0
0
128
0
32
0
8
4
0
0
172

## Slide 11: Lecture 2-1 IP Addressing & Subnetting
IP Addressing
Subnetting

## Slide 12: Lecture 2-1 IP Addressing & Subnetting
Subnetting

## Slide 13: Why Subnets?
In class A, B, or C networks, there are too many IP addresses to fit on one segment.
  Thus, need routers and subnets to isolate parts.

## Slide 14: Subnets: A new interpretation
IP Addresses had a new subnet field inserted between network & local fields
  IP address := <network-number><subnet-number><host-number>
Ex: A Class A Network with 8-bit subnet field
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0| NETWORK | SUBNET | Host number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 15: Class C subnet example
See www.minasi.com -- newsletters, etc.
Look at IP Subnetting Tutorial http://www.ralphb.net/IPSubnet/index.html
New York
Ethernet Sw.
Los Angeles
Ethernet Sw.
PC1
PC6
PC5
PC2
PC7
PC3
PC4
Router
Router
WAN Link
Network address:
192.168.1.128
Mask:
255.255.255.192
Host addresses
192.168.1.129-190
Network address:
192.168.1.64
Mask:
255.255.255.192
Host addresses
192.168.1.65-126

## Slide 16: Sample Question
[Q1] Given: Class C IP Address 196.72.84.0
5 subnets
[Q2] Given: Class B IP Address 132.84.0.0
12 subnets

## Slide 17: Subnet Mask for Class C
137.45.104.172
255.255.255.0

## Slide 18: “Anding” a Binary Subnet Mask
10001001001011010110100010101100
11111111111111111111111100000000
10001001001011010110100000000000
subnet ID = (137.45.104.0)

## Slide 19: Subnet example
192.168.1.0 = Basic Class C Network ID
255.255.255.0 = Class C Mask
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1 1 0| (Sub)NETWORK | Local Addr|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Old Class C
Boundary
Between
Network and Local
New Class C
Subnet Boundary
Between
Network and Local
Must Use 2 extra bits for the
First feasible sub-division of
Class C into two subnets
192.168.1.64, 192.168.1.128 New sub-Network IDs
255.255.255.192 = New Subnet Mask

## Slide 20: SubNetwork IDs, Host Ranges & Broadcast Addresses
Using extra two bits in Network ID
  00 – Can’t use because this is the part of the original Class C’s Network ID
  01 – Available 01000000 = 64
  10 – Available 10000000 = 128
  11 – Can’t use because this is part of the original Class C’s broadcast address
Hence
  192.168.1.64 is the first sub-Network ID
  192.168.1.128 is the second

## Slide 21: Binary for the subnetwork IDs
Byte boundaries shown by dashed lines
Subnet IDs = Local address field of all zeroes (6 bits)
01 or 10 to get bottom byte (8 bits)
Result = 64 or 128 when translated to decimal
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1 1 0| (Sub)NETWORK 0 1|0 0 0 0 0 0|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
192 . 168 . 1 . 64
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1 1 0| (Sub)NETWORK 1 0|0 0 0 0 0 0|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
192 . 168 . 1 . 128

## Slide 22: Binary for Masks (Old .vs. New)
A Mask is a device for indicating how long the (sub)network field is
All 1’s covering the entire network id portion
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1 1 1|1 1 1 1 1 1… OLD NETWORK MASK …1 1 1 1|0 0 0 0 0 0 0 0|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
255 . 255 . 255 . 0
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1 1 1|1 1 1 1 1 1… (Sub)NETWORK MASK …1 1 1 1 1 1|0 0 0 0 0 0|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
255 . 255 . 255 . 192

## Slide 23: Host Ranges
Network Mask is 255.255.255.192
192.168.1.64 has 62 host addresses
  First available host address = 192.168.1.65
  Last available host address = 192.168.1.126
  Broadcast address = 192.168.1.127
192.168.1.128 has 62 host addresses
  First available host address = 192.168.1.129
  Last available host address = 192.168.1.190
  Broadcast address = 192.168.1.191

## Slide 24: Binary for Broadcast addresses
Broadcast addresses have all 1’s in the host field
Remember, we always translate 8 bit octets to decimal!
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1 1 0| (Sub)NETWORK 0 1|1 1 1 1 1 1|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
192 . 168 . 1 . 127
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1 1 0| (Sub)NETWORK 1 0|1 1 1 1 1 1|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
192 . 168 . 1 . 191

## Slide 25: Recap: Network Classes
IANA (Internet Assigned Numbers Authority)
Class A
  IP address := <8bits>.<24bits>
  16 Million hosts in a class A network domain
Class B
  IP address = <16bits>.<16bits>
  65534 hosts in a class B network domain
Class C
  IP address = <24bits>.<8bits>
  256 hosts in a class C network domain
 Waste of Address Range~!

## Slide 26: Note on Classful vs. Classless
Note that, in classful subnetting, we lose quite a few blocks of addresses.
RFC 1519 (Classless Inter-Domain Routing = CIDR) was introduced in 1993 to deal with rapid depletion of IP address space due to “Classful Fragmentation”
Problem:
  Given the entire internet was “classful” in 1993, how to transition to classless methods?
  What exactly is the impact to internet protocols (in all the millions of devices and hosts) of such a change?

## Slide 27: Impact of CIDR
We needed new routing protocols (haven’t introduced those yet)
We need new ways of handling masks
The bottom line is:
  There is a way to use all those un-used addresses (all zeroes, all ones) that we discarded in classful subnetting.
  (Ex) 192.211.1.8 /24

## Slide 28: Routable and Nonroutable Addresses
Nonroutable Address [RFC 1918]
  Internet Router ignore the following addresses.
    10.0.0.0 – 10.255.255.255
    172.16.0.0 – 172.31.255.255
    192.168.0.0 – 192.168.255.255
  Millions of networks can exist with the same nonroutable address.
  “Intranet” : Internal Internet
  NAT (Network Address Translation) router
  Side benefit : “Security”

## Slide 29: VLSM (Variable Length Subnet Masking)
Can support variable length of subnet id in a single domain
How?
  Decide the necessary number of bits for a host id first
  Then, get the number of bits for a subnet id

## Slide 30: VLSM: Sample Question
[Given] IP Addr 192.3.4.0/24
  AtlantaHQ: 58 hosts
  PerthHQ: 26 hosts
  SydneyHQ: 10 hosts
  CorpusHQ:10 hosts
  WAN1: 2 IP addresses
  WAN2: 2 IP addresses
  WAN3: 2 IP addresses
Give a subnet address, an address range, a broadcast address, and a network prefix
Reference: Cisco Network Fundamental course

## Slide 31: H/W (e.g., Ethernet) Addresses
A Hardware (H/W) address of all 1’s signifies the broadcast address at the link layer of Ethernet
Ethernet NICs can also be configured (through software) with several Multicast addresses
All Ethernet NICs will accept a packet with either
  Individual HW address of NIC
  The broadcast address
  Any of the configured multicast addresses
Finally, Ethernet NICs can be put into promiscuous mode –
  Accept all packets regardless of H/W address
  Useful for monitoring, “sniffing”, debugging

## Slide 32: Useful commands (Win2K)
nbtstat - displays protocol information of NetBIOS over TCP/IP.
hostname - displays the domain name of a system
arp -a - displays the current ARP cache (physical address to IP address mappings)
nbtstat -c - displays the IP address to domain name mappings
tracert - used to discover the path taken to reach a destination
ipconfig - used to display current TCP/IP network configuration parameter values, (ipconfig –all)
netstat - displays protocol statistics and current TCP/IP connections