## Slide 1: Lecture 4 Routing
Routing in Packet Networks
Shortest Path Routing

## Slide 2: Lecture 2-2 Routing
Routing in Packet Networks

## Slide 3: Network Layer
Network Layer: the most complex layer
  Requires the coordinated actions of multiple, geographically distributed network elements (switches & routers)
  Must be able to deal with very large scales
    Billions of users (people & communicating devices)
  Biggest Challenges
    Addressing: where should information be directed to?
    Routing: what path should be used to get information there?

## Slide 4: Network Layer Functions
Essential
Routing: mechanisms for determining the set of best paths for routing packets requires the collaboration of network elements
Forwarding: transfer of packets from NE inputs to outputs
Priority & Scheduling: determining order of packet transmission in each NE
Optional: congestion control, segmentation & reassembly, security

## Slide 5: Routing in Packet Networks
1
2
3
4
5
6
Node
(switch or router)
Three possible (loopfree) routes from 1 to 6:
  1-3-6, 1-4-5-6, 1-2-5-6
Which is “best”?
  Min delay? Min hop? Max bandwidth? Min cost? Max reliability?

## Slide 6: Creating the Routing Tables
Need information on state of links
  Link up/down; congested; delay or other metrics
Need to distribute link state information using a routing protocol
  What information is exchanged? How often?
  Exchange with neighbors; Broadcast or flood
Need to compute routes based on information
  Single metric; multiple metrics
  Single route; alternate routes

## Slide 7: Routing Algorithm Requirements
Responsiveness to changes
  Topology or bandwidth changes, congestion
  Rapid convergence of routers to consistent set of routes
  Freedom from persistent loops
Optimality
  Resource utilization, path length
Robustness
  Continues working under high load, congestion, faults, equipment failures, incorrect implementations
Simplicity
  Efficient software implementation, reasonable processing load

## Slide 8: Classifications of Routing
Centralized vs. Distributed Routing
Static vs. Dynamic Routing
Flat vs. Hierarchical Routing

## Slide 9: Centralized vs Distributed Routing
Centralized Routing
  All routes determined by a central node
  All state information sent to central node
  Problems adapting to frequent topology changes
  Does not scale
Distributed Routing
  Routes determined by routers using distributed algorithm
  State information exchanged by routers
  Adapts to topology and other changes
  Better scalability

## Slide 10: Static vs Dynamic Routing
Static Routing
  Set up manually, do not change; requires administration
  Works when traffic predictable & network is simple
  Used to override some routes set by dynamic algorithm
  Used to provide default router
Dynamic Routing
  Adapt to changes in network conditions
  Automated
  Calculates routes based on received updated network state information

## Slide 11: Routing in Virtual-Circuit Packet Networks
1
2
3
4
5
6
A
B
C
D
1
5
2
3
7
1
8
5
4
2
3
6
5
2
Switch or router
Host
VCI
Route determined during connection setup
Tables in switches implement forwarding that realizes selected route

## Slide 12: Routing Tables in VC Packet Networks
Incoming Outgoing
Node VCI Node VCI
A 1 3 2
A 5 3 3
3 2 A 1
3 3 A 5
Incoming Outgoing
Node VCI Node VCI
1 2 6 7
1 3 4 4
4 2 6 1
6 7 1 2
6 1 4 2
4 4 1 3
Incoming Outgoing
Node VCI Node VCI
3 7 B 8
3 1 B 5
B 5 3 1
B 8 3 7
Incoming Outgoing
Node VCI Node VCI
C 6 4 3
4 3 C 6
Incoming Outgoing
Node VCI Node VCI
2 3 3 2
3 4 5 5
3 2 2 3
5 5 3 4
Incoming Outgoing
Node VCI Node VCI
4 5 D 2
D 2 4 5
Node 1
Node 2
Node 3
Node 4
Node 6
Node 5
Example: VCI from A to D
  From A & VCI 5 → 3 & VCI 3 → 4 & VCI 4
  → 5 & VCI 5 → D & VCI 2

## Slide 13: Routing Tables in Datagram Packet Networks
2 2
3 3
4 4
5 2
6 3
Node 1
Node 2
Node 3
Node 4
Node 6
Node 5
1 1
2 4
4 4
5 6
6 6
1 3
2 5
3 3
4 3
5 5
Destination Next node
1 1
3 1
4 4
5 5
6 5
1 4
2 2
3 4
4 4
6 6
1 1
2 2
3 3
5 5
6 3
Destination Next node
Destination Next node
Destination Next node
Destination Next node
Destination Next node

## Slide 14: Flat vs Hierarchical Routing
Flat Routing
  All routers are peers
  Does not scale
Hierarchical Routing
  Partitioning: Domains, autonomous systems, areas...
  Some routers part of routing backbone
  Some routers only communicate within an area
  Efficient because it matches typical traffic flow patterns
  Scales

## Slide 15: Non-Hierarchical Addresses and Routing
0000 0111 1010 1101
0001 0100 1011 1110
0011 0101 1000 1111
0011 0110 1001 1100
R1
1
2
5
4
3
0000 1 0111 1 1010 1 … …
0001 4 0100 4 1011 4 … …
R2
No relationship between addresses & routing proximity
Routing tables require 16 entries each

## Slide 16: Hierarchical Addresses and Routing
0000 0001 0010 0011
0100 0101 0110 0111
1100 1101 1110 1111
1000 1001 1010 1011
R1
R2
1
2
5
4
3
00 1 01 3 10 2 11 3
00 3 01 4 10 3 11 5
Prefix indicates network where host is attached
Routing tables require 4 entries each

## Slide 17: Specialized Routing
Flooding
  Useful in starting up network
  Useful in propagating information to all nodes

## Slide 18: Flooding (1)
Send a packet to all nodes in a network
No routing tables available
Need to broadcast packet to all nodes (e.g. to propagate link state information)
Approach
Send packet on all ports except one where it arrived
Exponential growth in packet transmissions

## Slide 19
1
2
3
4
5
6
Flooding is initiated from Node 1: Hop 1 transmissions
Flooding (2)

## Slide 20
1
2
3
4
5
6
Flooding is initiated from Node 1: Hop 2 transmissions
Flooding (3)

## Slide 21
1
2
3
4
5
6
Flooding is initiated from Node 1: Hop 3 transmissions
Flooding (4)

## Slide 22: Limited Flooding
Time-to-Live field in each packet limits number of hops to certain diameter
Each switch adds its ID before flooding; discards repeats
Source puts sequence number in each packet; switches records source address and sequence number and discards repeats

## Slide 23: Lecture 2-2 Routing
Routing in Packet Networks
Shortest Path Routing

## Slide 24: Lecture 2-2 Routing
Shortest Path Routing

## Slide 25: Shortest Paths & Routing
Many possible paths connect any given source and to any given destination
Routing involves the selection of the path to be used to accomplish a given transfer
Typically it is possible to attach a cost or distance to a link connecting two nodes
Routing can then be posed as a shortest path problem

## Slide 26: Routing Metrics
Means for measuring desirability of a path
Path Length = sum of costs or distances
Possible metrics
  Hop count: rough measure of resources used
  Reliability: link availability; BER
  Delay: sum of delays along path; complex & dynamic
  Bandwidth: “available capacity” in a path
  Load: Link & router utilization along path
  Cost: $$$

## Slide 27: Shortest Path Approaches
Distance Vector Protocols
Neighbors exchange list of distances to destinations
Best next-hop determined for each destination
Ford-Fulkerson (distributed) shortest path algorithm
Link State Protocols
Link state information flooded to all routers
Routers have complete topology information
Shortest path (& hence next hop) calculated
Dijkstra (centralized) shortest path algorithm

## Slide 28: Distance Vector Do you know the way to San Jose?
San Jose 392
San Jose 596
San Jose 294
San Jose 250

## Slide 29: Distance Vector
Local Signpost
Direction
Distance
Routing Table
For each destination list:
Next Node
Distance
Table Synthesis
Neighbors exchange table entries
Determine current best next hop
Inform neighbors
  Periodically
  After changes
dest
next
dist

## Slide 30: Shortest Path to SJ
i
j
San
Jose
Cij
Dj
Di
If Di is the shortest distance to SJ from i
and if j is a neighbor on the shortest path, then Di = Cij + Dj
Focus on how nodes find their shortest path to a given destination node, i.e. SJ

## Slide 31: But we don’t know the shortest paths
i only has local info
from neighbors
Dj"
Cij”
i
San
Jose
j
Cij
Dj
Di
j"
Cij'
j'
Dj'
Pick current
shortest path

## Slide 32: Why Distance Vector Works
San
Jose
1 Hop
From SJ
2 Hops
From SJ
3 Hops
From SJ
Accurate info about SJ
ripples across network,
Shortest Path Converges
SJ sends
accurate info
Hop-1 nodes
calculate current
(next hop, dist), &
send to neighbors

## Slide 33: Bellman-Ford Algorithm
Consider computations for one destination d
Initialization
  Each node table has 1 row for destination d
  Distance of node d to itself is zero: Dd=0
  Distance of other node j to d is infinite: Dj=, for j d
  Next hop node nj = -1 to indicate not yet defined for j  d
Send Step
  Send new distance vector to immediate neighbors across local link
Receive Step
  At node j, find the next hop that gives the minimum distance to d,
    Minj { Cij + Dj }
    Replace old (nj, Dj(d)) by new (nj*, Dj*(d)) if new next node or distance
  Go to send step

## Slide 34: Bellman-Ford Algorithm
Now consider parallel computations for all destinations d
Initialization
  Each node has 1 row for each destination d
  Distance of node d to itself is zero: Dd(d)=0
  Distance of other node j to d is infinite: Dj(d)=  , for j  d
  Next node nj = -1 since not yet defined
Send Step
  Send new distance vector to immediate neighbors across local link
Receive Step
  For each destination d, find the next hop that gives the minimum distance to d,
    Minj { Cij+ Dj(d) }
    Replace old (nj, Di(d)) by new (nj*, Dj*(d)) if new next node or distance found
  Go to send step

## Slide 35
Iteration | Node 1 | Node 2 | Node 3 | Node 4 | Node 5
Initial | (-1, ) | (-1, ) | (-1, ) | (-1, ) | (-1, )
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
3
1
5
4
6
2
2
3
4
2
1
1
2
3
5
San
Jose
Table entry
@ node 1
for dest SJ
Table entry
@ node 3
for dest SJ

## Slide 36
Iteration | Node 1 | Node 2 | Node 3 | Node 4 | Node 5
Initial | (-1, ) | (-1, ) | (-1, ) | (-1, ) | (-1, )
1 | (-1, ) | (-1, ) | (6,1) | (-1, ) | (6,2)
2 |  |  |  |  | 
3 |  |  |  |  | 
San
Jose
D6=0
D3=D6+1
n3=6
3
1
5
4
6
2
2
3
4
2
1
1
2
3
5
D6=0
D5=D6+2
n5=6
0
2
1

## Slide 37
Iteration | Node 1 | Node 2 | Node 3 | Node 4 | Node 5
Initial | (-1, ) | (-1, ) | (-1, ) | (-1, ) | (-1, )
1 | (-1, ) | (-1, ) | (6, 1) | (-1, ) | (6,2)
2 | (3,3) | (5,6) | (6, 1) | (3,3) | (6,2)
3 |  |  |  |  | 
San
Jose
3
1
5
4
6
2
2
3
4
2
1
1
2
3
5
0
1
2
3
3
6

## Slide 38
Iteration | Node 1 | Node 2 | Node 3 | Node 4 | Node 5
Initial | (-1, ) | (-1, ) | (-1, ) | (-1, ) | (-1, )
1 | (-1, ) | (-1, ) | (6, 1) | (-1, ) | (6,2)
2 | (3,3) | (5,6) | (6, 1) | (3,3) | (6,2)
3 | (3,3) | (4,4) | (6, 1) | (3,3) | (6,2)
San
Jose
3
1
5
4
6
2
2
3
4
2
1
1
2
3
5
0
1
2
6
3
3
4

## Slide 39
Iteration | Node 1 | Node 2 | Node 3 | Node 4 | Node 5
Initial | (3,3) | (4,4) | (6, 1) | (3,3) | (6,2)
1 | (3,3) | (4,4) | (4, 5) | (3,3) | (6,2)
2 |  |  |  |  | 
3 |  |  |  |  | 
San
Jose
3
1
5
4
6
2
2
3
4
2
1
1
2
3
5
0
1
2
3
3
4
Network disconnected; Loop created between nodes 3 and 4
5

## Slide 40
Iteration | Node 1 | Node 2 | Node 3 | Node 4 | Node 5
Initial | (3,3) | (4,4) | (6, 1) | (3,3) | (6,2)
1 | (3,3) | (4,4) | (4, 5) | (3,3) | (6,2)
2 | (3,7) | (4,4) | (4, 5) | (5,5) | (6,2)
3 |  |  |  |  | 
San
Jose
3
1
5
4
6
2
2
3
4
2
1
1
2
3
5
0
2
5
3
3
4
7
5
Node 4 could have chosen 2 as next node because of tie

## Slide 41
Iteration | Node 1 | Node 2 | Node 3 | Node 4 | Node 5
Initial | (3,3) | (4,4) | (6, 1) | (3,3) | (6,2)
1 | (3,3) | (4,4) | (4, 5) | (3,3) | (6,2)
2 | (3,7) | (4,4) | (4, 5) | (5,5) | (6,2)
3 | (3,7) | (4,6) | (4, 7) | (5,5) | (6,2)
San
Jose
3
1
5
4
6
2
2
3
4
2
1
1
2
3
5
0
2
5
5
7
4
7
6
Node 2 could have chosen 5 as next node because of tie

## Slide 42
3
5
4
6
2
2
3
4
2
1
1
2
3
5
1
Iteration | Node 1 | Node 2 | Node 3 | Node 4 | Node 5
1 | (3,3) | (4,4) | (4, 5) | (3,3) | (6,2)
2 | (3,7) | (4,4) | (4, 5) | (2,5) | (6,2)
3 | (3,7) | (4,6) | (4, 7) | (5,5) | (6,2)
4 | (2,9) | (4,6) | (4, 7) | (5,5) | (6,2)
San
Jose
0
7
7
5
6
9
2
Node 1 could have chose 3 as next node because of tie

## Slide 43: Counting to Infinity Problem
3
1
2
4
1
1
1
3
1
2
4
1
1
X
(a)
(b)
Update | Node 1 | Node 2 | Node 3
Before break | (2,3) | (3,2) | (4, 1)
After break | (2,3) | (3,2) | (2,3)
1 | (2,3) | (3,4) | (2,3)
2 | (2,5) | (3,4) | (2,5)
3 | (2,5) | (3,6) | (2,5)
4 | (2,7) | (3,6) | (2,7)
5 | (2,7) | (3,8) | (2,7)
… | … | … | …
Nodes believe best path is through each other
(Destination is node 4)

## Slide 44: Problem: Bad News Travels Slowly
Remedies
Split Horizon
  Do not report route to a destination to the neighbor from which route was learned
Poisoned Reverse
  Report route to a destination to the neighbor from which route was learned, but with infinite distance
  Breaks erroneous direct loops immediately
  Does not work on some indirect loops

## Slide 45: Split Horizon with Poison Reverse
3
1
2
4
1
1
1
3
1
2
4
1
1
X
(a)
(b)
Nodes believe best path is through each other
Update | Node 1 | Node 2 | Node 3 | 
Before break | (2, 3) | (3, 2) | (4, 1) | 
After break | (2, 3) | (3, 2) | (-1, ) | Node 2 advertizes its route to 4 to node 3 as having distance infinity; node 3 finds there is no route to 4
1 | (2, 3) | (-1, ) | (-1, ) | Node 1 advertizes its route to 4 to node 2 as having distance infinity; node 2 finds there is no route to 4
2 | (-1, ) | (-1, ) | (-1, ) | Node 1 finds there is no route to 4

## Slide 46: Link-State Algorithm
Basic idea: two step procedure
  Each source node gets a map of all nodes and link metrics (link state) of the entire network
  Find the shortest path on the map from the source node to all destination nodes
Broadcast of link-state information
  Every node i in the network broadcasts to every other node in the network:
    ID’s of its neighbors: Ni=set of neighbors of i
    Distances to its neighbors: {Cij | j Ni}
  Flooding is a popular method of broadcasting packets

## Slide 47: Dijkstra Algorithm: Finding shortest paths in order
s
w
w"
w'
Closest node to s is 1 hop away
w"
x
x'
2nd closest node to s is 1 hop
away from s or w”
x
z
z'
3rd closest node to s is 1 hop
away from s, w”, or x
w'
Find shortest paths from source s to all other destinations

## Slide 48: Dijkstra’s algorithm
N: set of nodes for which shortest path already found
Initialization: (Start with source node s)
  N = {s}, Ds = 0, “s is distance zero from itself”
  Dj=Csj for all j  s, distances of directly-connected neighbors
Step A: (Find next closest node i)
  Find i  N such that
  Di = min Dj for j  N
  Add i to N
  If N contains all the nodes, stop
Step B: (update minimum costs)
  For each node j  N
  Dj = min (Dj, Di+Cij)
  Go to Step A
Minimum distance from s to j through node i in N

## Slide 49: Execution of Dijkstra’s algorithm
Iteration | N | D2 | D3 | D4 | D5 | D6
Initial | {1} | 3 | 2 | 5 |  | 
1 | {1,3} | 3 | 2 | 4 |  | 3
2 | {1,2,3} | 3 | 2 | 4 | 7 | 3
3 | {1,2,3,6} | 3 | 2 | 4 | 5 | 3
4 | {1,2,3,4,6} | 3 | 2 | 4 | 5 | 3
5 | {1,2,3,4,5,6} | 3 | 2 | 4 | 5 | 3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3










## Slide 50: Shortest Paths in Dijkstra’s Algorithm
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3

## Slide 51: Routing table at node 1
Destination | Next node | Cost
2 | 2 | 3
3 | 3 | 2
4 | 3 | 4
5 | 3 | 5
6 | 3 | 3

## Slide 52: Reaction to Failure
If a link fails,
  Router sets link distance to infinity & floods the network with an update packet
  All routers immediately update their link database & recalculate their shortest paths
  Recovery very quick
But watch out for old update messages
  Add time stamp or sequence # to each update message
  Check whether each received update message is new
  If new, add it to database and broadcast
  If older, send update message on arriving link

## Slide 53: Why is Link State Better?
Fast, loopless convergence
Support for precise metrics, and multiple metrics if necessary (throughput, delay, cost, reliability)
Support for multiple paths to a destination
  algorithm can be modified to find best two paths