## Slide 1: ITEC 109
Lecture 25
Sound

## Slide 2: Review
Photography
  Arrays of data
  Simple transformations

## Slide 3: Objectives
See another real world usage of arrays
  Sound

## Slide 4: Sound
Pressure in the air
Sounds are made up of rises and falls in pressure
  Compressions / rarefactions
Waves of sound data
  Frequency
  Amplitude
  Shape

## Slide 5: Waves
Simple wave
  Sine wave
Cycle
  One compression and rarefaction
Amplitude
  Distance from 0 point to greatest pressure
  Volume
  Formula for converting to decibels (db)
Compression
Rarefaction

## Slide 6: Waves
Pitch
  How often the cycle occurs
  Longer= lower
  Shorter= higher
Chipmunk effect
Real sound
  Several waves combined
  Sine waves don’t work

## Slide 7: Computers
Analog (real world) / Digital (0s and 1s)
  Pick a ceiling / floor for amplitudes
  How many cycles a second are there?
Record X times a second (sampling)
  CD quality = 44.1khz recording means 44,100 samples per second
  44,100 ints per second (10 megs a minute)
  CDs hold 650 MB or ~70 minutes of audio
hz = cycles per second

## Slide 8: Code
Python has lots of APIs for sounds
  JES makes life easy
sampleRate=22050; #Use for all your code
duration=1; # How long to play the sound (seconds)
numSamples = sampleRate*duration;
mySound = makeEmptySound(duration*sampleRate);
setSampleValueAt(mySound, 0, 440);
#To play the sound
play(mySound);
#To play and make sure it is unique
blockingPlay(mySound);
Note: This doesn’t actually make noise

## Slide 9: Problem
People are used to
Computers deal with

## Slide 10: Transformation
Each note is mapped to a specific frequency
Multiply by the 12th root of 2 to goto the next note
  261.626 * 2^(1/12) = 277.183 = C#
261.626 hz

## Slide 11: Problem
Just knowing the frequency isn’t enough
  Compression / rarefaction
Need to generate a wave
  Sound different

## Slide 12: Array tie in
0
1
2
3
4
5
6
7
10
10
10
10
5
5
5
5
Array holds the sampled values for the wave
This array is small compared to a regular CD.
For example, a crumb compared to the 16ft party sub that is an audio CD

## Slide 13: Square
Need both rarefaction and compression
How many array values for the top / bottom
Cycles in a sample (frequency)
Half a cycle on top
Half on bottom
Compression
Rarefaction

## Slide 14: Code
SamplingRate = 22050;
amp = 4000;
example = makeEmptySound(SamplingRate*1);
interval = 1.0/440;
samplesPerCycle = interval*SamplingRate;
halfCycle = samplesPerCycle/2;
value=440;
num=1;
for I in range (0, example.getLength()):
if (num > halfCycle):
num=0;
value=value*-1;
num=num+1;
raw = value * amp;
setSampleValueAt(example,i, raw);
play(example)
Play A4 for 1 second

## Slide 15: Triangle
Shape analysis
Start at amplitude, add increment until half cycle
Decrement for other half
Starting value
Slowly incrementing
Slowly decrementing

## Slide 16: Code
SamplingRate = 22050;
amp = 4000;
example = makeEmptySound(SamplingRate*1);
interval = 1.0/440; #What could this be?
samplesPerCycle = interval*SamplingRate;
halfCycle = samplesPerCycle/2;
value= 440/2.0;
increment = amp / samplesPerCycle;
num=1;
for i in range(0, example.getLength()):
if (num > halfCycle):
num=0;
increment=increment*-1;
num=num+1;
value=value+increment;
setSampleValueAt(example,i, value*amp);
play(example)

## Slide 17: Reality
What can you do with these simplistic music creation tools?
Academic curiosity or actually useful?

## Slide 18: Do the wave
Sine wave
  Math.sin(value); + for loop
Figure out duration (1 second)
Determine interval (space between samples)
  1/frequency
Figure out how many samples per cycle
  Interval * Sampling Rate
Feed sin a value for each sample

## Slide 19: Code
SamplingRate = 22050;
amp = 4000; //For volume
example = makeSound(SamplingRate*1);
interval = 1.0/440;
samplesPerCycle = interval*SamplingRate;
maxCycle = 2*3.14159;
for i in range(0, example.getLength()):
raw = Math.sin( (i/samplesPerCycle) *maxCycle);
raw = raw * amp;
setSampleValueAt(example,i, raw);
Note: Values will always range from 0 to 2Pi
The base sine wave is then adjusted for volume (multiplied by the amplitude)
Creates the note A4 for 1 second

## Slide 20: Demo
Process
  Note->Frequency->Sample
Program
  Creates X sample notes
  Plays based on what is typed in
  Simulator loop

## Slide 21: Auto-tune
What is it?
Example
How?
  Examine frequency
  Increase or decrement to right frequency
Makes horrible singers sound like pop singers…

## Slide 22: Summary
Music on computers
  Arrays are crucial
Note->frequency
Shape of wave
  Square
  Triangle
  Sine